## Slide 1
September 24, 2019
www.eia.gov/ieo
#IEO2019
International Energy Outlook 2019 with projections to 2050

## Slide 2
International Energy Outlook 2019 with projections to 2050 September 2019
U.S. Energy Information Administration
Office of Energy Analysis
U.S. Department of Energy
Washington, DC 20585
This publication is on the Web at:
https://www.eia.gov/ieo
  This report was prepared by the U.S. Energy Information Administration (EIA), the statistical and analytical agency within the U.S. Department of Energy. By law, EIA's data, analyses, and forecasts are independent of approval by any other officer or employee of the United States Government. The views in this report therefore should not be construed as representing those of the Department of Energy or other federal agencies.

## Slide 3
International Energy Outlook 2019 is dedicated to the memory of Linda Doman.
Linda led or contributed to the development of the International Energy Outlook for more than three decades.

## Slide 4: Table of contents Page
Preamble 5 Consumption 16 Industrial 32 Buildings 48 Transportation 64 Electricity 84 Coal 104 Petroleum and other liquids 114 Natural gas 130 Energy-related carbon dioxide 146 References 160

## Slide 5: Preamble

## Slide 7: The International Energy Outlook 2019 provides long-term world energy projections
The U.S. Energy Information Administration’s (EIA) International Energy Outlook (IEO) presents an analysis of long-term world energy markets in sixteen regions through 2050.
Reference case projections in each edition of the IEO are not predictions of what is most likely to happen, but rather they are modeled projections under various alternative assumptions.
The IEO projections are published under the Department of Energy Organization Act of 1977, which requires that EIA analyze “international aspects, economic and otherwise, of the evolving energy situation” and “long-term relationships between energy supply and consumption in the United States and world communities.”
EIA develops the IEO using the World Energy Projection System Plus (WEPS+), an integrated economic model that captures long-term relationships among energy supply, demand, and prices across regional markets under various assumptions.
Energy market projections are uncertain because the events that shape future developments in technology, demographic changes, economic trends, and resource availability that drive energy use are fluid.

## Slide 8: The Reference case provides a baseline to measure the impact of alternative assumptions
The Reference case reflects current trends and relationships among supply, demand, and prices in the future. It is a reasonable baseline case to compare with cases that include alternative assumptions about economic drivers, policy changes, or other determinants of the energy system to estimate the potential impact of these assumptions.
The Reference case includes some anticipated changes over time:
  Expected regional economic and demographic trends, based on the views of leading forecasters
  Planned changes to infrastructure, both new construction and announced retirements
  Assumed incremental cost and performance improvements in known technologies based on historical trends
This case does not include some of the potential future changes:
  Changes to national boundaries and international agreements
  Major disruptive geopolitical or economic events
  Future technological breakthroughs
  Changes to current policies as reflected in laws, regulations, and stated targets that indicate future activity

## Slide 9: Side cases address two significant sources of uncertainty
To see the impact of economic growth on energy consumption, EIA adjusted the assumptions about regional factors of growth in the High and Low Economic Growth cases. The resulting compound annual growth rates of global gross domestic product (GDP) during the projection period (2018–2050) vary from the Reference case as follows:
  3.7% per year, High Economic Growth case
  3.0% per year, Reference case
  2.4% per year, Low Economic Growth case
The High and Low Oil Price cases address the uncertainty associated with world energy prices. EIA altered the assumptions about both oil supply and demand to achieve higher and lower oil prices, as seen in the 2050 price of North Sea Brent crude oil in 2018 dollars:
  $185/barrel, High Oil Price case
  $100/barrel, Reference case
  $45/barrel, Low Oil Price case

## Slide 11: Future oil prices are a key source of uncertainty in the projections—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
High Oil Price | 91.0166 | 124.6585 | 122.7559 | 117.4584 | 105.1128 | 55.0197 | 45.4184 | 55.2307 | 71.2108 | 93.3033 | 109.1112 | 120.7303 | 125.9787 | 130.4358 | 135.7103 | 139.3984 | 142.7345 | 145.7865 | 148.6034 | 151.2226 | 153.6728 | 155.9767 | 158.1526 | 160.2155 | 162.1778 | 164.0499 | 165.8406 | 167.5576 | 169.2072 | 170.7952 | 172.3265 | 173.8055 | 175.2361 | 176.6216 | 177.9652 | 179.2695 | 180.5372 | 181.7704 | 182.9712 | 184.1413 | 185.2827
Low Oil Price | 91.0166 | 124.6585 | 122.7559 | 117.4584 | 105.1128 | 55.0197 | 45.4184 | 55.2307 | 71.2108 | 39.5464 | 33.1361 | 33.5324 | 35.523 | 36.7418 | 37.6319 | 38.337 | 38.923 | 39.4254 | 39.8659 | 40.2585 | 40.6129 | 40.9363 | 41.2337 | 41.5092 | 41.7659 | 42.0064 | 42.2325 | 42.4461 | 42.6484 | 42.8407 | 43.0239 | 43.1989 | 43.3664 | 43.5271 | 43.6815 | 43.8301 | 43.9734 | 44.1117 | 44.2454 | 44.3747 | 44.5001
Reference | 91.0166 | 124.6585 | 122.7559 | 117.4584 | 105.1128 | 55.0197 | 45.4184 | 55.2307 | 71.2108 | 59.7199 | 60.669 | 65.4051 | 67.4405 | 69.4758 | 70.5993 | 71.7228 | 72.8463 | 73.9698 | 75.0933 | 76.2168 | 77.3403 | 78.4638 | 79.5874 | 80.7109 | 81.8344 | 82.9579 | 84.0814 | 85.2049 | 86.3284 | 87.4519 | 88.5754 | 89.6989 | 90.8224 | 91.9459 | 93.0694 | 94.1929 | 95.3164 | 96.4399 | 97.5634 | 98.6869 | 99.8104
World oil prices in three cases
real 2018 dollars per barrel
World energy consumption in three cases
quadrillion British thermal units
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series0 | 241.9063 | 239.8771 | 237.3892 | 239.9006 | 238.7762 | 239.1221 | 240.3993 | 246.5396 | 249.4171 | 249.7916 | 250.3128 | 251.0728 | 251.5003 | 251.8939 | 252.4176 | 252.8175 | 253.3604 | 254.2294 | 255.2374 | 256.369 | 257.2477 | 257.9954 | 258.4918 | 259.2723 | 260.1996 | 261.3745 | 262.6472 | 263.8339 | 265.0725 | 266.5788 | 268.1732 | 269.7337 | 271.3875 | 273.0057 | 274.6428 | 276.486 | 278.4691 | 280.5958 | 282.6116 | 284.6088 | 286.816
series1 | 241.9063 | 239.8771 | 237.3892 | 239.9001 | 238.7759 | 239.1176 | 240.3988 | 246.7673 | 249.7046 | 250.2625 | 250.9261 | 252.2439 | 253.8067 | 254.8062 | 255.693 | 255.9359 | 256.7002 | 257.5928 | 258.7582 | 260.4028 | 262.0638 | 263.8724 | 265.7952 | 267.9903 | 269.9737 | 272.1471 | 274.1879 | 276.2275 | 278.2536 | 280.6515 | 282.9803 | 285.7603 | 288.4656 | 291.5175 | 294.5588 | 297.5672 | 301.9347 | 306.9541 | 312.0448 | 317.2798 | 322.6963
series2 | 241.9063 | 239.8771 | 237.3892 | 239.9001 | 238.7759 | 239.1179 | 240.4002 | 246.7832 | 249.4956 | 249.5659 | 249.6017 | 250.0012 | 250.1989 | 250.4131 | 250.5873 | 250.5086 | 250.7328 | 251.1895 | 251.8126 | 252.3168 | 252.858 | 253.2938 | 253.6781 | 254.1936 | 254.7484 | 255.5976 | 256.5556 | 257.3825 | 258.5986 | 259.5662 | 260.5789 | 261.7242 | 263.1062 | 264.5645 | 266.0165 | 267.6435 | 269.2883 | 270.9612 | 272.6757 | 274.3789 | 276.0443
series3 | 295.5912 | 313.1417 | 328.6067 | 336.7234 | 343.9578 | 347.132 | 350.5848 | 362.9966 | 370.571 | 377.1849 | 384.7196 | 390.3047 | 395.3838 | 400.6029 | 406.1304 | 412.0994 | 418.9836 | 426.1523 | 433.2966 | 440.6043 | 447.9256 | 455.4815 | 462.684 | 470.2897 | 477.771 | 485.7819 | 493.6997 | 501.9892 | 510.4209 | 518.5304 | 526.7052 | 536.8521 | 546.804 | 556.894 | 567.0924 | 577.2179 | 586.5982 | 595.7719 | 605.4031 | 614.4289 | 623.8824
series4 | 295.5912 | 313.1417 | 328.6067 | 336.7234 | 343.9578 | 347.132 | 350.5848 | 362.9307 | 370.756 | 377.2212 | 384.4322 | 391.4205 | 399.3514 | 407.2982 | 415.4525 | 423.4133 | 432.4928 | 442.1159 | 451.2805 | 461.1616 | 470.9446 | 480.9433 | 490.3907 | 500.345 | 509.4404 | 519.8412 | 532.2334 | 544.5777 | 557.2906 | 569.6159 | 582.9669 | 597.1325 | 611.3545 | 625.4514 | 640.0987 | 654.693 | 669.1358 | 684.4754 | 700.451 | 716.3675 | 732.7099
series5 | 295.5912 | 313.1417 | 328.6067 | 336.7234 | 343.9578 | 347.132 | 350.5848 | 362.8274 | 370.2597 | 376.2116 | 383.0422 | 387.3391 | 391.2318 | 395.3452 | 399.056 | 403.3137 | 408.7334 | 414.4423 | 420.1378 | 425.7012 | 431.3627 | 437.5074 | 443.5854 | 450.0482 | 456.187 | 462.4736 | 469.4872 | 476.2456 | 483.1958 | 490.1405 | 497.3176 | 504.5982 | 512.1174 | 519.4139 | 527.0432 | 534.4605 | 542.6231 | 551.1545 | 559.7932 | 568.3975 | 577.1428
history projections
Low Oil Price case
Reference case
High Oil Price case

## Slide 12: —with greater energy consumption differences in non-OECD regions
In addition to the Reference case, EIA includes a Low Oil Price case and a High Oil Price case that use different assumptions about future oil prices, based on different views of supply and demand for liquid fuels.
In the Low Oil Price case, lower economic activity, especially in countries that are not a part of the Organization of Economic Cooperation and Development (OECD), discourages energy consumption. Simultaneously but independently, greater resource availability and lower extraction costs encourage additional petroleum supplies, despite the reduced economic growth. The resulting lower oil prices encourage liquid fuels consumption and discourage energy conservation and fuel switching.
In the High Oil Price case, energy demand increases because non-OECD economies grow more quickly than in the Reference case, despite tighter petroleum supply conditions. Although energy consumption rises, higher oil prices limit the growth in liquid fuels, and consumers conserve or switch to alternative fuels whenever possible.

## Slide 13: Oil prices vary widely across the High Oil Price, Reference, and Low Oil Price cases—
Chart: Low Oil Price case
| 2050
NGPL | 19.7824
non-OPEC | 57.2312
OPEC | 53.4091
Chart: High Oil Price case
| 2050
NGPL | 21.3537
non-OPEC | 62.0475
OPEC | 46.9441
OPEC crude and lease condensate
non-OPEC crude and lease condensate
NGPL and other liquid fuels
Chart: Reference case
| 2018 | 2050
NGPL | 16.8942 | 20.3142
non-OPEC | 47.9982 | 59.0839
OPEC | 34.8553 | 47.7016
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series0 | 46.6107 | 46.0594 | 45.6422 | 45.7375 | 45.5147 | 46.2194 | 46.6107 | 47.0673 | 47.3547 | 47.5161 | 47.2421 | 47.0349 | 46.7939 | 46.4704 | 46.131 | 45.817 | 45.4719 | 45.2293 | 45.0021 | 44.7871 | 44.5702 | 44.3917 | 44.2046 | 44.0134 | 43.8535 | 43.7577 | 43.7029 | 43.6785 | 43.7021 | 43.7112 | 43.7629 | 43.8721 | 43.9757 | 44.085 | 44.2198 | 44.3661 | 44.5403 | 44.7384 | 44.9852 | 45.1272 | 45.3193
series1 | 46.6107 | 46.0594 | 45.6422 | 45.7375 | 45.5147 | 46.2194 | 46.6107 | 47.0673 | 47.3547 | 47.4588 | 47.0791 | 46.7008 | 46.5294 | 46.181 | 45.7667 | 45.246 | 44.7564 | 44.3249 | 43.9054 | 43.6138 | 43.3074 | 43.0922 | 42.8922 | 42.7176 | 42.4709 | 42.3468 | 42.2728 | 42.1876 | 42.1503 | 42.139 | 42.206 | 42.3029 | 42.3775 | 42.4969 | 42.6915 | 42.9389 | 43.2265 | 43.6478 | 44.1268 | 44.6446 | 45.1354
series2 | 46.6107 | 46.0594 | 45.6422 | 45.7375 | 45.5147 | 46.2194 | 46.6107 | 47.0673 | 47.3547 | 47.5274 | 47.42 | 47.2462 | 47.0344 | 46.7957 | 46.4946 | 46.2238 | 46.0054 | 45.808 | 45.6395 | 45.4939 | 45.3092 | 45.1833 | 45.1111 | 45.0161 | 44.9045 | 44.8831 | 44.9429 | 44.9681 | 45.0991 | 45.1963 | 45.3429 | 45.4933 | 45.7097 | 45.8901 | 46.1499 | 46.4068 | 46.6637 | 46.9475 | 47.2439 | 47.4908 | 47.7554
series3 | 41.902 | 43.2246 | 44.9796 | 46.2847 | 48.1773 | 49.4163 | 49.998 | 51.3552 | 52.573 | 53.7001 | 54.934 | 55.606 | 56.2341 | 56.8073 | 57.4449 | 58.1621 | 58.7277 | 59.3788 | 59.9973 | 60.6142 | 61.2404 | 61.8876 | 62.4896 | 63.0949 | 63.7305 | 64.4544 | 65.1694 | 65.8913 | 66.6509 | 67.3386 | 68.0401 | 68.8635 | 69.6594 | 70.4625 | 71.2537 | 72.0534 | 72.8502 | 73.6633 | 74.5034 | 75.2666 | 76.1347
series4 | 41.902 | 43.2246 | 44.9796 | 46.2847 | 48.1773 | 49.4163 | 49.998 | 51.3552 | 52.573 | 53.7001 | 54.934 | 55.6092 | 56.488 | 57.2747 | 58.0649 | 58.7362 | 59.3892 | 60.0355 | 60.5659 | 61.1659 | 61.7004 | 62.2821 | 62.8182 | 63.3894 | 63.8328 | 64.5298 | 65.2427 | 65.9012 | 66.6454 | 67.447 | 68.3768 | 69.3829 | 70.2807 | 71.3439 | 72.5165 | 73.7276 | 74.9403 | 76.2989 | 77.7222 | 79.2378 | 80.687
series5 | 41.902 | 43.2246 | 44.9796 | 46.2847 | 48.1773 | 49.4163 | 49.998 | 51.3552 | 52.573 | 53.7001 | 54.934 | 55.578 | 56.0974 | 56.7036 | 57.1357 | 57.6988 | 58.2359 | 58.7832 | 59.3103 | 59.794 | 60.2802 | 60.7463 | 61.2266 | 61.7519 | 62.212 | 62.7348 | 63.4556 | 64.0605 | 64.723 | 65.3723 | 66.0798 | 66.7819 | 67.6011 | 68.4057 | 69.2475 | 70.1626 | 70.9711 | 71.8837 | 72.7969 | 73.7589 | 74.8163
World petroleum and other liquid fuels production
million barrels per day

## Slide 14: —affecting where crude oil and condensate is produced
In the Reference case, world production of crude oil and lease condensate increases from about 80 million barrels per day (b/d) in 2018 to 107 million b/d in 2050. Total liquids production increases from 100 million b/d in 2018 to 127 million b/d in 2050.
Liquid fuels consumption increases 45% in non-OECD countries and falls 4% in OECD countries.
In the High Oil Price case, world liquid fuels consumption in 2050 is 4 million b/d higher than in the Reference case. Primarily, emerging, non-OECD nations drive faster economic growth, which contributes to higher energy demand. In the High Oil Price case, proportionally higher amounts of crude oil are supplied by countries that are not part of the Organization of the Petroleum Exporting Countries (OPEC).
In the Low Oil Price case, world liquids consumption in 2050 is 1 million b/d higher than in the Reference case. Slower non-OECD economic growth assumptions lead to lower energy demand, but the lower prices mean that consumers use more liquid fuels. Low-cost producers located in OPEC countries supply more crude oil and condensate to the global marketplace.

## Slide 15: Energy consumption varies considerably across the High and Low Economic Growth cases—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series0 | 43.9103 | 44.8105 | 45.4163 | 46.1021 | 47.1214 | 48.31 | 49.1713 | 50.4477 | 51.6038 | 52.5899 | 53.5348 | 54.451 | 55.3702 | 56.2261 | 57.1205 | 58.0691 | 59.0361 | 60.0298 | 61.0454 | 62.0641 | 63.0899 | 64.0421 | 64.9349 | 65.8729 | 66.8367 | 67.8056 | 68.7673 | 69.7447 | 70.7169 | 71.7191 | 72.7441 | 73.7943 | 74.8917 | 75.9803 | 77.0754 | 78.2039 | 79.3156 | 80.4449 | 81.5439 | 82.6682 | 83.8476
series1 | 43.9103 | 44.8105 | 45.4163 | 46.1021 | 47.1214 | 48.31 | 49.1713 | 50.4477 | 51.6021 | 52.7815 | 54.1421 | 55.5244 | 56.9083 | 58.185 | 59.3858 | 60.6188 | 61.9147 | 63.2839 | 64.6999 | 66.0641 | 67.4715 | 68.7734 | 70.084 | 71.4353 | 72.7729 | 74.1255 | 75.5176 | 76.9597 | 78.4505 | 79.9827 | 81.5534 | 83.1804 | 84.8749 | 86.6371 | 88.4107 | 90.2541 | 92.2307 | 94.3764 | 96.651 | 98.9743 | 101.3075
series2 | 43.9103 | 44.8105 | 45.4163 | 46.1021 | 47.1214 | 48.31 | 49.1713 | 50.4477 | 51.6021 | 52.4591 | 53.0535 | 53.592 | 54.1692 | 54.712 | 55.2579 | 55.8262 | 56.4791 | 57.1934 | 57.9443 | 58.6522 | 59.3724 | 60.0697 | 60.7643 | 61.4675 | 62.147 | 62.7928 | 63.438 | 64.0963 | 64.7954 | 65.5419 | 66.2976 | 67.0516 | 67.8276 | 68.5892 | 69.3029 | 70.0182 | 70.7156 | 71.444 | 72.1736 | 72.9054 | 73.6169
series3 | 45.32 | 48.1953 | 50.5471 | 53.1687 | 55.6164 | 57.8545 | 60.4491 | 63.1737 | 66.1569 | 69.0423 | 72.3059 | 75.8016 | 79.2154 | 82.7526 | 86.3548 | 90.1 | 93.862 | 97.7525 | 101.7377 | 105.8218 | 110.0483 | 114.353 | 118.6667 | 123.1385 | 127.7314 | 132.442 | 137.2565 | 142.1075 | 147.06 | 152.1134 | 157.3722 | 162.7048 | 168.2689 | 173.8899 | 179.7104 | 185.5914 | 191.491 | 197.4803 | 203.5251 | 209.6058 | 215.868
series4 | 45.32 | 48.1953 | 50.5471 | 53.1687 | 55.6164 | 57.8545 | 60.4491 | 63.1737 | 66.1569 | 69.311 | 73.2151 | 77.5153 | 81.7995 | 86.2035 | 90.6642 | 95.3283 | 100.0994 | 105.1272 | 110.3044 | 115.7831 | 121.4129 | 127.2457 | 133.1711 | 139.1878 | 145.4005 | 151.8346 | 158.5751 | 165.4695 | 172.5615 | 179.8395 | 187.3451 | 195.2201 | 203.3132 | 211.7754 | 220.443 | 229.4269 | 238.7091 | 248.315 | 258.0893 | 268.0137 | 278.0691
series5 | 45.32 | 48.1953 | 50.5471 | 53.1687 | 55.6164 | 57.8545 | 60.4491 | 63.1737 | 66.1569 | 68.8732 | 71.7604 | 74.699 | 77.5421 | 80.4517 | 83.3983 | 86.4871 | 89.5681 | 92.7287 | 95.9553 | 99.2895 | 102.6967 | 106.246 | 109.7493 | 113.3189 | 116.945 | 120.6414 | 124.4499 | 128.2391 | 132.1439 | 136.0684 | 140.1806 | 144.293 | 148.5633 | 152.916 | 157.2937 | 161.7044 | 166.1253 | 170.6428 | 175.0888 | 178.442 | 181.6491
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series0 | 241.9063 | 239.8771 | 237.3892 | 239.9006 | 238.7762 | 239.1221 | 240.3993 | 246.5396 | 249.4171 | 249.7916 | 250.3128 | 251.0728 | 251.5003 | 251.8939 | 252.4176 | 252.8175 | 253.3604 | 254.2294 | 255.2374 | 256.369 | 257.2477 | 257.9954 | 258.4918 | 259.2723 | 260.1996 | 261.3745 | 262.6472 | 263.8339 | 265.0725 | 266.5788 | 268.1732 | 269.7337 | 271.3875 | 273.0057 | 274.6428 | 276.486 | 278.4691 | 280.5958 | 282.6116 | 284.6088 | 286.816
series1 | 241.9063 | 239.8771 | 237.3892 | 239.9001 | 238.7759 | 239.1209 | 240.3993 | 246.7941 | 249.6875 | 250.2052 | 251.3415 | 253.0338 | 254.6064 | 256.1267 | 257.6552 | 258.8975 | 260.4729 | 262.3665 | 264.2714 | 266.3288 | 268.2693 | 270.1717 | 272.0543 | 274.1498 | 276.318 | 278.8731 | 281.4478 | 283.9687 | 286.6368 | 289.3488 | 292.2134 | 295.4923 | 298.7689 | 302.3052 | 305.9786 | 309.5056 | 314.4872 | 319.671 | 324.933 | 330.1095 | 335.7634
series2 | 241.9063 | 239.8771 | 237.3892 | 239.9001 | 238.7759 | 239.1174 | 240.3993 | 246.8243 | 249.5783 | 249.7995 | 249.33 | 249.0758 | 248.9007 | 248.6854 | 248.4777 | 247.9571 | 247.6535 | 247.5808 | 247.7325 | 247.9598 | 247.9043 | 247.9204 | 247.9367 | 248.2361 | 248.5363 | 248.8773 | 249.2849 | 249.5585 | 250.2417 | 250.9337 | 251.4976 | 252.4717 | 253.4074 | 254.4574 | 255.5436 | 256.5734 | 257.5218 | 258.5325 | 259.8896 | 260.9358 | 262.064
series3 | 295.5912 | 313.1417 | 328.6067 | 336.7234 | 343.9578 | 347.132 | 350.5848 | 362.9966 | 370.571 | 377.1849 | 384.7196 | 390.3047 | 395.3838 | 400.6029 | 406.1304 | 412.0994 | 418.9836 | 426.1523 | 433.2966 | 440.6043 | 447.9256 | 455.4815 | 462.684 | 470.2897 | 477.771 | 485.7819 | 493.6997 | 501.9892 | 510.4209 | 518.5304 | 526.7052 | 536.8521 | 546.804 | 556.894 | 567.0924 | 577.2179 | 586.5982 | 595.7719 | 605.4031 | 614.4289 | 623.8824
series4 | 295.5912 | 313.1417 | 328.6067 | 336.7234 | 343.9578 | 347.132 | 350.5848 | 363.0112 | 370.9023 | 377.7898 | 386.514 | 394.7938 | 403.4328 | 412.1266 | 421.0849 | 429.9442 | 439.9896 | 450.1522 | 460.1659 | 470.8013 | 481.3212 | 492.0222 | 502.4602 | 513.3811 | 523.8759 | 535.0765 | 547.4937 | 559.9308 | 572.6675 | 585.1079 | 598.1237 | 612.8724 | 627.6067 | 642.9182 | 658.0789 | 673.1347 | 688.5229 | 703.7728 | 719.6263 | 734.8967 | 751.1424
series5 | 295.5912 | 313.1417 | 328.6067 | 336.7234 | 343.9578 | 347.132 | 350.5848 | 362.8696 | 370.3095 | 376.1682 | 382.9495 | 386.2957 | 389.8917 | 393.5523 | 397.3472 | 401.1464 | 406.538 | 412.0248 | 417.6243 | 423.204 | 428.8105 | 434.2925 | 439.5604 | 445.037 | 450.2394 | 455.9993 | 462.6406 | 469.4069 | 476.2636 | 482.8942 | 489.9314 | 496.953 | 504.0641 | 511.3131 | 518.4938 | 525.7469 | 533.4943 | 541.0919 | 549.2574 | 556.674 | 563.6442

## Slide 16: —with greater variation across non-OECD regions
From 2018 to 2050, world real GDP increases by 3.0% per year in the Reference case, 3.7% in the High Economic Growth case, and 2.4% per year in the Low Economic growth case.
In OECD countries, over the same time period, real GDP increases by 1.5% per year in the Reference case, 2.1% per year in the High Economic Growth case, and 1.1% per year in the Low Economic growth case.
In non-OECD countries, during the same time period, growth is 3.8% per year in the Reference case, 4.6% in the High Economic Growth case, and 3.2% in the Low Economic Growth case.
In the Reference case, world energy consumption totals 911 quadrillion British thermal units (Btu) in 2050—287 quadrillion Btu in the OECD countries and 624 quadrillion Btu in the non-OECD countries. In the High Economic Growth case, world energy use in 2050 is about 1,090 quadrillion Btu. In the Low Economic Growth case, world energy use in 2050 is about 830 quadrillion Btu.

## Slide 17: Consumption

## Slide 19: Economic growth is highest in non-OECD countries in the Reference case –
World gross domestic product (GDP)
trillion 2010 dollars, purchasing power parity (PPP)
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
OECD | 43.9103 | 44.8105 | 45.4163 | 46.1021 | 47.1214 | 48.31 | 49.1713 | 50.4477 | 51.6038 | 52.5899 | 53.5348 | 54.451 | 55.3702 | 56.2261 | 57.1205 | 58.0691 | 59.0361 | 60.0298 | 61.0454 | 62.0641 | 63.0899 | 64.0421 | 64.9349 | 65.8729 | 66.8367 | 67.8056 | 68.7673 | 69.7447 | 70.7169 | 71.7191 | 72.7441 | 73.7943 | 74.8917 | 75.9803 | 77.0754 | 78.2039 | 79.3156 | 80.4449 | 81.5439 | 82.6682 | 83.8476
Non-OECD | 45.32 | 48.1953 | 50.5471 | 53.1687 | 55.6164 | 57.8545 | 60.4491 | 63.1737 | 66.1569 | 69.0423 | 72.3059 | 75.8016 | 79.2154 | 82.7526 | 86.3548 | 90.1 | 93.862 | 97.7525 | 101.7377 | 105.8218 | 110.0483 | 114.353 | 118.6667 | 123.1385 | 127.7314 | 132.442 | 137.2565 | 142.1075 | 147.06 | 152.1134 | 157.3722 | 162.7048 | 168.2689 | 173.8899 | 179.7104 | 185.5914 | 191.491 | 197.4803 | 203.5251 | 209.6058 | 215.868
history projections
Chart: 
| 2010 | 2030 | 2050
OECD | 35.3436 | 45.8869 | 58.3474
Non-OECD | 7.8931 | 15.3881 | 26.2804
World per capita GDP
thousand 2010 dollars PPP

## Slide 20: —where per capita GDP grows rapidly as a result of economic development
In the Reference case, combined gross domestic product (GDP) in the countries that are not part of the Organization of Economic Cooperation and Development (OECD) grows by 3.8% per year on average between 2018 and 2050, compared with 1.5% per year in the OECD countries.
Since 1990, non-OECD countries have led world economic growth, accompanied by strong growth in energy demand in those countries.
GDP per person, an indicator of a country's standard of living, increases similarly in OECD and non-OECD regions in absolute terms. However, the proportional increase in non-OECD countries is much larger, more than double (a 150% increase) between 2018 and 2050, as opposed to less than a 50% increase in OECD countries.

## Slide 21: Economic growth varies widely across non-OECD regions in the Reference case—
Chart: OECD
| total OECD |  | Japan | OECD Europe | Canada | South Korea | United States | Mexico and Chile | Australia and New Zealand
growth rate | 1.5285 | 0 | 0.24112 | 1.3017 | 1.3271 | 1.7427 | 1.8898 | 2.106 | 2.3948
Chart: non-OECD
| total non-OECD |  | Russia | Brazil | other Europe and Eurasia | other Americas | Middle East | China | other Asia | Africa | India
growth rate | 3.7649 | 0 | 1.1454 | 1.4728 | 2.2953 | 2.4433 | 2.565 | 3.8674 | 3.8784 | 3.9298 | 5.4038
Average annual percent change in GDP, 2018-2050
percent per year

## Slide 22: —with the highest rates occurring in non-OECD Asia and Africa
Both OECD and non-OECD regions are diverse, with wide spreads in economic growth.
In the non-OECD regions, India, China, other Asia, and Africa grow at an average rate of nearly 4% or higher. These regions were home to about two-thirds of the world’s population in 2018.
Japan (OECD) and Russia (non-OECD) are the slowest-growing economies, partly as a result of declining populations and aging workforces.
The projected GDP growth in China slows considerably compared with its growth from 2000 to 2010, when GDP increased by an average of about 10% per year.

## Slide 23: World energy consumption rises nearly 50% between 2018 and 2050 in the Reference case —
World energy consumption
quadrillion British thermal units
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
OECD | 241.9063 | 239.8771 | 237.3892 | 239.9006 | 238.7762 | 239.1221 | 240.3993 | 246.5396 | 249.4171 | 249.7916 | 250.3128 | 251.0728 | 251.5003 | 251.8939 | 252.4176 | 252.8175 | 253.3604 | 254.2294 | 255.2374 | 256.369 | 257.2477 | 257.9954 | 258.4918 | 259.2723 | 260.1996 | 261.3745 | 262.6472 | 263.8339 | 265.0725 | 266.5788 | 268.1732 | 269.7337 | 271.3875 | 273.0057 | 274.6428 | 276.486 | 278.4691 | 280.5958 | 282.6116 | 284.6088 | 286.816
Non-OECD | 295.5912 | 313.1417 | 328.6067 | 336.7234 | 343.9578 | 347.132 | 350.5848 | 362.9966 | 370.571 | 377.1849 | 384.7196 | 390.3047 | 395.3838 | 400.6029 | 406.1304 | 412.0994 | 418.9836 | 426.1523 | 433.2966 | 440.6043 | 447.9256 | 455.4815 | 462.684 | 470.2897 | 477.771 | 485.7819 | 493.6997 | 501.9892 | 510.4209 | 518.5304 | 526.7052 | 536.8521 | 546.804 | 556.894 | 567.0924 | 577.2179 | 586.5982 | 595.7719 | 605.4031 | 614.4289 | 623.8824

## Slide 24: —with almost all of the increase occurring in non-OECD countries
In the Reference case, most increases in energy consumption come from non-OECD countries, where strong economic growth, increased access to marketed energy, and rapid population growth lead to rising energy consumption.
In OECD countries, growth in energy consumption is slower as a result of relatively slower population and economic growth, improvements in energy efficiency, and less growth in energy-intensive industries.
Energy consumption in non-OECD countries increases nearly 70% between 2018 and 2050 in contrast to a 15% increase in OECD countries.

## Slide 25: In the Reference case, non-OECD Asia accounts for most of the increase in energy use—
Non-OECD energy consumption by region
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe and Eurasia | 49.6204 | 48.9379 | 49.6645 | 51.5489 | 54.3034
Americas | 28.8492 | 32.4655 | 36.2917 | 39.9969 | 44.0472
Africa | 19.8242 | 25.5409 | 31.4163 | 39.8833 | 51.4165
Middle East | 29.1961 | 38.6886 | 44.9535 | 50.7568 | 57.7649
Asia | 168.1012 | 239.0867 | 285.5996 | 344.5195 | 416.3503
history projections
Asia
Middle East
Africa
Americas
Europe and Eurasia

## Slide 26: —but substantial growth also occurs in other non-OECD regions
More than half of the projected increase in global energy consumption occurs in non-OECD Asian countries, a group that includes China and India. Energy demand in non-OECD Asia is larger than in any other region in 2018, and it is projected to almost double between 2018 and 2050, making it both the largest and fastest-growing region in the world for energy consumption.
China and India have been among the world’s fastest-growing economies during much of the past decade, and they remain primary contributors to future growth in world energy demand.
Non-OECD regions outside of Asia contribute to substantial increases in energy consumption. Fast-paced population growth and access to ample domestic resources are important determinants of energy demand in Africa and the Middle East, where energy use increases about 110% and 55%, respectively, between 2018 and 2050.
Non-OECD Europe and Eurasia has the smallest projected increase in energy consumption (11%). Much of the low growth is related to Russia, where the population declines. The low growth is also a result of significant gains in energy efficiency achieved by replacing older physical assets with more efficient ones.

## Slide 27: The industrial sector is the largest consumer of energy—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Industrial | 71.5616 | 72.2329 | 72.8759 | 73.2586 | 73.0365 | 73.1882 | 73.4008 | 74.3386 | 75.4226 | 75.2135 | 75.6938 | 76.4138 | 76.7069 | 77.0287 | 77.3407 | 77.6938 | 77.7757 | 78.1691 | 78.5709 | 78.9827 | 79.2832 | 79.6315 | 79.7913 | 80.08 | 80.3717 | 80.8148 | 81.2001 | 81.512 | 81.7657 | 82.2274 | 82.7613 | 83.1161 | 83.5829 | 83.8816 | 84.1727 | 84.6368 | 85.1577 | 85.6771 | 86.1117 | 86.542 | 87.0884
Transportation | 57.0743 | 56.5891 | 55.6602 | 55.9012 | 56.8212 | 57.6618 | 58.8719 | 59.6174 | 59.8305 | 60.0787 | 59.908 | 59.6888 | 59.4684 | 59.0917 | 58.6758 | 58.2419 | 57.8417 | 57.4246 | 57.0533 | 56.6822 | 56.2944 | 55.9547 | 55.6644 | 55.4115 | 55.2571 | 55.1571 | 55.1435 | 55.1641 | 55.2453 | 55.3498 | 55.5015 | 55.7566 | 56.0111 | 56.353 | 56.7084 | 57.0727 | 57.4284 | 57.8587 | 58.2727 | 58.6909 | 59.152
Commercial | 19.9434 | 19.6439 | 19.3128 | 20.044 | 19.9155 | 20.3114 | 20.2614 | 20.6087 | 20.979 | 21.1192 | 21.2151 | 21.3271 | 21.4486 | 21.567 | 21.6866 | 21.8076 | 21.9512 | 22.1033 | 22.2675 | 22.4425 | 22.6056 | 22.7461 | 22.8818 | 23.0172 | 23.1743 | 23.3352 | 23.4953 | 23.6568 | 23.8183 | 23.9967 | 24.1709 | 24.3572 | 24.5388 | 24.7361 | 24.9308 | 25.1359 | 25.3538 | 25.587 | 25.8225 | 26.0494 | 26.3118
Residential | 28.6483 | 27.2338 | 26.5643 | 27.7657 | 26.7405 | 26.4591 | 26.3229 | 26.5254 | 27.3745 | 27.3688 | 27.1447 | 27.0854 | 27.0573 | 27.0682 | 27.097 | 27.1103 | 27.172 | 27.2373 | 27.3096 | 27.4228 | 27.515 | 27.5818 | 27.6457 | 27.702 | 27.7934 | 27.8817 | 27.9695 | 28.0558 | 28.1351 | 28.2306 | 28.3245 | 28.4347 | 28.5215 | 28.624 | 28.7186 | 28.8159 | 28.9109 | 29.015 | 29.1236 | 29.2055 | 29.3363
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Industrial | 142.3201 | 150.3382 | 157.4106 | 158.8739 | 162.7163 | 163.177 | 163.5208 | 161.6371 | 163.4 | 163.4374 | 164.4297 | 165.779 | 166.338 | 167.0576 | 168.0323 | 169.5779 | 170.7891 | 172.4906 | 174.218 | 176.165 | 178.137 | 180.299 | 182.1362 | 184.3454 | 186.2834 | 188.7219 | 190.9644 | 193.4855 | 196.0452 | 198.322 | 200.69 | 203.6911 | 206.5265 | 209.3999 | 212.3834 | 215.2774 | 218.3429 | 221.0174 | 224.1557 | 226.7109 | 229.5688
Transportation | 45.378 | 47.7906 | 49.832 | 51.6843 | 53.6914 | 56.0137 | 58.5232 | 59.6698 | 61.0718 | 62.3682 | 63.8442 | 65.4093 | 67.025 | 68.6107 | 70.2274 | 71.7993 | 73.2914 | 74.7358 | 76.0714 | 77.3796 | 78.6545 | 79.8466 | 80.95 | 82.0919 | 83.3162 | 84.6759 | 85.992 | 87.4046 | 88.8251 | 90.3096 | 91.6786 | 93.256 | 94.7815 | 96.4276 | 98.096 | 99.7838 | 101.3666 | 103.0137 | 104.6729 | 106.3144 | 108.0468
Commercial | 8.8406 | 9.3013 | 9.7845 | 10.2203 | 10.3346 | 10.8026 | 11.1979 | 11.4066 | 11.6358 | 11.8332 | 12.0854 | 12.315 | 12.5727 | 12.8374 | 13.1216 | 13.4055 | 13.741 | 14.0696 | 14.4191 | 14.7723 | 15.1385 | 15.485 | 15.8231 | 16.1719 | 16.5247 | 16.8799 | 17.2377 | 17.582 | 17.9333 | 18.2797 | 18.6434 | 19.0147 | 19.3943 | 19.794 | 20.1854 | 20.5847 | 20.9411 | 21.3064 | 21.6751 | 22.0345 | 22.4025
Residential | 23.8797 | 25.2205 | 25.808 | 26.7311 | 27.6981 | 28.3848 | 29.6607 | 30.8987 | 31.5101 | 32.0603 | 32.6634 | 33.2021 | 33.8209 | 34.493 | 35.2293 | 35.9663 | 36.8815 | 37.7687 | 38.6912 | 39.6575 | 40.6595 | 41.5287 | 42.4345 | 43.3731 | 44.3406 | 45.3123 | 46.2422 | 47.179 | 48.1279 | 49.0561 | 50.052 | 51.1758 | 52.3439 | 53.5693 | 54.8185 | 56.0725 | 57.0929 | 58.1212 | 59.1536 | 60.145 | 61.2154
history projections

## Slide 28: —and constitutes more than half of global energy consumption
The industrial sector, which includes refining, mining, manufacturing, agriculture, and construction, accounts for the largest share of energy consumption of any end-use sector—more than 50% of end-use energy consumption during the entire projection period. World industrial sector energy use increases by more than 30% from 2018 to 2050, reaching about 315 quadrillion British thermal units (Btu) by 2050.
Gross output, a measure of total sales across sectors, more than doubles during the projection period from 2018 to 2050, and about half of this growth is related to industrial activity. The remaining growth comes from the service sector and reflects non-industrial activities.
Most of the increase in industrial sector energy use occurs in non-OECD nations. Industrial sector energy use in non-OECD countries grows by more than 1.0% per year in the Reference case compared with an increase of 0.5% per year in OECD countries.

## Slide 29: While energy consumption in each end-use sector grows—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Transportation | 102.4522 | 104.3797 | 105.4922 | 107.5856 | 110.5127 | 113.6755 | 117.3951 | 119.2872 | 120.9023 | 122.447 | 123.7522 | 125.0981 | 126.4934 | 127.7024 | 128.9032 | 130.0412 | 131.133 | 132.1603 | 133.1247 | 134.0618 | 134.9489 | 135.8013 | 136.6145 | 137.5034 | 138.5733 | 139.833 | 141.1355 | 142.5687 | 144.0703 | 145.6594 | 147.1801 | 149.0126 | 150.7926 | 152.7806 | 154.8044 | 156.8565 | 158.795 | 160.8724 | 162.9456 | 165.0053 | 167.1987
Industrial | 213.8817 | 222.5712 | 230.2865 | 232.1325 | 235.7529 | 236.3652 | 236.9216 | 235.9757 | 238.8226 | 238.6509 | 240.1235 | 242.1928 | 243.0449 | 244.0862 | 245.373 | 247.2717 | 248.5648 | 250.6597 | 252.789 | 255.1478 | 257.4202 | 259.9305 | 261.9275 | 264.4254 | 266.6551 | 269.5367 | 272.1645 | 274.9976 | 277.8109 | 280.5494 | 283.4513 | 286.8072 | 290.1094 | 293.2815 | 296.5562 | 299.9142 | 303.5006 | 306.6945 | 310.2674 | 313.2529 | 316.6572
Commercial | 28.784 | 28.9452 | 29.0973 | 30.2643 | 30.2501 | 31.1139 | 31.4593 | 32.0153 | 32.6148 | 32.9524 | 33.3005 | 33.6421 | 34.0213 | 34.4045 | 34.8083 | 35.2131 | 35.6922 | 36.1729 | 36.6866 | 37.2148 | 37.7441 | 38.231 | 38.7049 | 39.1891 | 39.6991 | 40.2151 | 40.7331 | 41.2387 | 41.7516 | 42.2764 | 42.8143 | 43.3719 | 43.9331 | 44.5301 | 45.1162 | 45.7205 | 46.2949 | 46.8934 | 47.4977 | 48.0839 | 48.7143
Residential | 52.528 | 52.4543 | 52.3724 | 54.4968 | 54.4386 | 54.8439 | 55.9835 | 57.4241 | 58.8846 | 59.4291 | 59.8081 | 60.2875 | 60.8782 | 61.5611 | 62.3263 | 63.0766 | 64.0535 | 65.006 | 66.0008 | 67.0802 | 68.1745 | 69.1105 | 70.0802 | 71.0751 | 72.134 | 73.194 | 74.2117 | 75.2348 | 76.263 | 77.2866 | 78.3765 | 79.6105 | 80.8654 | 82.1933 | 83.5371 | 84.8884 | 86.0038 | 87.1362 | 88.2773 | 89.3505 | 90.5516
history projections
industrial
transportation
residential
commercial
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Natural gas | 79.9888 | 82.8199 | 83.7582 | 86.4264 | 86.8641 | 86.6315 | 87.8869 | 89.1498 | 91.1322 | 92.021 | 92.8571 | 94.5092 | 95.4782 | 96.5741 | 97.7156 | 98.9533 | 100.4157 | 101.7379 | 103.0814 | 104.4435 | 105.6493 | 106.8682 | 107.8473 | 109.1496 | 110.4488 | 111.9128 | 113.0751 | 114.4709 | 115.8874 | 117.3383 | 118.8434 | 120.4248 | 121.9895 | 123.5863 | 125.2068 | 126.8884 | 128.5358 | 130.1279 | 131.8537 | 133.4395 | 135.2783
Liquids | 168.6902 | 169.5063 | 171.8223 | 173.7223 | 177.4535 | 182.0356 | 186.3722 | 187.4017 | 189.0942 | 190.321 | 191.5094 | 192.6491 | 193.5942 | 194.2968 | 195.0877 | 196.0934 | 196.6481 | 197.532 | 198.4113 | 199.2939 | 200.2206 | 201.19 | 202.0498 | 202.9156 | 203.9326 | 205.2183 | 206.533 | 207.9471 | 209.4891 | 210.8822 | 212.3979 | 214.1945 | 215.9172 | 217.7048 | 219.49 | 221.3209 | 223.1759 | 225.1081 | 227.1648 | 228.8907 | 230.9204
Coal | 68.2421 | 72.5539 | 75.827 | 75.4266 | 75.664 | 74.25 | 70.7695 | 69.4963 | 69.1282 | 68.1186 | 67.6639 | 67.1861 | 66.8248 | 66.6307 | 66.5179 | 66.4589 | 66.3527 | 66.4477 | 66.567 | 66.7926 | 67.0464 | 67.3702 | 67.6344 | 68.0343 | 68.3982 | 68.9043 | 69.5034 | 70.1063 | 70.7358 | 71.4436 | 72.1374 | 73.0343 | 73.9431 | 74.8996 | 75.9012 | 76.9227 | 77.9542 | 78.918 | 79.9357 | 80.8925 | 81.8601
Renewables | 17.2803 | 17.7939 | 18.7759 | 19.7401 | 20.3745 | 21.0336 | 22.587 | 22.7592 | 22.9165 | 22.695 | 22.9081 | 23.0993 | 23.2265 | 23.3742 | 23.5808 | 23.8464 | 24.0205 | 24.339 | 24.6566 | 25.0428 | 25.401 | 25.7699 | 26.0903 | 26.497 | 26.8087 | 27.2308 | 27.6745 | 28.1031 | 28.5049 | 28.8918 | 29.2911 | 29.7624 | 30.2049 | 30.5973 | 31.0098 | 31.413 | 31.8895 | 32.3156 | 32.7769 | 33.1494 | 33.5821
Electricity | 63.4445 | 65.6764 | 67.0649 | 69.1637 | 70.5982 | 72.0479 | 74.1439 | 75.8952 | 78.9533 | 80.3237 | 82.0458 | 83.7768 | 85.314 | 86.8785 | 88.5087 | 90.2507 | 92.0065 | 93.9422 | 95.8848 | 97.9318 | 99.9703 | 101.875 | 103.7053 | 105.5965 | 107.4732 | 109.5127 | 111.4588 | 113.4124 | 115.2786 | 117.2158 | 119.1524 | 121.3862 | 123.6457 | 125.9975 | 128.4061 | 130.8346 | 133.0389 | 135.127 | 137.2568 | 139.3205 | 141.481

## Slide 30: —end-use fuel composition increasingly shifts toward electricity
End-use fuels include those fuels consumed in the industrial, transportation, and buildings sectors and exclude fuels used for electric power generation.
Liquid fuels, because of energy density, cost, and chemical properties, continue to be the predominant transportation fuel and an important industrial feedstock.
Electricity use in the residential and commercial building sectors increases rapidly because of growing income, a growing population, and increased access to electricity in non-OECD regions.
Electricity use in the industrial sector and transportation sector also grows, respectively, as a result of increasing product demand and increasing use of electric vehicles.
Coal continues to be an important end-use fuel in industrial processes, including the production of cement and steel.

## Slide 31: Renewable energy becomes the leading source of primary energy consumption by 2050 in the Reference case—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
petroleum and other liquids (including biofuels) | 177.1134 | 178.1151 | 180.905 | 182.5306 | 185.17 | 189.236 | 192.3045 | 196.3772 | 198.9067 | 201.4107 | 203.3438 | 204.2479 | 204.9958 | 205.4973 | 206.0977 | 206.9262 | 207.3929 | 208.2029 | 209.0014 | 209.8059 | 210.6537 | 211.6128 | 212.4554 | 213.3034 | 214.3079 | 215.5909 | 216.9236 | 218.3636 | 219.9364 | 221.3475 | 222.882 | 224.7715 | 226.5857 | 228.4582 | 230.3369 | 232.2627 | 234.2361 | 236.2908 | 238.4794 | 240.322 | 242.4784
natural gas | 119.4739 | 123.0407 | 125.8031 | 127.5078 | 128.2341 | 130.1315 | 132.8652 | 135.2757 | 138.1902 | 138.8932 | 139.9052 | 141.3506 | 142.2871 | 143.1639 | 143.9712 | 145.1821 | 147.1665 | 148.9179 | 150.7007 | 152.2809 | 153.7743 | 155.8944 | 157.9705 | 160.0602 | 162.1918 | 164.4619 | 166.3872 | 168.5964 | 170.7634 | 172.9608 | 175.3318 | 177.7108 | 180.1777 | 182.5719 | 185.0794 | 187.6381 | 189.8404 | 191.9514 | 194.3152 | 196.4473 | 198.8813
coal | 155.1826 | 164.8458 | 170.9137 | 173.7897 | 173.0709 | 168.7674 | 162.595 | 161.3757 | 160.0896 | 158.1461 | 156.7278 | 155.9609 | 155.6045 | 155.5206 | 155.6111 | 155.6036 | 155.2934 | 155.2068 | 155.2005 | 155.5401 | 155.7602 | 156.0513 | 156.1351 | 156.6697 | 157.0363 | 157.655 | 158.2975 | 158.8695 | 159.5295 | 160.2701 | 161.0195 | 162.3808 | 163.7937 | 165.2394 | 166.7836 | 168.3692 | 170.5593 | 172.7098 | 174.9276 | 177.0655 | 179.2196
nuclear | 27.3807 | 26.2491 | 24.478 | 24.6535 | 25.1392 | 25.439 | 25.7129 | 27.415 | 27.9585 | 28.346 | 28.7235 | 28.8809 | 28.8741 | 28.9896 | 29.4051 | 29.5319 | 29.9954 | 30.5535 | 31.1116 | 31.6718 | 32.2341 | 32.4782 | 32.6066 | 32.8549 | 33.1032 | 33.3515 | 33.6454 | 33.9393 | 34.2331 | 34.527 | 34.8209 | 35.0769 | 35.3329 | 35.5889 | 35.845 | 36.101 | 36.4555 | 36.8099 | 37.1644 | 37.5189 | 37.8731
renewable energy (excluding biofuels) | 58.3469 | 60.7681 | 63.8961 | 68.1424 | 71.1197 | 72.6801 | 77.5065 | 89.0925 | 94.8431 | 100.1804 | 106.3321 | 110.9372 | 115.1227 | 119.3254 | 123.4629 | 127.6732 | 132.4957 | 137.5004 | 142.5198 | 147.6745 | 152.751 | 157.4401 | 162.0083 | 166.6738 | 171.3313 | 176.0971 | 181.0932 | 186.0544 | 191.031 | 196.0037 | 200.8242 | 206.6458 | 212.3015 | 218.0413 | 223.6904 | 229.3329 | 233.9761 | 238.6058 | 243.1281 | 247.6839 | 252.246
history projections
renewables
petroleum
and other
liquids
natural gas
coal
nuclear
Chart: 
| 2018 | 2050
Nuclear | 27.9585 | 37.8731
Natural gas | 138.1902 | 198.8813
Coal | 160.0896 | 179.2196
Liquids | 198.9067 | 242.4784
Renewables | 94.8431 | 252.246

## Slide 32: —although consumption increases for all primary energy sources
Use of all primary energy sources grows throughout the Reference case. Although renewable energy is the world’s fastest growing form of energy, fossil fuels to continue to meet much of the world’s energy demand.
Driven by electricity demand growth and economic and policy drivers, worldwide renewable energy consumption increases by 3% per year between 2018 and 2050. Nuclear consumption increases by 1% per year.
As a share of primary energy consumption, petroleum and other liquids declines from 32% in 2018 to 27% in 2050. On an absolute basis, liquids consumption increases in the industrial, commercial, and transportation sectors and declines in the residential and electric power sectors.
Natural gas is the world’s fastest growing fossil fuel, increasing by 1.1% per year, compared with liquids’ 0.6% per year growth and coal’s 0.4% per year growth.
Coal use is projected to decline until the 2030s as regions replace coal with natural gas and renewables in electricity generation as a result of both cost and policy drivers. In the 2040s, coal use increases as a result of increased industrial usage and rising use in electric power generation in non-OECD Asia excluding China.

## Slide 33: Industrial

## Slide 35: World industrial gross output growth continues to slow—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
OECD | 0.12163 | 0.083754 | 0.057445 | 0.063978 | 0.06067 | 0.048548 | 0.054382 | 0.049458 | 0.049591 | 0.037345 | 0.043389 | 0.04362 | 0.040438 | 0.038157 | 0.037025 | 0.036469 | 0.035566 | 0.034793 | 0.034311 | 0.033426 | 0.03294 | 0.031857 | 0.030656 | 0.030187 | 0.029914 | 0.029623 | 0.029428 | 0.029038 | 0.028195 | 0.027599 | 0.027589 | 0.027314 | 0.027493 | 0.027316 | 0.027044 | 0.026747 | 0.025909 | 0.025217 | 0.024678 | 0.023935 | 0.023672
non-OECD | 0.059127 | 0.04762 | 0.0062822 | 0.015404 | 0.026974 | -0.0069963 | 0.006385 | 0.036941 | 0.021592 | 0.011561 | 0.014873 | 0.017304 | 0.017799 | 0.016139 | 0.015489 | 0.015651 | 0.015824 | 0.015779 | 0.015439 | 0.015234 | 0.01468 | 0.013679 | 0.012598 | 0.012579 | 0.013156 | 0.013442 | 0.013151 | 0.012943 | 0.012525 | 0.012629 | 0.01299 | 0.013012 | 0.013209 | 0.0129 | 0.012562 | 0.012755 | 0.012595 | 0.012308 | 0.011991 | 0.012047 | 0.012613
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
OECD | 71.5616 | 75.6938 | 79.2832 | 82.7613 | 87.0884
non-OECD | 142.3201 | 164.4297 | 178.137 | 200.69 | 229.5688

## Slide 36: —but non-OECD industrial energy consumption growth remains strong in the Reference case
Growth in industrial gross output, a measure of sales across industrial sectors, slows worldwide in the Reference case from 4.2% in 2018 to 2.2% in 2050. Industrial gross output growth in countries that are not part of the Organization of Economic Cooperation and Development (OECD) slows from 5.0% in 2018 to 2.3% in 2050, but it continues to outpace growth in OECD countries, which slows from 2.2% in 2018 to 1.3% in 2050.
Industrial consumption of delivered energy grows slowly from 2018 to 2050 at less than 0.5% per year in OECD countries and at 1.1% per year in non-OECD countries.
Industrial output growth outpaces energy consumption because of increased industrial energy efficiency and higher growth in non-energy-intensive manufacturing output in key regions, especially in non-OECD countries.
Declining industrial energy consumption in China is more than offset by growth in other non-OECD countries.
The industrial share of worldwide energy consumption declines from about 40% in 2018 to 35% in 2050, largely because of faster growth in the transportation sector.

## Slide 37: In the Reference case, gross output from industrial activities doubles by 2050—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
non-manufacturing | 29215.6617 | 30558.7983 | 31335.348 | 32527.8741 | 33872.7266 | 34956.2926 | 36184.3033 | 37142.0948 | 38243.8984 | 39224.7697 | 40411.9126 | 41705.0399 | 42935.9369 | 44155.8777 | 45410.7708 | 46681.4936 | 47927.7823 | 49201.6313 | 50513.1211 | 51843.9343 | 53185.6543 | 54486.9566 | 55782.5285 | 57121.0359 | 58502.5128 | 59911.7651 | 61359.15 | 62829.4243 | 64305.888 | 65816.3692 | 67389.8397 | 68966.9174 | 70614.6913 | 72281.4484 | 73979.8031 | 75709.2644 | 77448.5834 | 79215.9589 | 80996.2781 | 82796.9673 | 84687.4051
non-energy-intensive | 35277.4563 | 38401.0425 | 40290.7417 | 42517.2163 | 45251.1597 | 47207.2485 | 49656.686 | 53182.2535 | 56018.2234 | 57774.3698 | 60116.6768 | 62557.701 | 64970.6984 | 67275.2276 | 69559.0541 | 71911.8871 | 74326.5718 | 76761.5146 | 79230.5847 | 81702.1571 | 84208.5436 | 86711.5684 | 89168.8774 | 91640.7444 | 94164.8973 | 96738.0369 | 99350.5658 | 101995.3206 | 104632.0427 | 107263.1108 | 109941.1347 | 112670.4654 | 115475.5665 | 118338.2484 | 121227.3329 | 124160.0542 | 127067.2068 | 129944.9819 | 132812.2423 | 135647.6965 | 138479.6845
energy-intensive | 25625.462 | 27629.0601 | 28913.1125 | 30399.457 | 31642.4319 | 32159.5303 | 33136.8867 | 34127.8548 | 35410.6756 | 36621.5137 | 37888.7527 | 39254.8428 | 40594.0341 | 41923.6735 | 43255.6408 | 44609.9459 | 45990.2385 | 47388.5173 | 48802.9536 | 50231.7714 | 51686.4342 | 53147.1731 | 54588.3424 | 56047.2767 | 57541.5097 | 59075.1989 | 60638.8277 | 62225.2252 | 63797.6756 | 65386.7178 | 67030.1291 | 68719.3339 | 70462.6152 | 72238.8896 | 74045.5627 | 75885.9417 | 77710.1822 | 79520.4884 | 81338.7926 | 83142.8843 | 84971.9881
services | 88907.5391 | 92731.1016 | 96133.4844 | 99134.7578 | 102287.3203 | 105601.8125 | 109193.1797 | 113961.386 | 118903.634 | 123008.478 | 127486.388 | 132250.731 | 137098.48 | 141939.089 | 146961.17 | 152146.403 | 157403.566 | 162810.886 | 168394.761 | 174142.259 | 180053.437 | 186096.287 | 192111.285 | 198311.812 | 204679.798 | 211210.996 | 217845.079 | 224555.899 | 231352.095 | 238287.487 | 245438.546 | 252748.817 | 260306.634 | 268008.882 | 275881.224 | 283897.529 | 291917.841 | 300042.642 | 308250.954 | 316520.103 | 324942.081
services
(non-industrial
sector)
energy-intensive
manufacturing
non-energy-
intensive manufacturing
non-manufacturing
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
non-manufacturing | 23.6329 | 30.7445 | 32.3181 | 34.6122 | 36.8421
non-energy-intensive manufacturing and non-manufacturing | 81.9518 | 83.8113 | 92.1159 | 105.1323 | 120.0989
energy-intensive manufacturing | 107.8213 | 125.6264 | 133.0335 | 143.754 | 159.7634

## Slide 38: —with about half of industrial energy consumption in the energy-intensive industries
World gross output, a measure of total sales across business sectors, more than doubles worldwide from 2018 to 2050, with about half of this growth related to industrial activity. The remaining growth comes from the services sector and reflects non-industrial activities (i.e., commercial sector energy consumption).
Gross output shares remain steady across industrial subsectors, with energy-intensive manufacturing (basic chemicals, food, iron and steel, non-ferrous metals, non-metallic minerals, paper, and refining) maintaining about a 28% share throughout the projection period. Non-energy-intensive manufacturing (metal-based durables, other chemicals, and other manufacturing) grows from 43% to 45%, and non-manufacturing sectors decline from 29% to 27%.
Following these gross output trends, the share of energy consumed by energy-intensive manufacturing holds steady at about 50% from 2018 to 2050. During the same period, the share of energy consumed by non-energy-intensive manufacturing increases from 35% to 38%.

## Slide 39: Energy-intensive manufacturing continues its shift toward non-OECD Asia—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Africa | 838.1227 | 1035.219 | 1531.858 | 2249.502 | 3225.404
Other Asia | 2175.3889 | 3239.622 | 4753.931 | 6564.524 | 8720.021
China | 8064.1602 | 16000.02 | 21073.59 | 25646.8 | 30021.46
India | 2033.806 | 4130.51 | 8004.02 | 13672.5 | 21399
Rest Of World | 12513.9844 | 13483.3818 | 16323.0351 | 18896.8031 | 21606.1031
Energy-intensive manufacturing gross output
by region
share
history projections

## Slide 40: —with India’s share growing steadily during the projection period
Gross output for energy-intensive manufacturing, which includes the production of iron and steel, food, paper, refined oil products, non-metallic minerals, aluminum, and basic chemicals, is increasingly concentrated in the non-OECD countries of Asia. India and China combined account for more than half of global output throughout the Reference case.
India and China see growth in energy-intensive manufacturing during the projection period, but India’s share of the global activity increases, from 11% in 2018 to 25% in 2050, while China’s share decreases, from 41% to 35%.
Other regions gaining share of energy-intensive manufacturing include other non-OECD Asia and Africa, while the rest of the world, collectively, decreases its share of energy-intensive manufacturing.

## Slide 41: Non-OECD Asia leads industrial energy consumption growth—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe | 23.6608 | 22.6657 | 22.5 | 23.0033 | 23.5814
America | 33.0723 | 37.0459 | 40.2662 | 42.9615 | 45.9748
Asia | 14.8284 | 15.9822 | 16.517 | 16.7965 | 17.5322
Industrial energy consumption
quadrillion British thermal units
history projections
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe and Eurasia | 18.8702 | 19.5664 | 19.9451 | 20.5306 | 20.9677
Americas | 12.3015 | 11.964 | 13.4176 | 14.5393 | 15.4946
Africa | 9.1497 | 10.6164 | 12.5492 | 16.061 | 20.5064
Middle East | 13.9775 | 17.3068 | 18.7556 | 20.4739 | 23.0587
Other Asia | 14.6856 | 17.3857 | 19.701 | 23.1888 | 26.8268
India | 11.8377 | 16.6652 | 23.2184 | 33.8172 | 47.3363
China | 61.4979 | 70.9252 | 70.5501 | 72.0793 | 75.3783
Asia
Americas
Europe
OECD
non-OECD
China
India
other Asia
Middle East
Africa
Americas
Europe
and Eurasia

## Slide 42: —but China remains the world’s largest single industrial energy consumer and India experiences the most growth in consumption
Non-OECD countries collectively consume more energy in the industrial sector than OECD countries, and their energy consumption growth is about twice the rate as in OECD countries through the projection period.
In 2018, China consumed 29% of the world’s industrial energy, and although its energy consumption continues to increase modestly throughout the projection period, its share decreases to 24% by 2050.
India’s industrial energy consumption nearly triples, growing from 16 quadrillion British thermal units (Btu) in 2018 to 47 quadrillion Btu by 2050 at an average annual rate of 3.4%.
India’s 31 quadrillion Btu growth in energy consumption from 2018 to 2050 represents 40% of the total world increase of 78 quadrillion Btu.

## Slide 43: Non-OECD countries lead industrial energy consumption growth —
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series3 | 8.7223 | 8.9175 | 8.7234 | 8.6704 | 8.7747 | 8.6419 | 8.2311 | 8.3767 | 8.3433 | 8.2147 | 8.1527 | 8.1492 | 8.1585 | 8.1649 | 8.1704 | 8.1834 | 8.1806 | 8.1952 | 8.2117 | 8.2341 | 8.2518 | 8.2673 | 8.263 | 8.2709 | 8.2733 | 8.2877 | 8.3067 | 8.3288 | 8.3469 | 8.3624 | 8.3772 | 8.4064 | 8.4361 | 8.4632 | 8.4907 | 8.5269 | 8.5631 | 8.604 | 8.6471 | 8.6856 | 8.7272
series2 | 25.8106 | 25.6638 | 25.7363 | 25.3464 | 24.6563 | 24.9012 | 25.0537 | 25.1219 | 25.5383 | 25.5081 | 25.4307 | 25.603 | 25.6035 | 25.6295 | 25.6594 | 25.7884 | 25.7511 | 25.9186 | 26.0597 | 26.2159 | 26.3673 | 26.557 | 26.6685 | 26.7782 | 26.8709 | 27.0135 | 27.1381 | 27.3052 | 27.4799 | 27.5568 | 27.6786 | 27.8559 | 28.0005 | 28.0935 | 28.2549 | 28.395 | 28.5868 | 28.7305 | 28.9456 | 29.0232 | 29.1941
series0 | 11.1906 | 11.3475 | 11.2367 | 11.0989 | 11.0856 | 10.9123 | 11.0945 | 11.1049 | 11.1797 | 11.1353 | 11.2819 | 11.4069 | 11.4672 | 11.5307 | 11.6071 | 11.705 | 11.7638 | 11.8511 | 11.9346 | 12.0248 | 12.0914 | 12.1598 | 12.2011 | 12.2446 | 12.2772 | 12.3424 | 12.4013 | 12.4697 | 12.5224 | 12.5739 | 12.6321 | 12.7022 | 12.7637 | 12.8247 | 12.8859 | 12.9449 | 13.0196 | 13.0767 | 13.1446 | 13.1992 | 13.2647
series1 | 20.4126 | 20.7562 | 21.3202 | 22.0776 | 22.2266 | 22.2433 | 22.5682 | 23.1185 | 23.749 | 23.862 | 24.2994 | 24.712 | 24.9294 | 25.1478 | 25.3339 | 25.4203 | 25.4825 | 25.5869 | 25.7251 | 25.8381 | 25.8805 | 25.9441 | 25.9537 | 26.0626 | 26.2163 | 26.4054 | 26.5581 | 26.5825 | 26.5659 | 26.8666 | 27.1884 | 27.2353 | 27.4453 | 27.5493 | 27.5681 | 27.773 | 27.9616 | 28.2141 | 28.2932 | 28.5318 | 28.7801
series4 | 5.4254 | 5.5479 | 5.8592 | 6.0652 | 6.2934 | 6.4895 | 6.4533 | 6.6168 | 6.6123 | 6.4935 | 6.529 | 6.5427 | 6.5483 | 6.5558 | 6.5698 | 6.5967 | 6.5976 | 6.6172 | 6.6399 | 6.6699 | 6.6922 | 6.7033 | 6.7049 | 6.7237 | 6.7339 | 6.7659 | 6.7958 | 6.8259 | 6.8505 | 6.8676 | 6.8849 | 6.9163 | 6.9374 | 6.9509 | 6.9732 | 6.9969 | 7.0267 | 7.0518 | 7.0811 | 7.1022 | 7.1224
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series3 | 53.5232 | 57.5095 | 60.6119 | 60.4645 | 60.7696 | 59.519 | 56.6501 | 55.5809 | 55.3402 | 54.5396 | 54.2116 | 53.8065 | 53.4868 | 53.3307 | 53.2564 | 53.2222 | 53.1545 | 53.2661 | 53.4087 | 53.6492 | 53.9208 | 54.2595 | 54.5587 | 54.9786 | 55.367 | 55.8818 | 56.4836 | 57.0891 | 57.7247 | 58.4363 | 59.137 | 60.021 | 60.9177 | 61.8587 | 62.843 | 63.8355 | 64.8459 | 65.7818 | 66.767 | 67.6957 | 68.6295
series2 | 32.6027 | 32.3805 | 33.4717 | 33.4787 | 35.4292 | 36.2277 | 37.0951 | 36.5782 | 36.8711 | 37.1269 | 37.7197 | 38.1555 | 38.4125 | 38.5945 | 38.8579 | 39.3617 | 39.5566 | 40.0291 | 40.4507 | 40.9607 | 41.4854 | 42.038 | 42.5082 | 43.034 | 43.5233 | 44.1354 | 44.637 | 45.1943 | 45.8122 | 46.256 | 46.8002 | 47.4529 | 48.0863 | 48.5968 | 49.1922 | 49.766 | 50.4118 | 50.9654 | 51.5961 | 52.0843 | 52.707
series0 | 18.6221 | 20.2173 | 21.0386 | 22.1212 | 22.9447 | 23.1439 | 23.8673 | 23.9492 | 25.4945 | 26.0828 | 26.6165 | 27.1789 | 27.5836 | 27.9925 | 28.4003 | 28.8425 | 29.2048 | 29.6576 | 30.0783 | 30.5265 | 30.9577 | 31.3809 | 31.7392 | 32.1137 | 32.4297 | 32.8225 | 33.2099 | 33.5849 | 33.8827 | 34.2098 | 34.4989 | 34.8785 | 35.2274 | 35.6234 | 36.0081 | 36.378 | 36.7638 | 37.0469 | 37.3588 | 37.6203 | 37.9006
series1 | 26.8686 | 29.2363 | 30.5898 | 30.7357 | 31.1648 | 31.3519 | 31.801 | 31.4214 | 31.5088 | 31.6284 | 31.6439 | 32.2305 | 32.3328 | 32.4854 | 32.6816 | 33.0883 | 33.6487 | 34.0272 | 34.4863 | 34.8899 | 35.3091 | 35.8089 | 36.2099 | 36.722 | 37.1749 | 37.7138 | 38.0627 | 38.6576 | 39.2992 | 39.7344 | 40.1976 | 40.8536 | 41.4002 | 42.0589 | 42.699 | 43.289 | 43.8776 | 44.3904 | 45.1812 | 45.7187 | 46.3397
series4 | 10.7035 | 10.9947 | 11.6987 | 12.0738 | 12.408 | 12.9347 | 14.1073 | 14.1073 | 14.1853 | 14.0596 | 14.238 | 14.4077 | 14.5224 | 14.6544 | 14.8362 | 15.0632 | 15.2246 | 15.5106 | 15.7941 | 16.1386 | 16.464 | 16.8117 | 17.1201 | 17.4971 | 17.7885 | 18.1684 | 18.5712 | 18.9595 | 19.3264 | 19.6855 | 20.0563 | 20.4851 | 20.895 | 21.2622 | 21.6411 | 22.0089 | 22.4438 | 22.8328 | 23.2525 | 23.5918 | 23.992

## Slide 44: —and coal remains the most-used industrial fuel but renewables have the fastest rate of growth
Although coal consumption in non-OECD countries dips slightly through 2035 and then rebounds and grows through 2050, coal remains the most common industrial energy source in these regions. By 2050, industrial coal use declines to about one-quarter of all industrial energy consumption.
Among industrial fuels, renewables have the highest growth rate among non-OECD countries at 1.7% per year, but they represent only 10% of industrial energy consumption by 2050.

## Slide 45: Led by India, industrial use of coal in non-OECD Asia increases after the mid-2020s—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Other non-OECD Asia | 2.9125 | 2.8323 | 2.7778 | 2.8021 | 3.0681 | 3.1807 | 3.299 | 3.4121 | 3.5036 | 3.5005 | 3.5551 | 3.6141 | 3.6463 | 3.6699 | 3.7039 | 3.7541 | 3.7903 | 3.8566 | 3.9221 | 3.9978 | 4.0652 | 4.1352 | 4.1933 | 4.27 | 4.3275 | 4.3956 | 4.4792 | 4.5623 | 4.6506 | 4.734 | 4.8249 | 4.9207 | 5.0115 | 5.0929 | 5.1812 | 5.2624 | 5.3507 | 5.4455 | 5.5161 | 5.5933 | 5.6908
China | 39.8948 | 43.2434 | 45.7536 | 45.7245 | 45.3459 | 43.9611 | 40.73 | 39.5795 | 39.017 | 38.1907 | 37.6057 | 36.8364 | 36.1946 | 35.6937 | 35.2432 | 34.7786 | 34.2954 | 33.9035 | 33.5257 | 33.1975 | 32.9039 | 32.6469 | 32.3822 | 32.1881 | 31.9889 | 31.8686 | 31.7793 | 31.705 | 31.631 | 31.6412 | 31.5907 | 31.6819 | 31.7558 | 31.9022 | 32.0597 | 32.2421 | 32.3782 | 32.4773 | 32.6046 | 32.6712 | 32.7566
India | 4.4794 | 4.8549 | 5.4254 | 5.6127 | 6.0913 | 5.9124 | 6.0241 | 6.0751 | 6.2465 | 6.2996 | 6.4491 | 6.6834 | 6.9114 | 7.1607 | 7.4424 | 7.7603 | 8.0897 | 8.4718 | 8.8722 | 9.2912 | 9.7166 | 10.1684 | 10.625 | 11.1038 | 11.5785 | 12.0717 | 12.6044 | 13.1292 | 13.6869 | 14.2339 | 14.8302 | 15.4565 | 16.1123 | 16.7503 | 17.412 | 18.0613 | 18.7634 | 19.4242 | 20.1308 | 20.8491 | 21.5429
row | 14.9588 | 15.4964 | 15.3785 | 14.9957 | 15.039 | 15.1067 | 14.8281 | 14.8908 | 14.9165 | 14.7635 | 14.7545 | 14.8218 | 14.893 | 14.9713 | 15.0373 | 15.1127 | 15.1597 | 15.2294 | 15.3004 | 15.3968 | 15.487 | 15.5764 | 15.6212 | 15.6877 | 15.7454 | 15.8335 | 15.9275 | 16.0214 | 16.1032 | 16.1896 | 16.2684 | 16.3682 | 16.4742 | 16.5766 | 16.6808 | 16.7966 | 16.9167 | 17.0389 | 17.1626 | 17.2678 | 17.3663
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
elec | 1.4926 | 1.651 | 1.7229 | 1.8195 | 1.975 | 2.0359 | 2.091 | 2.1092 | 2.1617 | 2.1809 | 2.2228 | 2.2755 | 2.316 | 2.365 | 2.4254 | 2.4944 | 2.562 | 2.6434 | 2.7279 | 2.817 | 2.9087 | 3.005 | 3.1024 | 3.2048 | 3.3046 | 3.4134 | 3.5281 | 3.644 | 3.761 | 3.8765 | 4.0025 | 4.1369 | 4.2754 | 4.4125 | 4.5544 | 4.6939 | 4.846 | 4.9821 | 5.1359 | 5.2872 | 5.4367
renewables | 1.7623 | 1.8567 | 1.9367 | 2.0075 | 2.0714 | 2.1059 | 2.5317 | 2.5095 | 2.5511 | 2.5071 | 2.5314 | 2.5766 | 2.6011 | 2.6398 | 2.697 | 2.7735 | 2.8361 | 2.9274 | 3.0204 | 3.1295 | 3.2389 | 3.3547 | 3.4698 | 3.5926 | 3.7009 | 3.8311 | 3.9655 | 4.0993 | 4.2273 | 4.3478 | 4.4927 | 4.6427 | 4.7955 | 4.9281 | 5.084 | 5.2101 | 5.3645 | 5.4769 | 5.6279 | 5.7764 | 5.9036
gas | 1.4699 | 1.5115 | 1.5596 | 1.5902 | 1.5833 | 1.5099 | 1.6477 | 1.6521 | 1.6807 | 1.6862 | 1.7395 | 1.8144 | 1.8882 | 1.965 | 2.047 | 2.1359 | 2.2288 | 2.3332 | 2.4413 | 2.5519 | 2.667 | 2.7904 | 2.92 | 3.0579 | 3.1984 | 3.3463 | 3.5023 | 3.6586 | 3.8282 | 3.9946 | 4.1691 | 4.3516 | 4.5426 | 4.7343 | 4.9277 | 5.1238 | 5.3288 | 5.5282 | 5.7334 | 5.9398 | 6.1468
liquids | 2.6335 | 2.7412 | 2.9763 | 2.9454 | 3.0661 | 3.4491 | 3.6882 | 3.6574 | 3.6956 | 3.6709 | 3.7225 | 3.7894 | 3.8384 | 3.8983 | 3.976 | 4.0887 | 4.1697 | 4.2871 | 4.4102 | 4.5445 | 4.6872 | 4.8349 | 4.9825 | 5.1339 | 5.2861 | 5.4557 | 5.627 | 5.7966 | 5.9756 | 6.1349 | 6.3226 | 6.5241 | 6.7291 | 6.9125 | 7.1168 | 7.3073 | 7.5198 | 7.6984 | 7.911 | 8.106 | 8.3063
coal | 4.4794 | 4.8549 | 5.4254 | 5.6127 | 6.0913 | 5.9124 | 6.0241 | 6.0751 | 6.2465 | 6.2996 | 6.4491 | 6.6834 | 6.9114 | 7.1607 | 7.4424 | 7.7603 | 8.0897 | 8.4718 | 8.8722 | 9.2912 | 9.7166 | 10.1684 | 10.625 | 11.1038 | 11.5785 | 12.0717 | 12.6044 | 13.1292 | 13.6869 | 14.2339 | 14.8302 | 15.4565 | 16.1123 | 16.7503 | 17.412 | 18.0613 | 18.7634 | 19.4242 | 20.1308 | 20.8491 | 21.5429
history projections

## Slide 46: —as a result of growth in coal-intensive industries and relatively low coal prices
In 2018, China accounted for more than 60% of the world’s industrial coal consumption, but its share falls to a little more than 40% in 2050 because of consumption growth in other countries and China’s policies to reduce coal use in the industrial sector. However, in the Reference case, China remains the world’s largest industrial coal consumer because of continued coal use in the chemicals sector.
Growth in India’s steel and cement sectors makes India the country with the highest industrial coal growth rate in the world. By 2050, more than two-thirds of worldwide industrial coal is consumed in India and China.
In the Reference case, flat coal prices relative to increasing natural gas prices keep coal a preferred industrial fuel for boilers and process heat.
In the Reference case, natural gas prices in China are nearly double coal prices on an energy equivalent basis by 2050, which leads to an increase in coal consumption in the later years.
Natural gas prices in India are consistently higher than coal and reach almost four times that of coal on an energy equivalent basis by 2050, encouraging industrial coal use instead of natural gas.

## Slide 47: Non-OECD economies increase industrial electricity use—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Renewables | 0.0001 | 0.0002 | 0.0003 | 0.0004 | 0.0003 | 0.0002 | 0 | 0.0021257 | 0.0021968 | 0.002139 | 0.0021606 | 0.0021037 | 0.0020369 | 0.0020005 | 0.0019447 | 0.0019002 | 0.0018957 | 0.0018916 | 0.0018107 | 0.0017365 | 0.0016682 | 0.0016192 | 0.0015648 | 0.0015171 | 0.0014749 | 0.0014408 | 0.0014391 | 0.0013928 | 0.0013471 | 0.0013075 | 0.001271 | 0.0012311 | 0.0011929 | 0.0011566 | 0.0011245 | 0.0010949 | 0.0010707 | 0.0010482 | 0.0010312 | 0.0010191 | 0.0010035
Liquids | 0.0888 | 0.0969 | 0.071 | 0.0602 | 0.0555 | 0.0435 | 0.0406 | 0.04695 | 0.047877 | 0.048029 | 0.048954 | 0.049701 | 0.050375 | 0.050907 | 0.051098 | 0.05158 | 0.052068 | 0.052695 | 0.053142 | 0.05364 | 0.054157 | 0.05466 | 0.054997 | 0.055374 | 0.055711 | 0.056154 | 0.056614 | 0.057049 | 0.057312 | 0.057712 | 0.057876 | 0.058346 | 0.058648 | 0.059104 | 0.059619 | 0.060103 | 0.060442 | 0.060626 | 0.060965 | 0.061217 | 0.061359
Natural Gas | 0.115 | 0.1406 | 0.1807 | 0.1779 | 0.1884 | 0.1831 | 0.1927 | 0.23637 | 0.2435 | 0.24503 | 0.25124 | 0.25584 | 0.2584 | 0.26072 | 0.26162 | 0.2637 | 0.26658 | 0.27059 | 0.27469 | 0.279 | 0.28332 | 0.28585 | 0.2875 | 0.28949 | 0.29121 | 0.29339 | 0.29752 | 0.30201 | 0.30599 | 0.31034 | 0.31385 | 0.31876 | 0.32329 | 0.32828 | 0.33337 | 0.33846 | 0.34312 | 0.34676 | 0.35103 | 0.35491 | 0.35867
Coal | 0.2109 | 0.1978 | 0.2162 | 0.2066 | 0.1606 | 0.1363 | 0.0978 | 0.13432 | 0.13481 | 0.13451 | 0.1358 | 0.13634 | 0.13734 | 0.13802 | 0.13785 | 0.13862 | 0.13932 | 0.14045 | 0.14123 | 0.14212 | 0.14305 | 0.14385 | 0.14417 | 0.14461 | 0.14486 | 0.14547 | 0.146 | 0.14653 | 0.14643 | 0.14691 | 0.14642 | 0.14715 | 0.1471 | 0.14775 | 0.14858 | 0.14934 | 0.14923 | 0.14874 | 0.14873 | 0.14834 | 0.14772
Electricity | 0.412 | 0.4397 | 0.42 | 0.449 | 0.4501 | 0.4792 | 0.5222 | 0.5446 | 0.55698 | 0.56198 | 0.5732 | 0.58403 | 0.59439 | 0.60278 | 0.60812 | 0.61673 | 0.6252 | 0.6355 | 0.64583 | 0.65669 | 0.66795 | 0.67919 | 0.68922 | 0.69984 | 0.71038 | 0.72216 | 0.7333 | 0.74541 | 0.75584 | 0.76821 | 0.7783 | 0.79226 | 0.80462 | 0.81903 | 0.83463 | 0.85015 | 0.86474 | 0.878 | 0.89333 | 0.90796 | 0.922
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Renewables | 0.0004 | 0.0004 | 0.0004 | 0.0005 | 0.0006 | 0.0004 | 0.0004 | 0.0014214 | 0.0013391 | 0.0012548 | 0.0011867 | 0.0011673 | 0.0011338 | 0.0011045 | 0.0010774 | 0.0010546 | 0.0010302 | 0.0010107 | 0.0009937 | 0.00098165 | 0.00096801 | 0.00099586 | 0.0010321 | 0.0010742 | 0.0011257 | 0.0011833 | 0.0011888 | 0.0011765 | 0.0011605 | 0.0011515 | 0.0011437 | 0.001123 | 0.0011009 | 0.0010777 | 0.0010568 | 0.0010361 | 0.0010275 | 0.0010206 | 0.0010203 | 0.0010228 | 0.0010175
Liquids | 0.2381 | 0.195 | 0.1718 | 0.1567 | 0.1509 | 0.1536 | 0.1492 | 0.1489 | 0.14788 | 0.14695 | 0.14683 | 0.14776 | 0.14913 | 0.15042 | 0.15178 | 0.15312 | 0.15415 | 0.15527 | 0.15668 | 0.15814 | 0.1591 | 0.15951 | 0.16012 | 0.16088 | 0.16171 | 0.16269 | 0.16375 | 0.16483 | 0.16579 | 0.16682 | 0.16785 | 0.1691 | 0.17042 | 0.17166 | 0.17298 | 0.17426 | 0.1755 | 0.17665 | 0.17782 | 0.17886 | 0.17982
Natural Gas | 0.1258 | 0.1416 | 0.1728 | 0.2032 | 0.2294 | 0.2268 | 0.2231 | 0.2262 | 0.22312 | 0.21668 | 0.21446 | 0.21443 | 0.21209 | 0.20978 | 0.20728 | 0.20441 | 0.20147 | 0.19882 | 0.19651 | 0.19449 | 0.19233 | 0.19079 | 0.18946 | 0.18838 | 0.18744 | 0.18669 | 0.18533 | 0.18398 | 0.18249 | 0.1812 | 0.17996 | 0.17881 | 0.17791 | 0.17697 | 0.1762 | 0.17544 | 0.17482 | 0.17403 | 0.17328 | 0.17239 | 0.17118
Coal | 0.8979 | 0.9042 | 0.8733 | 0.958 | 1.0257 | 1.0243 | 0.9663 | 1.0201 | 0.99685 | 0.97225 | 0.95318 | 0.93707 | 0.92397 | 0.91099 | 0.89875 | 0.88801 | 0.87804 | 0.86965 | 0.86264 | 0.85678 | 0.85144 | 0.84655 | 0.84208 | 0.83894 | 0.83669 | 0.83561 | 0.8357 | 0.83623 | 0.83713 | 0.83934 | 0.84198 | 0.84613 | 0.85115 | 0.85692 | 0.86342 | 0.87058 | 0.87795 | 0.88479 | 0.8918 | 0.8984 | 0.90486
Electricity | 1.8464 | 2.0047 | 2.1013 | 2.2234 | 2.3453 | 2.8041 | 2.926 | 2.9157 | 3.0552 | 3.2161 | 3.2819 | 3.3695 | 3.4491 | 3.5153 | 3.5821 | 3.6497 | 3.7205 | 3.7877 | 3.8549 | 3.9177 | 3.9792 | 4.0386 | 4.0895 | 4.1355 | 4.1817 | 4.2264 | 4.2681 | 4.2953 | 4.3074 | 4.3125 | 4.312 | 4.3106 | 4.3152 | 4.3229 | 4.3292 | 4.3364 | 4.3418 | 4.3306 | 4.3196 | 4.3063 | 4.2912
electricity
coal
natural gas
liquids
history projections
Energy consumption, non-OECD motor vehicle
production
quadrillion British thermal units
Energy consumption, non-OECD non-ferrous metals
production
quadrillion British thermal units

## Slide 48: —led by growth in the motor vehicle and non-ferrous metals industries
Non-OECD countries increase industrial electricity consumption by 49% from 2018 to 2050 while OECD nations experience an increase of 19% during the same period.
Emerging economies with industrial sectors that are not fully developed have a greater ability to increase electrification as newer technologies are used. From 2018 to 2050, purchased electricity is the fastest-growing fuel consumed in the non-OECD industrial sector; natural gas is the fastest-growing fuel in the OECD.
Industrial energy shares change slowly. Non-OECD industrial sector electricity consumption as a share of total energy consumption grows from 16% to 17% from 2018 to 2050, while it remains at about 15% in the OECD countries.
The metal-based durables and non-ferrous metals industries experience significantly greater growth in their share of electricity consumption.
Electricity as a share of motor vehicle manufacturing energy consumption increases from 56% in 2018 to 62% in 2050 in non-OECD countries, while OECD consumption in this industry remains steady at 55% during the same period. Declining electricity prices in non-OECD regions contribute to this change.

## Slide 49: Buildings

## Slide 51: Non-OECD countries drive increases in building energy consumption—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
commercial | 19.9434 | 19.6439 | 19.3128 | 20.044 | 19.9155 | 20.3114 | 20.2614 | 20.6087 | 20.979 | 21.1192 | 21.2151 | 21.3271 | 21.4486 | 21.567 | 21.6866 | 21.8076 | 21.9512 | 22.1033 | 22.2675 | 22.4425 | 22.6056 | 22.7461 | 22.8818 | 23.0172 | 23.1743 | 23.3352 | 23.4953 | 23.6568 | 23.8183 | 23.9967 | 24.1709 | 24.3572 | 24.5388 | 24.7361 | 24.9308 | 25.1359 | 25.3538 | 25.587 | 25.8225 | 26.0494 | 26.3118
residential | 28.6483 | 27.2338 | 26.5643 | 27.7657 | 26.7405 | 26.4591 | 26.3229 | 26.5254 | 27.3745 | 27.3688 | 27.1447 | 27.0854 | 27.0573 | 27.0682 | 27.097 | 27.1103 | 27.172 | 27.2373 | 27.3096 | 27.4228 | 27.515 | 27.5818 | 27.6457 | 27.702 | 27.7934 | 27.8817 | 27.9695 | 28.0558 | 28.1351 | 28.2306 | 28.3245 | 28.4347 | 28.5215 | 28.624 | 28.7186 | 28.8159 | 28.9109 | 29.015 | 29.1236 | 29.2055 | 29.3363
Building sector energy consumption
quadrillion British thermal units
history projections
OECD
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
commercial | 8.8406 | 9.3013 | 9.7845 | 10.2203 | 10.3346 | 10.8026 | 11.1979 | 11.4066 | 11.6358 | 11.8332 | 12.0854 | 12.315 | 12.5727 | 12.8374 | 13.1216 | 13.4055 | 13.741 | 14.0696 | 14.4191 | 14.7723 | 15.1385 | 15.485 | 15.8231 | 16.1719 | 16.5247 | 16.8799 | 17.2377 | 17.582 | 17.9333 | 18.2797 | 18.6434 | 19.0147 | 19.3943 | 19.794 | 20.1854 | 20.5847 | 20.9411 | 21.3064 | 21.6751 | 22.0345 | 22.4025
residential | 23.8797 | 25.2205 | 25.808 | 26.7311 | 27.6981 | 28.3848 | 29.6607 | 30.8987 | 31.5101 | 32.0603 | 32.6634 | 33.2021 | 33.8209 | 34.493 | 35.2293 | 35.9663 | 36.8815 | 37.7687 | 38.6912 | 39.6575 | 40.6595 | 41.5287 | 42.4345 | 43.3731 | 44.3406 | 45.3123 | 46.2422 | 47.179 | 48.1279 | 49.0561 | 50.052 | 51.1758 | 52.3439 | 53.5693 | 54.8185 | 56.0725 | 57.0929 | 58.1212 | 59.1536 | 60.145 | 61.2154
non-OECD
residential
commercial

## Slide 52: —as population and incomes grow faster in non-OECD countries
Energy consumed in the buildings sector, which includes residential and commercial structures, increases by 1.3% per year in the Reference case—a growth rate greater than that of worldwide annual population—up from 91 quadrillion to 139 quadrillion British thermal units (Btu) from 2018 to 2050. The buildings sector’s share of the world’s delivered energy consumption increases from about 20% in 2018 to 22% in 2050.
Most of the increase in energy use comes from countries that are not part of the Organization of Economic Cooperation and Development (OECD). Non-OECD countries are experiencing rising income, urbanization, and increased access to electricity, which lead to rising demand for energy. Building energy consumption in non-OECD countries increases at about 2% per year, about five times faster than in OECD countries, and non-OECD building energy consumption surpasses that of OECD countries by 2025.
In OECD countries, buildings energy consumption is projected increases at an average of 0.4% per year from 2018 to 2050, reflecting slow growth in personal income and gains in energy efficiency as a result of improved building shells, appliances, and equipment.

## Slide 53: Residential energy consumption per person increases in non-OECD countries—
Residential energy consumption per person
million British thermal units per person
Chart: 
| Mexico and Chile | Japan | South Korea | Australia and New Zealand | OECD Europe | United States | Canada | OECD
2050 | 4.5997 | 17.1615 | 19.3767 | 19.8172 | 19.566 | 28.5747 | 35.4522 | 20.4144
2018 | 4.0466 | 14.6502 | 15.7197 | 17.5325 | 18.5113 | 34.8093 | 36.5095 | 20.9588
Chart: 
| Africa | other Asia | Brazil | other Americas | India | other Europe and Eurasia | China | Middle East | Russia | non-OECD
2050 | 1.8524 | 3.2515 | 5.3446 | 5.6797 | 6.9357 | 16.314 | 16.1808 | 20.9016 | 36.8661 | 7.4525
2018 | 1.5969 | 2.239 | 4.1462 | 4.9181 | 2.0131 | 11.8551 | 8.0706 | 16.4876 | 27.8233 | 4.9638

## Slide 54: —but remains lower on average than residential per person energy consumption in OECD countries
In the Reference case, world residential energy consumption per person (energy intensity) increases by 0.6% per year from 2018 to 2050, as residential energy consumption (1.4% per year) grows faster than world population growth (0.7% per year). EIA does not consider non-marketed sources of energy, such as wood and waste in its IEO analyses.
In OECD countries, residential energy intensity decreases by an average of 0.1% per year from 2018 to 2050, compared with an average increase of 1.3% per year in non-OECD countries during the same period.
In the Reference case, India experiences the fastest relative growth in per person residential energy use because of increased access to energy sources and increased use of appliances and other energy-using equipment. However, in 2050, India’s residential use per person is only about 24% of that in the United States.
Although residential energy intensity in Africa grows by about 16% from 2018 to 2050, it remains the least energy-intensive region.

## Slide 55: Non-OECD countries, led by growing demand in China and India—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe | 11.9057 | 10.8912 | 11.2639 | 11.6145 | 12.0342
America | 13.3277 | 13.0429 | 12.8772 | 13.1875 | 13.6271
Asia | 3.415 | 3.2105 | 3.3739 | 3.5225 | 3.675
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe and Eurasia | 6.587 | 6.2689 | 6.8021 | 7.2541 | 7.832
Americas | 1.8667 | 2.2795 | 2.5023 | 2.841 | 3.2153
Africa | 1.539 | 2.1217 | 2.6705 | 3.4709 | 4.4329
Middle East | 3.2933 | 4.1761 | 5.0709 | 6.0638 | 7.0656
Other Asia | 2.0383 | 2.9123 | 3.6197 | 4.3081 | 5.0957
India | 1.8097 | 2.9469 | 5.0942 | 7.8407 | 11.5094
China | 6.7456 | 11.9579 | 14.8998 | 18.2735 | 22.0646
China
India
other Asia
Middle East
Africa
Americas
Europe
and Eurasia

## Slide 56: —account for most of the increase in residential energy consumption
OECD countries have modest growth in residential energy consumption, growing only 7% from 2018 to 2050.
Non-OECD Asia, a region that includes India and China, remains the fastest-growing region in residential sector energy consumption. About 70% of the projected increase in residential energy consumption occurs in non-OECD Asia, as standards of living increase and as demand for lighting and energy-using appliances and equipment increases.
China adds the most residential energy consumption of any country (in absolute terms), while India experiences the fastest relative growth in residential energy consumption from 2018 to 2050.
Residential energy consumption in Africa grows by an average of 2.5% per year from 2018 to 2050—which is faster than its population growth of 1.9% per year.

## Slide 57: In the Reference case, residential energy consumption increases from 2018 to 2050—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series2 | 4.3407 | 3.9445 | 3.8051 | 3.839 | 3.6303 | 3.6004 | 3.3953 | 3.5393 | 3.4935 | 3.4435 | 3.3588 | 3.2815 | 3.2378 | 3.2083 | 3.1883 | 3.1569 | 3.1419 | 3.1211 | 3.1117 | 3.1001 | 3.0984 | 3.0905 | 3.0809 | 3.0625 | 3.0585 | 3.0481 | 3.0413 | 3.0318 | 3.016 | 3.0162 | 3.0072 | 3.0033 | 2.9906 | 2.9917 | 2.9796 | 2.9761 | 2.959 | 2.9596 | 2.9575 | 2.947 | 2.9413
series4 | 0.67506 | 0.66813 | 0.55564 | 0.69461 | 0.70652 | 0.54827 | 0.59617 | 0.58528 | 0.65858 | 0.671 | 0.65949 | 0.65672 | 0.65279 | 0.64995 | 0.64983 | 0.65048 | 0.65112 | 0.65274 | 0.65291 | 0.65307 | 0.65196 | 0.6506 | 0.64921 | 0.64828 | 0.64652 | 0.64469 | 0.64362 | 0.64158 | 0.63967 | 0.63802 | 0.63669 | 0.63521 | 0.63421 | 0.63297 | 0.63143 | 0.63013 | 0.6289 | 0.62765 | 0.62661 | 0.62537 | 0.62412
series3 | 0.75955 | 0.67869 | 0.69036 | 0.6347 | 0.56607 | 0.56125 | 0.57057 | 0.55965 | 0.54805 | 0.53916 | 0.53179 | 0.52906 | 0.52613 | 0.52315 | 0.52018 | 0.51809 | 0.51477 | 0.51217 | 0.50943 | 0.50708 | 0.50379 | 0.50061 | 0.49761 | 0.49463 | 0.4918 | 0.489 | 0.48632 | 0.48375 | 0.48133 | 0.47903 | 0.47687 | 0.47474 | 0.47277 | 0.4709 | 0.46919 | 0.46758 | 0.46603 | 0.4646 | 0.46331 | 0.46215 | 0.46113
series1 | 12.1776 | 11.4175 | 11.1197 | 12.1011 | 11.4383 | 11.2517 | 11.2284 | 11.4876 | 11.9603 | 12.0241 | 11.851 | 11.8314 | 11.8004 | 11.7886 | 11.7824 | 11.7705 | 11.7765 | 11.7854 | 11.7848 | 11.8166 | 11.8241 | 11.8243 | 11.8279 | 11.8316 | 11.8461 | 11.8609 | 11.8723 | 11.8861 | 11.8992 | 11.91 | 11.9264 | 11.9546 | 11.9676 | 11.9809 | 11.9985 | 12.011 | 12.024 | 12.0307 | 12.0451 | 12.0426 | 12.0715
series0 | 10.6955 | 10.525 | 10.3936 | 10.4962 | 10.3994 | 10.4975 | 10.5325 | 10.3535 | 10.7141 | 10.6911 | 10.7436 | 10.7867 | 10.8402 | 10.8982 | 10.9563 | 11.0143 | 11.0877 | 11.1659 | 11.2507 | 11.3459 | 11.4367 | 11.5157 | 11.59 | 11.6649 | 11.7505 | 11.839 | 11.9259 | 12.0126 | 12.0989 | 12.1873 | 12.2773 | 12.3668 | 12.4564 | 12.5475 | 12.6398 | 12.7311 | 12.833 | 12.9324 | 13.0311 | 13.1283 | 13.2382
Residential sector energy consumption by fuel
quadrillion British thermal units
history projections
OECD
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series3 | 3.612 | 3.746 | 3.972 | 3.8381 | 3.8276 | 3.7751 | 3.6291 | 3.3477 | 3.2926 | 3.2384 | 3.1916 | 3.1343 | 3.093 | 3.0563 | 3.0197 | 2.9867 | 2.9558 | 2.9273 | 2.8925 | 2.8591 | 2.8282 | 2.7998 | 2.7704 | 2.7433 | 2.7164 | 2.6927 | 2.6703 | 2.6458 | 2.6212 | 2.6004 | 2.5771 | 2.5587 | 2.5388 | 2.5237 | 2.5094 | 2.4973 | 2.4778 | 2.4597 | 2.4432 | 2.4263 | 2.4115
series4 | 0.32156 | 0.41233 | 0.4886 | 0.69762 | 0.74485 | 0.82902 | 1.1443 | 1.1535 | 1.1627 | 1.172 | 1.1814 | 1.1908 | 1.2003 | 1.2099 | 1.2196 | 1.2294 | 1.2392 | 1.2491 | 1.2591 | 1.2692 | 1.2793 | 1.2896 | 1.2999 | 1.3103 | 1.3208 | 1.3313 | 1.342 | 1.3527 | 1.3636 | 1.3745 | 1.3855 | 1.3965 | 1.4077 | 1.419 | 1.4303 | 1.4418 | 1.4533 | 1.4649 | 1.4766 | 1.4885 | 1.5004
series2 | 4.6432 | 4.6823 | 4.81 | 4.9795 | 5.156 | 5.3395 | 5.3745 | 5.5101 | 5.3895 | 5.3243 | 5.2922 | 5.2388 | 5.2156 | 5.2024 | 5.196 | 5.1697 | 5.1788 | 5.1849 | 5.1933 | 5.1985 | 5.2074 | 5.2129 | 5.2101 | 5.2164 | 5.2211 | 5.228 | 5.2307 | 5.2344 | 5.2337 | 5.246 | 5.2491 | 5.2537 | 5.249 | 5.2535 | 5.2512 | 5.2512 | 5.2463 | 5.2532 | 5.2524 | 5.2554 | 5.2561
series1 | 8.1735 | 8.8834 | 8.5199 | 8.5779 | 8.8624 | 8.6704 | 8.9972 | 9.1237 | 9.3522 | 9.4937 | 9.6544 | 9.7702 | 9.9088 | 10.0591 | 10.2249 | 10.3762 | 10.5839 | 10.735 | 10.9068 | 11.0916 | 11.2717 | 11.4126 | 11.5714 | 11.7334 | 11.9024 | 12.043 | 12.2302 | 12.41 | 12.6057 | 12.7433 | 12.9436 | 13.1001 | 13.2762 | 13.4672 | 13.6446 | 13.8039 | 13.9789 | 14.1465 | 14.3232 | 14.465 | 14.6459
series0 | 7.1294 | 7.4965 | 8.0176 | 8.638 | 9.1073 | 9.7707 | 10.5156 | 11.7638 | 12.3131 | 12.8319 | 13.3438 | 13.868 | 14.4031 | 14.9652 | 15.5691 | 16.2043 | 16.9237 | 17.6724 | 18.4395 | 19.2391 | 20.0729 | 20.8139 | 21.5827 | 22.3696 | 23.1799 | 24.0173 | 24.769 | 25.5362 | 26.3037 | 27.0919 | 27.8968 | 28.8668 | 29.8722 | 30.906 | 31.9829 | 33.0783 | 33.9367 | 34.7969 | 35.6582 | 36.5098 | 37.4014
electricity
natural gas
liquids
renewables
coal
non-OECD

## Slide 58: —led by electricity and natural gas consumption growth
Electricity remains the main source of marketed energy consumption in the residential sector, and its use grows by 2.5% per year globally as rising population and standards of living in non-OECD countries increase the demand for appliances and personal equipment.
Residential natural gas consumption increases by 0.7% per year during the projection period, influenced by increasing use of natural gas for heating.
Coal consumption, used primarily for space heating, water heating, and cooking, continues to decline in the residential sector.

## Slide 59: In the Reference case, non-OECD countries account for much of the increase in commercial sector energy consumption—
Non-OECD commercial energy consumption
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe and Eurasia | 2.3186 | 2.3275 | 2.589 | 2.9082 | 3.3389
Americas | 0.96396 | 1.1879 | 1.406 | 1.6482 | 1.9262
Africa | 0.4528 | 0.58713 | 0.74804 | 0.95687 | 1.1917
Middle East | 1.0277 | 1.4582 | 1.8448 | 2.3456 | 2.6802
Other Asia | 1.265 | 1.7466 | 2.2577 | 2.7895 | 3.4082
India | 0.47947 | 0.98111 | 1.6062 | 2.3415 | 3.2027
China | 2.3331 | 3.7969 | 4.6867 | 5.6535 | 6.6546
China
India
other Asia
Middle East
Africa
Americas
Europe
and Eurasia
OECD commercial energy consumption
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe | 6.7476 | 7.0674 | 7.7812 | 8.3704 | 9.0652
Americas | 9.7281 | 10.5239 | 10.866 | 11.5232 | 12.5726
Asia | 3.4677 | 3.6238 | 3.9584 | 4.2772 | 4.6741
Asia
Americas
Europe
history projections

## Slide 60: —led by increasing demand in non-OECD Asia
The need for commercial services increases as populations and economies grow, which affects energy consumption for appliances, lighting, and other equipment in buildings. Non-OECD commercial sector energy consumption remains lower than in the OECD throughout the projection period, but it increases at about three times the rate of OECD commercial energy consumption.
Non-OECD Asia (China, India, and other non-OECD Asian countries) remains the fastest-growing region in the commercial sector. About 66% of the projected increase in non-OECD commercial energy consumption occurs in non-OECD Asia.
Commercial energy consumption increases the most in China (in absolute terms), although India experiences the fastest relative growth in commercial energy consumption from 2018 to 2050.
Africa has the second-highest projected rate of commercial energy consumption growth among the non-OECD regions, averaging 2.4% per year through the projection period.

## Slide 61: World commercial energy consumption continues to increase—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series4 | 0.11821 | 0.12355 | 0.11926 | 0.13109 | 0.13855 | 0.14274 | 0.15803 | 0.16746 | 0.16767 | 0.16788 | 0.16809 | 0.16831 | 0.16853 | 0.16875 | 0.16897 | 0.16919 | 0.16942 | 0.16964 | 0.16987 | 0.1701 | 0.17033 | 0.17057 | 0.1708 | 0.17104 | 0.17128 | 0.17152 | 0.17176 | 0.17201 | 0.17226 | 0.17251 | 0.17276 | 0.17301 | 0.17327 | 0.17352 | 0.17378 | 0.17404 | 0.17431 | 0.17457 | 0.17484 | 0.17511 | 0.17538
series3 | 0.3579 | 0.32297 | 0.32584 | 0.27176 | 0.27145 | 0.27179 | 0.25303 | 0.245 | 0.23664 | 0.23146 | 0.2275 | 0.22614 | 0.22478 | 0.22347 | 0.22216 | 0.22123 | 0.21977 | 0.21866 | 0.21753 | 0.21658 | 0.21517 | 0.21381 | 0.21254 | 0.21129 | 0.21009 | 0.20888 | 0.20773 | 0.20661 | 0.20555 | 0.20454 | 0.2036 | 0.20266 | 0.2018 | 0.20096 | 0.20019 | 0.19946 | 0.19875 | 0.19808 | 0.19747 | 0.1969 | 0.19639
series2 | 2.3886 | 2.2924 | 2.1874 | 2.2164 | 2.1083 | 2.4033 | 2.3869 | 2.4354 | 2.4232 | 2.4381 | 2.4064 | 2.3635 | 2.3423 | 2.3306 | 2.3228 | 2.3114 | 2.3082 | 2.2996 | 2.302 | 2.2997 | 2.3074 | 2.31 | 2.3107 | 2.3063 | 2.3105 | 2.3115 | 2.3132 | 2.3138 | 2.3108 | 2.318 | 2.3192 | 2.3238 | 2.3215 | 2.3307 | 2.3298 | 2.3353 | 2.3312 | 2.3398 | 2.3465 | 2.3476 | 2.3523
series1 | 6.7517 | 6.5757 | 6.3963 | 6.9878 | 6.9071 | 6.7737 | 6.7139 | 6.8869 | 7.0421 | 7.1069 | 7.0643 | 7.069 | 7.0649 | 7.0632 | 7.0601 | 7.0564 | 7.0716 | 7.0944 | 7.1142 | 7.1424 | 7.163 | 7.1831 | 7.2067 | 7.231 | 7.2615 | 7.293 | 7.324 | 7.3569 | 7.3916 | 7.4262 | 7.464 | 7.5087 | 7.5471 | 7.5861 | 7.6286 | 7.6697 | 7.7139 | 7.7551 | 7.8 | 7.8344 | 7.8848
series0 | 10.327 | 10.3292 | 10.284 | 10.4369 | 10.4901 | 10.7199 | 10.7496 | 10.8739 | 11.1094 | 11.175 | 11.3488 | 11.5002 | 11.6481 | 11.781 | 11.9125 | 12.0494 | 12.1822 | 12.3211 | 12.464 | 12.6137 | 12.7496 | 12.8686 | 12.981 | 13.0976 | 13.221 | 13.3502 | 13.4786 | 13.6074 | 13.7381 | 13.8755 | 14.0113 | 14.149 | 14.2951 | 14.4448 | 14.5984 | 14.7574 | 14.9357 | 15.1194 | 15.3037 | 15.4954 | 15.703
Commercial sector energy consumption by fuel
quadrillion British thermal units
history projections
OECD
non-OECD
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
series4 | 0.036564 | 0.047263 | 0.054471 | 0.077772 | 0.083185 | 0.089398 | 0.12797 | 0.12899 | 0.13002 | 0.13106 | 0.13211 | 0.13317 | 0.13423 | 0.13531 | 0.13639 | 0.13748 | 0.13858 | 0.13969 | 0.14081 | 0.14193 | 0.14307 | 0.14421 | 0.14537 | 0.14653 | 0.1477 | 0.14889 | 0.15008 | 0.15128 | 0.15249 | 0.15371 | 0.15494 | 0.15618 | 0.15743 | 0.15869 | 0.15995 | 0.16123 | 0.16252 | 0.16382 | 0.16513 | 0.16646 | 0.16779
series3 | 1.2591 | 1.3689 | 1.4948 | 1.5419 | 1.4507 | 1.4761 | 1.4328 | 1.3864 | 1.3673 | 1.3553 | 1.3487 | 1.3409 | 1.3356 | 1.3322 | 1.329 | 1.3272 | 1.3273 | 1.3282 | 1.3272 | 1.3266 | 1.3267 | 1.3293 | 1.3321 | 1.3355 | 1.3395 | 1.3443 | 1.3487 | 1.3523 | 1.356 | 1.3608 | 1.3656 | 1.3708 | 1.376 | 1.3821 | 1.3887 | 1.3959 | 1.4027 | 1.4098 | 1.4176 | 1.4258 | 1.4343
series2 | 1.3883 | 1.4111 | 1.4106 | 1.4721 | 1.4155 | 1.4854 | 1.4799 | 1.5389 | 1.5137 | 1.5124 | 1.5185 | 1.5053 | 1.506 | 1.5146 | 1.5287 | 1.5347 | 1.5506 | 1.5649 | 1.5843 | 1.601 | 1.6229 | 1.6405 | 1.6568 | 1.6712 | 1.6898 | 1.7081 | 1.7266 | 1.7431 | 1.7575 | 1.7799 | 1.7982 | 1.8178 | 1.8331 | 1.8565 | 1.8718 | 1.8915 | 1.9055 | 1.9274 | 1.9466 | 1.9642 | 1.9837
series1 | 1.7087 | 1.8289 | 1.8646 | 1.9273 | 2.0092 | 1.974 | 2.0732 | 2.0674 | 2.117 | 2.1507 | 2.1922 | 2.2102 | 2.2372 | 2.2642 | 2.2959 | 2.327 | 2.3714 | 2.4049 | 2.4472 | 2.4887 | 2.5302 | 2.5663 | 2.603 | 2.6442 | 2.6814 | 2.7173 | 2.7607 | 2.796 | 2.8405 | 2.8695 | 2.9145 | 2.9448 | 2.9803 | 3.022 | 3.0574 | 3.088 | 3.1226 | 3.1558 | 3.1924 | 3.2202 | 3.2542
series0 | 4.448 | 4.6452 | 4.96 | 5.2013 | 5.3761 | 5.7777 | 6.0841 | 6.2849 | 6.5079 | 6.6838 | 6.8938 | 7.1254 | 7.3596 | 7.5911 | 7.8316 | 8.0791 | 8.3532 | 8.6319 | 8.9197 | 9.2141 | 9.5156 | 9.8047 | 10.086 | 10.3744 | 10.6663 | 10.9613 | 11.2517 | 11.5392 | 11.8268 | 12.1157 | 12.4102 | 12.7251 | 13.0474 | 13.3746 | 13.7075 | 14.048 | 14.3478 | 14.6496 | 14.9534 | 15.2579 | 15.5624
electricity
natural gas
liquids
coal
renewables

## Slide 62: —led by a faster growth rate in non-OECD electricity use
From 2018 to 2050, OECD countries use more energy in the commercial sector than in non-OECD countries.
Electricity and natural gas remain the most prominent energy sources in the commercial sector.
Electricity is the fastest-growing source of energy use in the commercial sector. Commercial electricity use in non-OECD countries increases by an average of 2.8% per year from 2018 to 2050, compared with 1.1% per year in OECD countries.
Commercial natural gas consumption in non-OECD countries grows by 1.4% per year from 2018 to 2050, which is about four times the rate of the increase in OECD commercial sector.

## Slide 63: China switches from district heat to combined heat and power (CHP) for heating—
Chart: 
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
district heat | 1.7776 | 1.7095 | 1.6724 | 1.6183 | 1.5654 | 1.5172 | 1.4689 | 1.4264 | 1.3738 | 1.3315 | 1.2875 | 1.2493 | 1.2119 | 1.1703 | 1.1216 | 1.0792 | 1.0315 | 0.99208 | 0.94937 | 0.90566 | 0.8575 | 0.81846 | 0.76278 | 0.72896 | 0.68357 | 0.65304 | 0.62034 | 0.59076 | 0.5225 | 0.45387 | 0.38344 | 0.30354 | 0.22717
combined heat and power | 2.2658 | 2.333 | 2.4003 | 2.4724 | 2.5446 | 2.6168 | 2.689 | 2.7611 | 2.8375 | 2.9138 | 2.9901 | 3.0665 | 3.1428 | 3.2227 | 3.3026 | 3.3825 | 3.4624 | 3.5423 | 3.6253 | 3.7083 | 3.7913 | 3.8743 | 3.9573 | 4.043 | 4.1287 | 4.2144 | 4.3001 | 4.3858 | 4.5008 | 4.6158 | 4.7308 | 4.8458 | 4.9608
Chart: 
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
district heat | 0.58367 | 0.54415 | 0.51227 | 0.47755 | 0.45942 | 0.4424 | 0.42565 | 0.4103 | 0.39284 | 0.3777 | 0.36129 | 0.34586 | 0.33087 | 0.31477 | 0.29714 | 0.28137 | 0.26451 | 0.25002 | 0.23479 | 0.21953 | 0.2034 | 0.18983 | 0.17218 | 0.16042 | 0.14581 | 0.13548 | 0.12479 | 0.11507 | 0.094776 | 0.074789 | 0.054706 | 0.032451 | 0.011512
other | 2.9428 | 2.91 | 2.8786 | 2.8476 | 2.8177 | 2.7884 | 2.7599 | 2.7336 | 2.7081 | 2.6835 | 2.6593 | 2.6357 | 2.6146 | 2.5944 | 2.5751 | 2.5564 | 2.5387 | 2.5218 | 2.5057 | 2.4907 | 2.4767 | 2.464 | 2.4522 | 2.4414 | 2.4316 | 2.4231 | 2.4157 | 2.4095 | 2.4044 | 2.4006 | 2.398 | 2.3967 | 2.3967
Heat generation by source in China
quadrillion British thermal units
combined heat
and power
district heat
(heat only
boilers)
Coal consumption by buildings in China
quadrillion British thermal units
other uses
district heat

## Slide 64: —which results in a significant decline in coal consumption in its buildings
Coal is the main fuel for heating in China’s building sector in 2018; however, policies encourage a switch to clean heating sources. About two-thirds of northern China’s floorspace relies on district heat for space heating. Recent policies target a transition away from small-scale, coal-fired boilers for heating in this region, contributing to a larger trend of declining coal consumption in China.
China’s 2017–21 clean winter heating plan calls for 70% of northern China’s needs to be met through natural gas, electricity, renewables, CHP, or more efficient coal boilers.
Along with electricity-sector growth and fuel price shifts, this policy drives a transition from coal-fired heat-only boilers to CHP. The remaining district heat boilers are more efficient, and natural gas assumes a larger share of heat generation.
Although district heat accounts for only 17% of building sector coal consumption in 2018, it accounts for more than 50% of the overall decline in buildings’ coal consumption from 2018 to 2050.

## Slide 65: Transportation

## Slide 67: Transportation energy consumption continues to grow in non-OECD countries—
Transportation energy consumption
quadrillion British thermal units
Chart: 
history projections

## Slide 68: —but remains relatively flat in OECD countries
In countries that are not part of the Organization of Economic Cooperation and Development (OECD), transportation energy demand increases 77% from 2018 to 2050 in the Reference case. A few countries, including China and India, have particularly large populations, and their energy consumption for both personal travel and freight movement grows much more rapidly than in many OECD countries.
In OECD countries, improvements in vehicle fuel efficiency outpace projected increases in travel demand, and as a result, total projected transportation energy use for OECD countries declines by 1% from 2018 to 2050.
Transportation energy consumption in non-OECD countries has exceeded that in OECD countries since 2017, and by 2050, non-OECD countries will account for almost 65% of the world’s transportation-related energy use.

## Slide 69: Energy use for passenger travel accounts for most of the growth in transportation energy consumption—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
f | 18.6909 | 18.5567 | 17.828 | 17.8325 | 18.0675 | 18.1642 | 18.5804 | 19.2883 | 19.3746 | 19.4872 | 19.3221 | 19.2819 | 19.3236 | 19.3115 | 19.3082 | 19.3118 | 19.2772 | 19.2173 | 19.1769 | 19.14 | 19.0679 | 19.004 | 18.9501 | 18.89 | 18.8855 | 18.898 | 18.9466 | 18.9788 | 19.0271 | 19.0635 | 19.0978 | 19.2049 | 19.2709 | 19.3865 | 19.4988 | 19.6031 | 19.6625 | 19.7756 | 19.8783 | 19.9955 | 20.1425
residential | 37.0527 | 36.7718 | 36.5315 | 36.8573 | 37.2992 | 37.9912 | 38.983 | 39.4479 | 39.5634 | 39.6739 | 39.6781 | 39.5392 | 39.2877 | 38.9385 | 38.5393 | 38.1102 | 37.7456 | 37.3951 | 37.0672 | 36.738 | 36.4317 | 36.1584 | 35.9239 | 35.7347 | 35.5929 | 35.4858 | 35.4344 | 35.4328 | 35.4739 | 35.5484 | 35.6714 | 35.8214 | 36.012 | 36.2362 | 36.4806 | 36.7441 | 37.0269 | 37.3231 | 37.6242 | 37.9353 | 38.2599
Transportation sector energy consumption
quadrillion British thermal units
history projections
OECD
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
f | 22.8007 | 23.8554 | 24.8272 | 24.8142 | 25.3294 | 25.6719 | 26.5263 | 27.3524 | 27.8485 | 28.1638 | 28.6531 | 29.1303 | 29.5988 | 30.0129 | 30.416 | 30.8124 | 31.203 | 31.6086 | 31.9614 | 32.3502 | 32.7419 | 33.0546 | 33.2766 | 33.5274 | 33.8398 | 34.271 | 34.6463 | 35.1035 | 35.5405 | 36.0503 | 36.5016 | 37.1566 | 37.7304 | 38.3988 | 39.0727 | 39.7698 | 40.3791 | 41.0411 | 41.7185 | 42.3746 | 43.1063
p | 22.3549 | 23.4511 | 24.7032 | 26.5826 | 27.9673 | 29.8479 | 31.5528 | 32.3174 | 33.2233 | 34.2045 | 35.1911 | 36.279 | 37.4262 | 38.5977 | 39.8115 | 40.9869 | 42.0884 | 43.1271 | 44.11 | 45.0294 | 45.9125 | 46.792 | 47.6734 | 48.5644 | 49.4764 | 50.4049 | 51.3457 | 52.3011 | 53.2846 | 54.2593 | 55.177 | 56.0994 | 57.0511 | 58.0288 | 59.0234 | 60.014 | 60.9875 | 61.9726 | 62.9544 | 63.9398 | 64.9404
non-OECD
passenger
freight

## Slide 70: —and nearly doubles from 2018 to 2050 in non-OECD countries
Increases in economic activity, population, and disposable income lead to greater freight movement and passenger travel in non-OECD countries.
In non-OECD countries, gross domestic product (GDP) more than triples from 2018 to 2050, far outpacing population growth, which increases by about 30% during those years. The resulting increase in relative wealth leads to increased travel and greater consumption of goods.
In OECD countries, with slower economic and population growth, energy used for passenger travel declines until the 2030s because the impact of efficiency standards are greater than the impact of increases in travel.

## Slide 71: Light-duty vehicle consumption grows rapidly in non-OECD countries—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Bus | 0.88554 | 0.91527 | 0.9114 | 0.92022 | 0.93081 | 0.945 | 0.95299 | 1.0068 | 1.0139 | 1.0216 | 1.0283 | 1.035 | 1.0424 | 1.0493 | 1.0563 | 1.0631 | 1.0701 | 1.077 | 1.0838 | 1.0927 | 1.1007 | 1.1076 | 1.1143 | 1.1189 | 1.1249 | 1.1319 | 1.1389 | 1.1453 | 1.1511 | 1.1563 | 1.1612 | 1.1658 | 1.17 | 1.1742 | 1.1781 | 1.1818 | 1.1853 | 1.1886 | 1.1918 | 1.1951 | 1.1984
Rail | 0.2721 | 0.27535 | 0.27523 | 0.2789 | 0.28155 | 0.28803 | 0.29143 | 0.31633 | 0.31786 | 0.32091 | 0.32377 | 0.32578 | 0.3277 | 0.32925 | 0.33103 | 0.33271 | 0.33452 | 0.33627 | 0.33797 | 0.33982 | 0.34153 | 0.34284 | 0.34419 | 0.34533 | 0.34645 | 0.34757 | 0.34864 | 0.34957 | 0.35046 | 0.35134 | 0.35204 | 0.3529 | 0.35364 | 0.35444 | 0.3552 | 0.35584 | 0.35643 | 0.35698 | 0.35739 | 0.35785 | 0.3583
2-3 Wheeler | 0.24585 | 0.24621 | 0.24552 | 0.2445 | 0.24515 | 0.24439 | 0.24443 | 0.24306 | 0.24272 | 0.24191 | 0.24136 | 0.2399 | 0.23843 | 0.23713 | 0.236 | 0.23492 | 0.23396 | 0.23302 | 0.23208 | 0.23115 | 0.23036 | 0.22973 | 0.22918 | 0.22864 | 0.22808 | 0.22751 | 0.22705 | 0.22673 | 0.22653 | 0.22633 | 0.22607 | 0.22573 | 0.22537 | 0.22501 | 0.22463 | 0.22422 | 0.2238 | 0.22337 | 0.22293 | 0.22247 | 0.22196
Air | 5.9111 | 6.0543 | 6 | 6.1067 | 6.2043 | 6.4644 | 6.7464 | 6.9292 | 6.9839 | 7.1263 | 7.2847 | 7.4434 | 7.5987 | 7.7507 | 7.9096 | 8.081 | 8.2541 | 8.4257 | 8.607 | 8.7843 | 8.965 | 9.1383 | 9.3073 | 9.4822 | 9.6647 | 9.8498 | 10.0366 | 10.2277 | 10.4224 | 10.6194 | 10.8337 | 11.0464 | 11.2686 | 11.4961 | 11.7317 | 11.9761 | 12.2219 | 12.4748 | 12.7313 | 12.995 | 13.2723
LDV | 29.7381 | 29.2807 | 29.0994 | 29.3071 | 29.6374 | 30.0494 | 30.7477 | 30.9526 | 31.005 | 30.9631 | 30.8 | 30.4951 | 30.0804 | 29.5721 | 29.0063 | 28.3985 | 27.8529 | 27.3231 | 26.8064 | 26.29 | 25.7942 | 25.3399 | 24.929 | 24.5596 | 24.2288 | 23.9291 | 23.6831 | 23.4835 | 23.3234 | 23.1951 | 23.0983 | 23.0305 | 22.9944 | 22.9865 | 22.991 | 23.0062 | 23.0395 | 23.0793 | 23.1208 | 23.1649 | 23.209
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Bus | 2.8663 | 2.9288 | 3.0092 | 3.1033 | 3.1959 | 3.3141 | 3.3832 | 3.5188 | 3.6058 | 3.7298 | 3.8678 | 3.9966 | 4.1219 | 4.2426 | 4.3613 | 4.47 | 4.5723 | 4.6746 | 4.7732 | 4.8671 | 4.9555 | 5.0369 | 5.1171 | 5.1939 | 5.2693 | 5.3436 | 5.4175 | 5.4997 | 5.5979 | 5.697 | 5.7748 | 5.839 | 5.9029 | 5.974 | 6.0552 | 6.1333 | 6.205 | 6.2778 | 6.349 | 6.4153 | 6.4808
Rail | 0.49496 | 0.52452 | 0.5751 | 0.63556 | 0.70691 | 0.82877 | 0.92424 | 0.9957 | 1.0651 | 1.1675 | 1.2693 | 1.353 | 1.4304 | 1.5092 | 1.5885 | 1.6611 | 1.7296 | 1.7957 | 1.8538 | 1.9054 | 1.9503 | 1.9873 | 2.0204 | 2.0471 | 2.0698 | 2.0891 | 2.106 | 2.1193 | 2.1326 | 2.1461 | 2.155 | 2.1644 | 2.1782 | 2.2019 | 2.2243 | 2.2405 | 2.2437 | 2.2462 | 2.2465 | 2.247 | 2.2478
2-3 Wheeler | 1.2386 | 1.337 | 1.4108 | 1.4853 | 1.5408 | 1.5856 | 1.6267 | 1.675 | 1.7158 | 1.7422 | 1.7873 | 1.8363 | 1.8801 | 1.9154 | 1.9477 | 1.977 | 2.0033 | 2.0274 | 2.0496 | 2.0699 | 2.0885 | 2.1049 | 2.1198 | 2.1338 | 2.1467 | 2.1585 | 2.1691 | 2.1788 | 2.1875 | 2.1954 | 2.2026 | 2.2089 | 2.2146 | 2.2196 | 2.2241 | 2.2281 | 2.2311 | 2.2336 | 2.2356 | 2.2373 | 2.2386
Air | 4.1788 | 4.355 | 4.5212 | 4.7052 | 4.8752 | 5.1368 | 5.4177 | 5.2647 | 5.3475 | 5.5346 | 5.7472 | 5.9833 | 6.2197 | 6.4643 | 6.7146 | 6.9764 | 7.2367 | 7.5024 | 7.7746 | 8.0526 | 8.3417 | 8.6377 | 8.9334 | 9.2418 | 9.5592 | 9.8832 | 10.2153 | 10.55 | 10.8935 | 11.2432 | 11.5756 | 11.9306 | 12.3078 | 12.6921 | 13.0936 | 13.5047 | 13.9192 | 14.3485 | 14.7841 | 15.2322 | 15.7014
LDV | 13.5762 | 14.3057 | 15.1868 | 16.6532 | 17.6484 | 18.9826 | 20.201 | 20.8631 | 21.4891 | 22.0304 | 22.5196 | 23.1098 | 23.7741 | 24.4663 | 25.1994 | 25.9025 | 26.5465 | 27.127 | 27.6588 | 28.1344 | 28.5765 | 29.0253 | 29.4828 | 29.9479 | 30.4313 | 30.9304 | 31.4378 | 31.9534 | 32.473 | 32.9775 | 33.4691 | 33.9565 | 34.4476 | 34.9412 | 35.4261 | 35.9075 | 36.3884 | 36.8665 | 37.3392 | 37.808 | 38.2718
light-duty
vehicles
air
two or
three
wheel
vehicles
rail
buses
Passenger transportation energy consumption
quadrillion British thermal units
history projections

## Slide 72: —while air travel becomes an increasingly larger share of transportation energy consumption in OECD countries
In OECD countries, many of which show both slower projected economic growth and stricter fuel economy standards than non-OECD countries, energy consumption for passenger travel decreases by 3%, or more than 1 quadrillion British thermal units (Btu), from 2018 to 2050.
Energy used in air travel nearly doubles in OECD countries, but it is offset by energy consumption from light-duty vehicles, decreasing by nearly 8 quadrillion Btu.
In non-OECD countries, increased travel demand activity across all passenger modes of travel outpaces improvements in fuel efficiency standards.
The largest change in passenger transportation occurs in non-OECD countries in light-duty vehicles. From 2018 to 2050, related energy consumption increases by 17 quadrillion Btu.

## Slide 73: Freight transportation energy consumption remains relatively constant in OECD countries—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Rail | 0.96507 | 1.058 | 1.0321 | 1.0398 | 1.0968 | 1.0922 | 1.0281 | 1.1465 | 1.1494 | 1.1602 | 1.1558 | 1.1622 | 1.1645 | 1.1715 | 1.1824 | 1.1924 | 1.1971 | 1.2017 | 1.206 | 1.2215 | 1.2299 | 1.2331 | 1.2341 | 1.242 | 1.2466 | 1.2565 | 1.2634 | 1.2698 | 1.2739 | 1.2805 | 1.2875 | 1.2904 | 1.2918 | 1.2931 | 1.2946 | 1.2967 | 1.2968 | 1.2988 | 1.2996 | 1.3028 | 1.3095
Marine (domestic) | 0.38515 | 0.39431 | 0.37486 | 0.39346 | 0.4004 | 0.37902 | 0.36485 | 0.3582 | 0.35382 | 0.35374 | 0.353 | 0.353 | 0.35339 | 0.35346 | 0.35337 | 0.35307 | 0.35288 | 0.35255 | 0.35217 | 0.35219 | 0.35197 | 0.35224 | 0.35269 | 0.35299 | 0.35362 | 0.35417 | 0.3545 | 0.35511 | 0.35468 | 0.35455 | 0.35469 | 0.3548 | 0.3548 | 0.35472 | 0.35469 | 0.35461 | 0.35445 | 0.35439 | 0.35393 | 0.35339 | 0.35274
Marine (international) | 3.6855 | 3.527 | 3.2465 | 3.0853 | 2.9475 | 3.0004 | 3.4526 | 3.5544 | 3.5472 | 3.6786 | 3.529 | 3.5685 | 3.6578 | 3.6779 | 3.7097 | 3.7304 | 3.7519 | 3.7789 | 3.8008 | 3.8269 | 3.8366 | 3.8465 | 3.8628 | 3.8717 | 3.8832 | 3.8841 | 3.9012 | 3.9071 | 3.9171 | 3.9372 | 3.9485 | 3.9726 | 3.9866 | 4.016 | 4.0288 | 4.0397 | 4.045 | 4.0536 | 4.0527 | 4.0559 | 4.0659
Natural Gas Pipeline | 0.86813 | 0.87895 | 0.86743 | 0.8547 | 0.95646 | 0.93721 | 0.94065 | 0.9873 | 1.0153 | 0.969 | 0.95896 | 0.92797 | 0.91688 | 0.91535 | 0.92291 | 0.93754 | 0.93622 | 0.94225 | 0.94879 | 0.95848 | 0.94644 | 0.94788 | 0.9591 | 0.96231 | 0.97515 | 0.98139 | 0.98865 | 0.98958 | 0.9988 | 0.97313 | 0.95142 | 0.95903 | 0.94366 | 0.93806 | 0.94579 | 0.92727 | 0.88866 | 0.86813 | 0.85514 | 0.8528 | 0.86222
Lt Heavy Truck | 4.1034 | 3.9972 | 3.7456 | 3.6934 | 3.6527 | 3.6286 | 3.5842 | 3.6742 | 3.6958 | 3.6688 | 3.656 | 3.6294 | 3.5983 | 3.5701 | 3.5397 | 3.5161 | 3.4878 | 3.453 | 3.4303 | 3.4082 | 3.393 | 3.3804 | 3.3652 | 3.3524 | 3.35 | 3.3528 | 3.3624 | 3.3676 | 3.374 | 3.3803 | 3.3953 | 3.414 | 3.4278 | 3.4481 | 3.4648 | 3.4883 | 3.5077 | 3.5359 | 3.5597 | 3.5862 | 3.61
Med Heavy Truck | 2.4055 | 2.3978 | 2.2813 | 2.3301 | 2.3771 | 2.3952 | 2.384 | 2.4145 | 2.4056 | 2.4028 | 2.405 | 2.3949 | 2.3889 | 2.3846 | 2.3772 | 2.3704 | 2.3618 | 2.3479 | 2.3382 | 2.328 | 2.3137 | 2.3022 | 2.2862 | 2.2693 | 2.2631 | 2.2617 | 2.2667 | 2.2714 | 2.2812 | 2.2905 | 2.3042 | 2.3202 | 2.3399 | 2.3667 | 2.3932 | 2.4227 | 2.4511 | 2.4855 | 2.5209 | 2.556 | 2.5915
Hvy Heavy Truck | 6.2781 | 6.3035 | 6.2802 | 6.4357 | 6.6365 | 6.7316 | 6.8259 | 7.1532 | 7.2074 | 7.254 | 7.2643 | 7.2458 | 7.2437 | 7.2386 | 7.2231 | 7.212 | 7.1894 | 7.141 | 7.1006 | 7.0448 | 6.9963 | 6.9417 | 6.89 | 6.8393 | 6.8138 | 6.8073 | 6.8097 | 6.8182 | 6.8274 | 6.8473 | 6.8562 | 6.8939 | 6.9263 | 6.9698 | 7.017 | 7.0738 | 7.1189 | 7.1793 | 7.2363 | 7.2885 | 7.3506
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Rail | 1.405 | 1.4244 | 1.4077 | 1.4024 | 1.3515 | 1.2277 | 1.2576 | 1.2815 | 1.3121 | 1.3332 | 1.341 | 1.3517 | 1.3645 | 1.3756 | 1.3874 | 1.4012 | 1.4146 | 1.4333 | 1.4476 | 1.4629 | 1.4753 | 1.489 | 1.4991 | 1.5101 | 1.5169 | 1.5301 | 1.5402 | 1.5473 | 1.5556 | 1.5616 | 1.5706 | 1.5759 | 1.5817 | 1.5874 | 1.5927 | 1.598 | 1.6027 | 1.6057 | 1.6079 | 1.6114 | 1.6164
Marine (domestic) | 0.43799 | 0.47892 | 0.50856 | 0.53816 | 0.59776 | 0.6073 | 0.61728 | 0.63277 | 0.65085 | 0.66588 | 0.68164 | 0.69424 | 0.70901 | 0.72278 | 0.73609 | 0.74833 | 0.75995 | 0.7709 | 0.77755 | 0.78732 | 0.79723 | 0.80647 | 0.81453 | 0.82243 | 0.82989 | 0.83714 | 0.84423 | 0.85012 | 0.85544 | 0.86028 | 0.86505 | 0.8678 | 0.87083 | 0.87378 | 0.87683 | 0.8797 | 0.88198 | 0.88405 | 0.88594 | 0.88733 | 0.88826
Marine (international) | 3.6855 | 3.527 | 3.2465 | 3.0853 | 2.9475 | 3.0004 | 3.4526 | 3.5544 | 3.5472 | 3.6786 | 3.529 | 3.5685 | 3.6578 | 3.6779 | 3.7097 | 3.7304 | 3.7519 | 3.7789 | 3.8008 | 3.8269 | 3.8366 | 3.8465 | 3.8628 | 3.8717 | 3.8832 | 3.8841 | 3.9012 | 3.9071 | 3.9171 | 3.9372 | 3.9485 | 3.9726 | 3.9866 | 4.016 | 4.0288 | 4.0397 | 4.045 | 4.0536 | 4.0527 | 4.0559 | 4.0659
Natural Gas Pipeline | 1.8114 | 1.8241 | 1.5783 | 1.5703 | 1.5615 | 1.5651 | 1.6508 | 2.0346 | 2.0181 | 2.0508 | 2.0582 | 2.06 | 2.0501 | 2.057 | 2.0496 | 2.057 | 2.0792 | 2.1533 | 2.1675 | 2.2548 | 2.3413 | 2.4081 | 2.3697 | 2.391 | 2.3974 | 2.4755 | 2.4385 | 2.5133 | 2.5416 | 2.5883 | 2.5679 | 2.6369 | 2.6437 | 2.6617 | 2.7017 | 2.7428 | 2.757 | 2.7414 | 2.7717 | 2.7705 | 2.7888
Lt Heavy Truck | 2.018 | 2.1624 | 2.3069 | 2.2731 | 2.2871 | 2.2892 | 2.3346 | 2.3427 | 2.3321 | 2.2993 | 2.2982 | 2.3154 | 2.3316 | 2.3463 | 2.3551 | 2.3619 | 2.3642 | 2.3615 | 2.3675 | 2.373 | 2.3835 | 2.3908 | 2.3995 | 2.4074 | 2.4218 | 2.4393 | 2.4621 | 2.4835 | 2.5056 | 2.5306 | 2.5591 | 2.5959 | 2.6296 | 2.67 | 2.7072 | 2.75 | 2.7871 | 2.8321 | 2.8749 | 2.9192 | 2.9658
Med Heavy Truck | 4.9812 | 5.0767 | 5.2969 | 5.1436 | 5.1185 | 5.1223 | 5.2222 | 5.2825 | 5.2917 | 5.2565 | 5.2954 | 5.3452 | 5.3964 | 5.441 | 5.4709 | 5.4969 | 5.5077 | 5.5007 | 5.526 | 5.5559 | 5.5874 | 5.6036 | 5.6199 | 5.6299 | 5.6593 | 5.6979 | 5.7502 | 5.8 | 5.8539 | 5.9176 | 5.9849 | 6.0751 | 6.1628 | 6.2697 | 6.3707 | 6.4834 | 6.5833 | 6.7016 | 6.8175 | 6.9342 | 7.0605
Hvy Heavy Truck | 6.9155 | 7.6398 | 8.5547 | 8.6566 | 9.0025 | 9.2133 | 9.396 | 9.7965 | 10.1802 | 10.4739 | 10.8275 | 11.1288 | 11.4376 | 11.7405 | 12.0276 | 12.3225 | 12.5942 | 12.8362 | 13.0681 | 13.253 | 13.4547 | 13.6296 | 13.8088 | 13.9813 | 14.2008 | 14.4431 | 14.7225 | 15.0002 | 15.2951 | 15.6111 | 15.9467 | 16.3406 | 16.7414 | 17.1837 | 17.6273 | 18.0955 | 18.5276 | 19.0171 | 19.5046 | 19.9911 | 20.5031
heavy
heavy truck
medium
heavy truck
light
heavy truck
pipeline
international
marine
domestic
marine
rail
Freight transportation energy consumption
quadrillion British thermal units
history projections

## Slide 74: —while heavy trucks and international marine transportation continue to grow in non-OECD countries
In OECD countries, energy used to haul freight remains around 20 quadrillion Btu during the entire projection period, with heavy trucks and marine vessels remaining the dominant modes of freight transport.
In non-OECD countries, increases in industrial output lead to growing energy use in all modes of freight transport.
More than two-thirds of the increase in the world’s energy use for freight travel is a result of heavy-class, heavy-duty trucks such as semi-trailers. As economic activity increases, residents in non-OECD countries continue to increase their demand for goods and services, and producers who use these heavy-duty trucks become further integrated into global supply chains.
As transportation infrastructure improves and roadways are better able to support heavy trucks in non-OECD countries, energy consumption shifts from light- and medium-class heavy-duty trucks to heavier vehicles, particularly near the end of the projection period.

## Slide 75: Transportation energy consumption grows fastest in non-OECD countries in Asia and Africa—
Non-OECD transportation energy consumption
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe and Eurasia | 7.0794 | 7.6716 | 8.0071 | 8.1884 | 8.6167
Americas | 6.9511 | 8.36 | 9.2317 | 10.0951 | 11.5113
Africa | 4.0884 | 6.0738 | 7.6886 | 9.6834 | 12.6637
Middle East | 6.3021 | 8.0445 | 10.1992 | 11.154 | 12.4605
Other Asia | 8.8789 | 12.5436 | 15.8757 | 19.5959 | 24.9142
India | 2.9012 | 5.1658 | 8.0313 | 11.4901 | 15.0091
China | 9.1768 | 15.9848 | 19.6208 | 21.4716 | 22.8712
OECD transportation energy consumption
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Europe | 18.1933 | 18.9666 | 18.1029 | 17.2907 | 18.0094
Americas | 31.9018 | 33.5985 | 30.7282 | 30.1905 | 32.0171
Asia | 6.9791 | 7.3429 | 7.4633 | 8.0203 | 9.1255
Asia
Americas
Europe
history projections
China
India
other Asia
Middle East
Africa
Americas
Europe
and Eurasia

## Slide 76: —but little growth occurs in Europe and Eurasia
Transportation energy consumption grows fastest in non-OECD countries in Asia and Africa, which are the regions with the fastest growth in gross domestic product (GDP).
In OECD and non-OECD countries in Europe and Eurasia, where economic growth is slower, transportation energy consumption grows more slowly or decreases.
In OECD countries, improvements in vehicle fuel efficiency outpace projected increases in travel demand, and as a result, total transportation energy use for OECD countries to declines by 1% in the Reference case.

## Slide 77: In the Reference case, the share of transportation fuel from alternative energy sources increases through 2050—
Transportation energy consumption
quadrillion British thermal units
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
World: Residual Fuel Oil | 3.3656 | 3.221 | 2.963 | 2.7719 | 2.5717 | 2.4074 | 2.806 | 2.7363 | 2.7122 | 2.5889 | 1.809 | 1.8894 | 2.0403 | 2.0639 | 2.0822 | 2.0937 | 2.0855 | 2.0812 | 2.0783 | 2.0822 | 2.0614 | 2.0666 | 2.0678 | 2.0583 | 2.0481 | 2.0054 | 1.9984 | 1.9797 | 1.9661 | 1.9714 | 1.9672 | 1.9645 | 1.9487 | 1.9561 | 1.9285 | 1.912 | 1.8851 | 1.8656 | 1.8572 | 1.8361 | 1.8141
World: Distillate Fuel Oil and Biodiesel | 18.6855 | 18.8811 | 18.6067 | 18.8928 | 19.7275 | 20.2837 | 20.4048 | 21.1483 | 21.3223 | 21.6985 | 22.4125 | 22.2701 | 22.1087 | 21.9458 | 21.7449 | 21.5222 | 21.2628 | 20.9375 | 20.6107 | 20.2599 | 19.9039 | 19.5224 | 19.1599 | 18.7945 | 18.4732 | 18.1992 | 17.9327 | 17.6753 | 17.4224 | 17.202 | 17.0161 | 16.8696 | 16.7226 | 16.6236 | 16.5427 | 16.4849 | 16.4106 | 16.3777 | 16.3682 | 16.3397 | 16.3002
World: Liquefied Petroleum Gas | 0.20832 | 0.22385 | 0.22838 | 0.23402 | 0.23571 | 0.23567 | 0.23305 | 0.23696 | 0.25124 | 0.26055 | 0.26699 | 0.27696 | 0.28068 | 0.2799 | 0.27743 | 0.27205 | 0.26617 | 0.25994 | 0.25214 | 0.2443 | 0.23512 | 0.22641 | 0.21618 | 0.20626 | 0.19606 | 0.18601 | 0.17645 | 0.16675 | 0.15743 | 0.1492 | 0.14165 | 0.13387 | 0.1255 | 0.1183 | 0.11182 | 0.10582 | 0.10024 | 0.095177 | 0.090391 | 0.085901 | 0.081671
World: Jet Fuel | 6.545 | 6.6184 | 6.5127 | 6.5877 | 6.6815 | 6.9598 | 7.2189 | 7.341 | 7.4136 | 7.5736 | 7.7368 | 7.8929 | 8.0437 | 8.1831 | 8.334 | 8.5044 | 8.6767 | 8.8484 | 9.0324 | 9.2102 | 9.3912 | 9.5647 | 9.7338 | 9.9088 | 10.0915 | 10.2767 | 10.4636 | 10.6547 | 10.8494 | 11.0464 | 11.2608 | 11.4734 | 11.6955 | 11.923 | 12.1586 | 12.4029 | 12.6486 | 12.9016 | 13.1582 | 13.4215 | 13.6985
World: Motor Gasoline and E85 | 26.5734 | 25.8993 | 25.6287 | 25.7044 | 25.7943 | 25.9436 | 26.359 | 26.2724 | 26.1049 | 25.8473 | 25.4469 | 24.9384 | 24.4034 | 23.8336 | 23.2439 | 22.6491 | 22.1608 | 21.71 | 21.3118 | 20.9349 | 20.5973 | 20.2967 | 20.0463 | 19.8185 | 19.627 | 19.474 | 19.3556 | 19.2872 | 19.2631 | 19.2404 | 19.2362 | 19.2291 | 19.2569 | 19.277 | 19.2882 | 19.2912 | 19.3351 | 19.3855 | 19.406 | 19.4174 | 19.421
World: Other Liquids | 0.3258 | 0.34597 | 0.32761 | 0.29922 | 0.28607 | 0.28682 | 0.28661 | 0.27396 | 0.27499 | 0.26787 | 0.24582 | 0.2477 | 0.24985 | 0.25131 | 0.25338 | 0.25519 | 0.2571 | 0.25897 | 0.26051 | 0.26189 | 0.26317 | 0.26552 | 0.26665 | 0.26704 | 0.26753 | 0.26797 | 0.26849 | 0.26862 | 0.26866 | 0.26965 | 0.27007 | 0.2713 | 0.2713 | 0.27145 | 0.27148 | 0.27125 | 0.27093 | 0.2706 | 0.2708 | 0.27035 | 0.27003
World: Natural Gas | 1.0082 | 1.0264 | 1.0228 | 1.0297 | 1.1437 | 1.142 | 1.1541 | 1.1917 | 1.3135 | 1.3803 | 1.497 | 1.6414 | 1.7666 | 1.9129 | 2.0686 | 2.2187 | 2.3463 | 2.4788 | 2.5886 | 2.6956 | 2.769 | 2.8562 | 2.9302 | 3.0217 | 3.1193 | 3.2142 | 3.3107 | 3.3937 | 3.4814 | 3.5348 | 3.575 | 3.683 | 3.7631 | 3.8632 | 3.9902 | 4.0896 | 4.1697 | 4.2632 | 4.3338 | 4.4427 | 4.6011
World: Electricity | 0.35804 | 0.36969 | 0.36744 | 0.38101 | 0.38037 | 0.40231 | 0.4089 | 0.41675 | 0.43768 | 0.46169 | 0.49297 | 0.53187 | 0.57511 | 0.62121 | 0.67137 | 0.72664 | 0.78638 | 0.84978 | 0.91884 | 0.9932 | 1.0733 | 1.1563 | 1.2435 | 1.3364 | 1.4344 | 1.5336 | 1.6375 | 1.7382 | 1.8367 | 1.936 | 2.0345 | 2.1318 | 2.2274 | 2.3203 | 2.4171 | 2.5151 | 2.6082 | 2.6993 | 2.7882 | 2.8773 | 2.9653
history projections
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
World: Residual Fuel Oil | 4.9907 | 5.0606 | 4.975 | 5.1191 | 5.2119 | 5.2912 | 5.6578 | 5.2706 | 5.3468 | 5.4157 | 4.8842 | 4.893 | 4.8921 | 4.8509 | 4.8369 | 4.8046 | 4.7859 | 4.7704 | 4.7415 | 4.7135 | 4.7559 | 4.7494 | 4.7104 | 4.6522 | 4.598 | 4.5505 | 4.5865 | 4.5464 | 4.4842 | 4.4317 | 4.3964 | 4.3534 | 4.2924 | 4.3265 | 4.263 | 4.2056 | 4.1268 | 4.0497 | 4.0132 | 3.9333 | 3.9438
World: Distillate Fuel Oil and Biodiesel | 16.6731 | 17.7139 | 18.9628 | 19.2013 | 19.908 | 20.5608 | 21.1026 | 21.5135 | 22.0714 | 22.4736 | 23.6689 | 24.1977 | 24.6887 | 25.1053 | 25.481 | 25.775 | 25.9956 | 26.1487 | 26.2862 | 26.3675 | 26.3778 | 26.406 | 26.4412 | 26.4489 | 26.5185 | 26.6079 | 26.7149 | 26.8242 | 26.9288 | 27.1092 | 27.252 | 27.5112 | 27.7152 | 28.0176 | 28.3073 | 28.637 | 28.8583 | 29.1388 | 29.3997 | 29.6548 | 29.8716
World: Liquefied Petroleum Gas | 0.40756 | 0.46962 | 0.48427 | 0.49214 | 0.54844 | 0.551 | 0.5616 | 0.57207 | 0.59658 | 0.61371 | 0.62389 | 0.625 | 0.61694 | 0.60387 | 0.59056 | 0.57474 | 0.55907 | 0.54362 | 0.52668 | 0.51008 | 0.49252 | 0.47514 | 0.45656 | 0.44179 | 0.42853 | 0.41708 | 0.40894 | 0.40221 | 0.39721 | 0.39531 | 0.39491 | 0.3963 | 0.39716 | 0.39966 | 0.40238 | 0.40428 | 0.40394 | 0.40425 | 0.40491 | 0.40482 | 0.40336
World: Jet Fuel | 4.1626 | 4.3368 | 4.505 | 4.6904 | 4.8596 | 5.1188 | 5.3915 | 5.2647 | 5.3475 | 5.5346 | 5.7472 | 5.9833 | 6.2197 | 6.4643 | 6.7146 | 6.9764 | 7.2367 | 7.5024 | 7.7746 | 8.0526 | 8.3417 | 8.6377 | 8.9334 | 9.2418 | 9.5592 | 9.8832 | 10.2153 | 10.55 | 10.8935 | 11.2432 | 11.5756 | 11.9306 | 12.3078 | 12.6921 | 13.0936 | 13.5047 | 13.9192 | 14.3485 | 14.7841 | 15.2322 | 15.7014
World: Motor Gasoline and E85 | 15.423 | 16.1836 | 17.0469 | 18.2898 | 19.1203 | 20.314 | 21.4127 | 21.9103 | 22.283 | 22.5439 | 22.7987 | 23.1447 | 23.59 | 24.0935 | 24.6346 | 25.2029 | 25.7347 | 26.2134 | 26.6963 | 27.1432 | 27.5748 | 27.9929 | 28.445 | 28.8734 | 29.317 | 29.7731 | 30.1937 | 30.6377 | 31.1183 | 31.5223 | 31.9079 | 32.2279 | 32.5789 | 32.8537 | 33.1217 | 33.3669 | 33.6595 | 33.9797 | 34.2528 | 34.5599 | 34.8684
World: Other Liquids | 0.15544 | 0.17753 | 0.16024 | 0.10742 | 0.11282 | 0.12539 | 0.15234 | 0.13776 | 0.14027 | 0.14955 | 0.1421 | 0.14228 | 0.14238 | 0.14145 | 0.14111 | 0.14029 | 0.13987 | 0.13941 | 0.13852 | 0.13778 | 0.13702 | 0.13779 | 0.1371 | 0.1354 | 0.13379 | 0.13242 | 0.13147 | 0.13181 | 0.13001 | 0.12839 | 0.12658 | 0.12597 | 0.12413 | 0.12307 | 0.12117 | 0.11933 | 0.1171 | 0.11491 | 0.11476 | 0.11315 | 0.11177
World: Natural Gas | 2.8881 | 3.0955 | 2.9249 | 2.9893 | 3.1121 | 3.2245 | 3.351 | 3.8526 | 4.0893 | 4.375 | 4.6548 | 5.0445 | 5.4381 | 5.8529 | 6.2682 | 6.6959 | 7.1348 | 7.6254 | 8.0285 | 8.4807 | 8.9017 | 9.2726 | 9.5445 | 9.9031 | 10.247 | 10.6653 | 10.9563 | 11.3881 | 11.8039 | 12.2537 | 12.6339 | 13.1446 | 13.6098 | 14.0587 | 14.6205 | 15.164 | 15.6876 | 16.1721 | 16.6847 | 17.184 | 17.701
World: Electricity | 0.67371 | 0.746 | 0.76702 | 0.79015 | 0.81465 | 0.82373 | 0.89149 | 1.1483 | 1.197 | 1.2622 | 1.3245 | 1.3787 | 1.437 | 1.4986 | 1.5604 | 1.6295 | 1.7048 | 1.7925 | 1.8791 | 1.9743 | 2.0731 | 2.175 | 2.2818 | 2.3953 | 2.5143 | 2.6463 | 2.7848 | 2.9242 | 3.0692 | 3.2257 | 3.3913 | 3.566 | 3.7561 | 3.9563 | 4.1663 | 4.3819 | 4.5942 | 4.8057 | 5.0188 | 5.2323 | 5.4454
OECD
non-OECD

## Slide 78: —but refined petroleum and other liquids remain dominant
The worldwide transportation sector accounts for 59% of total end-use sector liquid fuels (residual fuel oil, diesel, motor gasoline, and jet fuel) consumption in 2050, about the same as in 2018.
Within the transportation sector, the use of refined petroleum and other liquid fuels continues to increase through 2050, but its share decreases from 94% to about 82% as alternative fuel use slowly increases.
Motor gasoline, including biofuel additives such as ethanol, remains the primary fuel for transportation purposes, accounting for 32% of the world’s transportation-related energy use in 2050.
A continuing global rise in air travel demand leads to jet fuel consumption more than doubling from 2018 to 2050.
Natural gas and electricity, although starting from much lower levels of use than liquid fuels, are the fastest-growing forms of transportation energy use. Consumption of each more than quadruples from 2018 to 2050.

## Slide 79: In OECD countries, increases in jet fuel consumption are more than offset by declines in motor gasoline and distillate fuel consumption—
Transportation fuel consumption
quadrillion British thermal units
Chart: 
| motor gasoline and E85 | distillate fuel oil and biodiesel | jet fuel | residual fuel oil | natural gas | electricity | liquefied petroleum gas | other liquids
series1 | 34.8684 | 29.8716 | 15.7014 | 3.9438 | 17.701 | 5.4454 | 0.40336 | 0.11177
series0 | 22.283 | 22.0714 | 5.3475 | 5.3468 | 4.0893 | 1.197 | 0.59658 | 0.14027
Chart: 
| motor gasoline and E85 | distillate fuel oil and biodiesel | jet fuel | residual fuel oil | natural gas | electricity | liquefied petroleum gas | other liquids
series1 | 19.421 | 16.3002 | 13.6985 | 1.8141 | 4.6011 | 2.9653 | 0.081671 | 0.27003
series0 | 26.1049 | 21.3223 | 7.4136 | 2.7122 | 1.3135 | 0.43768 | 0.25124 | 0.27499
OECD
non-OECD

## Slide 80: —as on-road vehicles become more efficient
Improvements in on-road fuel economy are the primary driver in reduced motor gasoline consumption in OECD countries by about 7 quadrillion Btu between 2017 and 2050. Most of the reduction occurs in the United States, where the effects of increasingly stringent fuel efficiency standards more than offset increases in vehicle-miles traveled.
Diesel consumption also decreases in OECD regions, mainly in OECD Europe, in part as a result of increasing on-road efficiency standards. Demand for marine distillate increases in part because of a 2020 reduction in global sulfur emission limits for international ships.
Natural gas (driven by favorable economics in heavy trucking) and electricity (driven by its use in passenger rail and light-duty vehicles) are the fastest-growing forms of energy used for transportation in OECD countries on a percentage basis.
Growing air travel activity increases jet fuel consumption by more than 16 quadrillion Btu from 2018 to 2050.

## Slide 81: Light-duty vehicle stocks increase significantly in non-OECD countries—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Total OECD:ICE LPG | 6.3729 | 6.6029 | 6.6637 | 6.5751 | 6.3472 | 6.0708 | 5.948 | 6.2882 | 6.9352 | 7.3796 | 7.7027 | 8.25 | 8.5651 | 8.7033 | 8.7753 | 8.7246 | 8.6495 | 8.5599 | 8.3882 | 8.1773 | 7.8978 | 7.6638 | 7.3008 | 6.9542 | 6.5589 | 6.1466 | 5.7361 | 5.3009 | 4.8731 | 4.4882 | 4.1259 | 3.8077 | 3.4981 | 3.2261 | 2.9757 | 2.7379 | 2.5114 | 2.2998 | 2.1014 | 1.9159 | 1.7412
Total OECD:ICE or Hybrid Motor Gasoline | 518.0286 | 514.0885 | 515.2072 | 513.9488 | 514.7663 | 517.5178 | 522.9045 | 521.3881 | 520.4418 | 518.3657 | 515.2195 | 511.4169 | 507.5821 | 504.4358 | 501.5482 | 499.1686 | 497.2162 | 495.457 | 494.3981 | 493.6278 | 493.6013 | 493.4297 | 493.7535 | 493.8112 | 494.0481 | 494.7476 | 495.0169 | 496.077 | 497.7823 | 498.7126 | 499.4955 | 499.4082 | 499.6982 | 499.0595 | 497.6876 | 495.7094 | 494.2723 | 492.5513 | 490.0334 | 487.7324 | 485.1681
Total OECD:ICE or Hybrid Diesel | 143.8853 | 148.1226 | 151.874 | 154.5553 | 157.2779 | 159.9473 | 164.797 | 168.0002 | 171.6299 | 175.3847 | 178.6406 | 180.4585 | 180.887 | 180.061 | 178.2217 | 175.4736 | 171.8904 | 167.5068 | 162.4122 | 156.7036 | 150.3818 | 143.7201 | 136.4683 | 128.8681 | 120.9951 | 112.7834 | 104.5928 | 96.4135 | 88.331 | 81.0295 | 74.2522 | 68.0699 | 62.1557 | 57.2737 | 52.5521 | 48.4805 | 44.4039 | 41.0415 | 38.3307 | 35.7443 | 33.4945
Total OECD:Plug In Hybrids | 4.3e-05 | 0.010709 | 0.045381 | 0.089232 | 0.14679 | 0.2267 | 0.35541 | 0.53011 | 0.86691 | 1.2285 | 1.6252 | 2.3996 | 3.428 | 4.4604 | 5.5365 | 6.7376 | 8.0762 | 9.5839 | 11.2482 | 12.8888 | 14.6129 | 16.5859 | 18.8481 | 21.0565 | 23.2636 | 25.5545 | 27.7869 | 30.1589 | 32.502 | 34.5348 | 36.544 | 38.2379 | 40.309 | 41.7442 | 43.1932 | 44.4481 | 45.7151 | 46.9462 | 47.8259 | 48.7382 | 49.4844
Total OECD:ICE Natural Gas | 0.34057 | 0.35821 | 0.38075 | 0.39359 | 0.40969 | 0.40065 | 0.73095 | 2.7949 | 5.0898 | 8.0859 | 11.6583 | 15.6522 | 19.936 | 24.3789 | 29.0211 | 33.3767 | 37.402 | 41.2306 | 44.2037 | 46.9392 | 48.8763 | 51.1336 | 52.9197 | 55.0836 | 56.8943 | 58.3828 | 59.9387 | 60.9688 | 61.6352 | 62.322 | 62.8881 | 63.9221 | 64.4103 | 65.4118 | 66.5254 | 67.4966 | 68.3217 | 68.8065 | 69.4823 | 69.6868 | 69.9236
Total OECD:Electric Vehicles | 0.024787 | 0.058051 | 0.10787 | 0.21284 | 0.34012 | 0.51679 | 0.69343 | 2.3524 | 3.5063 | 4.4751 | 5.8513 | 7.6415 | 9.7506 | 12.2076 | 15.0227 | 18.2696 | 21.925 | 25.8873 | 30.2885 | 35.1005 | 40.3403 | 45.7534 | 51.4086 | 57.4558 | 64.0577 | 70.8394 | 77.9892 | 84.7935 | 91.412 | 98.2138 | 104.9071 | 111.6166 | 117.946 | 124.2624 | 130.934 | 137.8174 | 144.1946 | 150.406 | 156.6037 | 162.8431 | 168.9428
Total OECD:Hydrogen Fuel Cell | 0 | 0 | 0.000108 | 0.000131 | 0.000131 | 0.000211 | 0.001251 | 0.004172 | 0.009439 | 0.019477 | 0.036466 | 0.06665 | 0.11044 | 0.15578 | 0.20647 | 0.26123 | 0.31475 | 0.36676 | 0.41435 | 0.46058 | 0.50437 | 0.546 | 0.58087 | 0.61263 | 0.64185 | 0.6682 | 0.69186 | 0.71142 | 0.72826 | 0.74276 | 0.75529 | 0.76565 | 0.7743 | 0.78166 | 0.78808 | 0.79366 | 0.79851 | 0.80305 | 0.80776 | 0.81253 | 0.81756
Total OECD:ICE or Hybrid Other | 5.3e-05 | 5.3e-05 | 6.5e-05 | 7.9e-05 | 0.000109 | 0.000809 | 0.002054 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
history projections
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Total Non-OECD:ICE LPG | 13.5908 | 14.8508 | 15.9452 | 16.8457 | 17.564 | 18.3487 | 18.6045 | 19.5313 | 20.3555 | 20.9337 | 21.2646 | 21.2986 | 20.9667 | 20.431 | 19.8707 | 19.2158 | 18.5787 | 17.997 | 17.3525 | 16.7559 | 16.1146 | 15.493 | 14.7599 | 14.2045 | 13.6695 | 13.195 | 12.8382 | 12.5366 | 12.2832 | 12.1949 | 12.1405 | 12.1786 | 12.1441 | 12.1887 | 12.2282 | 12.237 | 12.1497 | 12.0743 | 12.0059 | 11.9172 | 11.7651
Total Non-OECD:Hydrogen Fuel Cell | 0 | 0 | 0 | 0 | 0 | 0 | 1.7008e-09 | 1.7008e-09 | 2.803e-09 | 4.0437e-09 | 5.5266e-09 | 7.1806e-09 | 8.7128e-09 | 1.0254e-08 | 1.2008e-08 | 1.3833e-08 | 1.571e-08 | 1.7839e-08 | 1.9762e-08 | 2.1908e-08 | 2.3591e-08 | 1.1429e-07 | 1.9992e-07 | 3.0156e-07 | 4.0287e-07 | 5.0212e-07 | 6.1307e-07 | 7.2148e-07 | 8.2105e-07 | 9.2915e-07 | 1.0293e-06 | 1.5273e-06 | 1.9743e-06 | 2.4593e-06 | 2.9352e-06 | 3.3646e-06 | 3.7495e-06 | 4.087e-06 | 4.4215e-06 | 4.7239e-06 | 4.9876e-06
Total Non-OECD:ICE or Hybrid Motor Gasoline | 270.3026 | 295.4777 | 325.8957 | 356.4457 | 388.2513 | 421.9301 | 452.4625 | 472.4808 | 492.1175 | 510.9798 | 529.1903 | 548.7358 | 569.7074 | 591.702 | 614.6625 | 637.6902 | 660.18 | 681.6557 | 703.5348 | 724.4633 | 745.0317 | 764.2564 | 783.4514 | 800.9403 | 817.4924 | 833.2345 | 846.8391 | 860.3631 | 874.6092 | 885.8196 | 896.1538 | 903.5094 | 910.9224 | 915.1828 | 918.847 | 921.2268 | 925.3412 | 930.1273 | 933.3827 | 938.0895 | 943.6408
Total Non-OECD:ICE or Hybrid Diesel | 41.5275 | 44.5888 | 48.7896 | 52.8523 | 57.0661 | 61.028 | 63.5846 | 66.9386 | 71.9475 | 77.5353 | 83.7062 | 89.0786 | 93.0946 | 96.0031 | 98.0094 | 98.9241 | 99.0603 | 98.4561 | 97.3098 | 95.997 | 95.1806 | 94.7694 | 93.9919 | 93.0174 | 92.284 | 91.3117 | 91.1365 | 90.3446 | 88.8057 | 88.4144 | 88.0003 | 88.4401 | 87.9658 | 89.098 | 89.6706 | 90.4957 | 89.9921 | 89.4053 | 89.6754 | 88.8996 | 88.1052
Total Non-OECD:ICE Natural Gas | 12.6013 | 14.5231 | 16.183 | 19.5039 | 22.037 | 22.4359 | 22.9875 | 26.7132 | 30.3397 | 34.0673 | 38.1027 | 42.5766 | 47.1601 | 51.6638 | 56.4618 | 61.2705 | 66.0869 | 71.0402 | 75.2678 | 79.0356 | 82.0211 | 84.7243 | 86.5902 | 88.9212 | 90.7017 | 92.1193 | 93.6432 | 94.8349 | 95.4554 | 96.3984 | 97.1903 | 98.6875 | 99.4635 | 101.0764 | 102.646 | 104.4375 | 105.6663 | 106.3017 | 107.2521 | 107.9354 | 108.0663
Total Non-OECD:Plug In Hybrids | 0.00034 | 0.000665 | 0.001144 | 0.001895 | 0.026639 | 0.088107 | 0.22712 | 0.64761 | 1.4636 | 2.2013 | 3.1633 | 4.5205 | 6.2321 | 8.3063 | 10.4803 | 13.16 | 16.4317 | 20.3631 | 25.0027 | 30.3036 | 35.9211 | 42.4755 | 49.8352 | 57.8707 | 66.4627 | 75.6277 | 84.8477 | 95.2213 | 105.9182 | 116.4673 | 127.0546 | 137.3766 | 148.1197 | 157.9274 | 167.4064 | 176.2721 | 184.7942 | 192.8338 | 199.8343 | 206.2845 | 212.0049
Total Non-OECD:Electric Vehicles | 0.0025263 | 0.0083683 | 0.020799 | 0.036961 | 0.087908 | 0.25494 | 0.51346 | 1.1802 | 2.1933 | 3.7491 | 6.0235 | 8.0533 | 10.4361 | 13.1695 | 15.6402 | 18.8485 | 22.6191 | 27.2169 | 31.9488 | 37.4791 | 43.357 | 49.3671 | 55.7972 | 62.76 | 70.3125 | 78.5196 | 87.4774 | 95.9466 | 104.2598 | 113.7145 | 123.7544 | 134.8121 | 146.6315 | 159.4774 | 173.337 | 188.1539 | 202.7494 | 217.2319 | 232.5078 | 247.6688 | 262.8002
Total Non-OECD:ICE or Hybrid Other | 0 | 0 | 0 | 0 | 0 | 1.7e-05 | 1.7e-05 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
OECD
non-OECD

## Slide 82: —and vehicles with alternative-fuel powertrains represent an increasingly larger share of the fleet
From 2018 to 2050, the light-duty vehicle fleet transitions from primarily gasoline and diesel vehicles; by 2050, electricity and natural gas powers over one-third of the light-duty vehicle fleet in the Reference case.
OECD electric light-duty vehicle stocks increase from 3.5 million vehicles in 2018 to 169 million in 2050, and electric vehicle stocks in the non-OECD countries are projected to increase from 2.2 million vehicles in 2018 to 269 million in 2050.
Much of the decline in diesel consumption in OECD countries comes as Europe gradually transitions from diesel powered light-duty vehicles to electric vehicles. Because stocks reflect existing vehicles, the rate of growth in vehicle stocks is lower than that of new vehicle sales.
Many regions, including non-OECD Europe and Eurasia, the Middle East, and Africa, maintain mostly petroleum-fueled light-duty fleets throughout the projection period. These regions continue to operate largely gasoline and diesel vehicle fleets because of many reasons, such as cost, infrastructure, climate, and geography.

## Slide 83: Growth in light-duty passenger travel gradually slows in China—
Passenger vehicle travel (select regions)
trillion vehicle miles traveled
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
tr_passengermile_usa_tot_bvehmiles | 3796.4238 | 3797.9341 | 3851.2016 | 3942.5872 | 4029.4818 | 4137.0672 | 4271.0895 | 4351.534 | 4417.5874 | 4485.0575 | 4539.6234 | 4583.7629 | 4622.1089 | 4655.1695 | 4686.3312 | 4719.6287 | 4766.1775 | 4812.9509 | 4865.216 | 4908.6923 | 4952.1344 | 4995.5825 | 5038.4669 | 5081.4332 | 5124.8685 | 5166.8237 | 5214.268 | 5264.2164 | 5316.2624 | 5368.8253 | 5422.1735 | 5475.6069 | 5530.0118 | 5585.7699 | 5642.3709 | 5699.7023 | 5758.1872 | 5816.8474 | 5874.1316 | 5930.8243 | 5985.7267
tr_passengermile_eur_tot_bvehmiles | 3193.3766 | 3235.5344 | 3233.5204 | 3271.6265 | 3400.6195 | 3520.2148 | 3687.3859 | 3795.1435 | 3857.6883 | 3904.9789 | 3959.8808 | 4014.277 | 4066.4783 | 4115.9329 | 4166.6983 | 4220.0106 | 4274.5195 | 4329.8662 | 4385.1014 | 4441.9374 | 4499.5717 | 4552.87 | 4603.8945 | 4656.511 | 4711.2174 | 4767.6463 | 4824.1792 | 4881.7217 | 4939.5259 | 4998.1785 | 5056.6298 | 5118.5723 | 5183.4647 | 5247.4699 | 5312.599 | 5379.3737 | 5446.5392 | 5513.6613 | 5582.4127 | 5652.1209 | 5725.179
tr_passengermile_chi_tot_bvehmiles | 1676.1827 | 1878.8776 | 2063.2608 | 2394.5429 | 2655.39 | 3136.9635 | 3505.7614 | 3768.5898 | 4035.355 | 4334.4415 | 4631.4853 | 4898.2259 | 5141.5909 | 5391.058 | 5631.8199 | 5856.41 | 6063.7903 | 6263.2282 | 6445.8733 | 6613.1755 | 6769.4505 | 6909.5834 | 7040.8655 | 7160.8385 | 7273.3671 | 7379.7109 | 7483.1717 | 7576.3759 | 7667.0224 | 7756.5681 | 7826.7515 | 7908.1881 | 7992.0056 | 8074.9279 | 8158.3989 | 8236.7888 | 8313.7912 | 8390.8957 | 8464.1699 | 8536.9818 | 8610.9978
tr_passengermile_ind_tot_bvehmiles | 1000.3975 | 1081.0007 | 1158.7474 | 1261.1502 | 1386.4846 | 1551.9725 | 1737.7344 | 1870.2441 | 2033.9044 | 2207.4912 | 2393.4007 | 2588.6154 | 2782.5464 | 2976.8163 | 3174.707 | 3377.4997 | 3584.0618 | 3790.9531 | 3992.5433 | 4188.3605 | 4376.7272 | 4555.1301 | 4724.6935 | 4886.4469 | 5040.3377 | 5186.6011 | 5325.4129 | 5457.7444 | 5583.9838 | 5705.2379 | 5824.0111 | 5936.8585 | 6094.9251 | 6310.9993 | 6520.9564 | 6701.8434 | 6800.4755 | 6895.9026 | 6987.6542 | 7076.5804 | 7163.314
tr_passengermile_oas_tot_bvehmiles | 1505.0778 | 1622.4727 | 1716.3571 | 1856.0277 | 1961.565 | 2054.273 | 2209.6825 | 2313.4565 | 2419.8075 | 2522.1252 | 2627.4477 | 2739.5482 | 2852.1322 | 2965.1269 | 3080.8166 | 3202.2751 | 3326.0004 | 3453.0834 | 3584.8209 | 3721.4251 | 3861.5439 | 4003.4235 | 4148.319 | 4299.1406 | 4454.3474 | 4613.831 | 4776.8122 | 4948.3564 | 5128.9515 | 5314.7778 | 5512.6044 | 5702.473 | 5898.7997 | 6099.5245 | 6306.5682 | 6518.4598 | 6731.13 | 6947.7857 | 7165.7645 | 7388.6311 | 7618.8145
tr_passengermile_mid_tot_bvehmiles | 627.9078 | 656.389 | 687.5429 | 769.3967 | 847.8492 | 942.3654 | 1029.504 | 1061.9685 | 1095.1353 | 1122.3458 | 1155.0139 | 1190.2085 | 1227.9044 | 1268.3321 | 1310.5809 | 1354.941 | 1399.054 | 1444.1944 | 1491.3202 | 1539.8912 | 1590.2302 | 1642.2027 | 1695.1547 | 1750.4249 | 1806.8051 | 1864.4456 | 1921.055 | 1977.2786 | 2033.8805 | 2090.5209 | 2139.9008 | 2194.7268 | 2249.5599 | 2304.5689 | 2360.3317 | 2418.073 | 2475.8891 | 2535.2952 | 2596.3911 | 2658.9282 | 2721.6293
tr_passengermile_afr_tot_bvehmiles | 494.2312 | 521.9271 | 550.4454 | 576.1746 | 606.1767 | 686.4224 | 778.31 | 800.0728 | 821.4226 | 853.6813 | 887.0606 | 919.6567 | 954.5282 | 990.2064 | 1028.5837 | 1067.3031 | 1108.2506 | 1151.2847 | 1195.5153 | 1240.9911 | 1287.2063 | 1334.733 | 1384.1091 | 1434.5204 | 1486.7041 | 1540.6344 | 1597.2742 | 1655.1672 | 1715.0839 | 1778.0333 | 1836.7352 | 1896.2078 | 1955.8587 | 2017.6874 | 2081.1126 | 2145.8142 | 2212.5845 | 2281.5588 | 2351.9234 | 2425.2115 | 2501.721
history projections
China
other non-OECD
Asia
India
United States
OECD Europe
Middle East
Africa

## Slide 84: —but grows more rapidly in other parts of non-OECD Asia
In the Reference case, China’s population peaks in about 2030, leading to a gradual slowing of light-duty passenger travel growth.
Growing populations and economies in India and other non-OECD Asia (including Thailand, Indonesia, and Vietnam) lead to increased demand for personal travel.
The United States and OECD Europe, with less unmet travel demand and slowly growing populations, see less growth in passenger travel.
The population growth in Africa, which nearly doubles from 2018 to 2050 in the Reference case, leads to an increase in travel demand and passenger vehicle travel.

## Slide 85: Electricity

## Slide 87: In the Reference case, the projected growth rate in net electricity generation in non-OECD countries is more than two times higher than in OECD countries—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Total OECD | 10068.4111 | 10083.7266 | 10010.5237 | 10058.9725 | 10014.3434 | 10071.8265 | 10153.7782 | 10343.8969 | 10538.3281 | 10581.6307 | 10714.7246 | 10820.4115 | 10925.4326 | 11028.6585 | 11129.5783 | 11229.0279 | 11343.8839 | 11458.3754 | 11576.4994 | 11696.0727 | 11806.4634 | 11917.3809 | 12023.8267 | 12133.9478 | 12246.0771 | 12364.1394 | 12489.6584 | 12617.2768 | 12746.3708 | 12875.4546 | 13002.2696 | 13133.9696 | 13267.39 | 13402.7071 | 13541.0223 | 13681.9655 | 13832.8054 | 13983.8804 | 14136.334 | 14288.7194 | 14444.1191
Total Non-OECD | 10063.4375 | 10761.9045 | 11258.2309 | 11895.1948 | 12378.3503 | 12743.075 | 13331.5091 | 13760.4746 | 14229.9073 | 14699.34 | 15168.7727 | 15537.0563 | 15905.3399 | 16273.6235 | 16641.9072 | 17010.1908 | 17465.6999 | 17921.209 | 18376.718 | 18832.2271 | 19287.7362 | 19764.8282 | 20241.9202 | 20719.0122 | 21196.1042 | 21673.1962 | 22159.503 | 22645.8099 | 23132.1167 | 23618.4236 | 24104.7304 | 24714.9132 | 25325.096 | 25935.2788 | 26545.4616 | 27155.6444 | 27685.1465 | 28214.6485 | 28744.1505 | 29273.6525 | 29803.1546
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
RESIDENTIAL: electricity | 17.8249 | 18.0215 | 18.4112 | 19.1342 | 19.5067 | 20.2682 | 21.048 | 22.1173 | 23.0272 | 23.5229 | 24.0874 | 24.6547 | 25.2433 | 25.8634 | 26.5254 | 27.2186 | 28.0113 | 28.8383 | 29.6902 | 30.5851 | 31.5096 | 32.3296 | 33.1727 | 34.0346 | 34.9304 | 35.8563 | 36.695 | 37.5488 | 38.4026 | 39.2792 | 40.174 | 41.2336 | 42.3286 | 43.4535 | 44.6227 | 45.8093 | 46.7697 | 47.7294 | 48.6893 | 49.6382 | 50.6397
COMMERCIAL: electricity | 14.775 | 14.9744 | 15.244 | 15.6383 | 15.8661 | 16.4975 | 16.8337 | 17.1588 | 17.6173 | 17.8588 | 18.2426 | 18.6256 | 19.0078 | 19.3721 | 19.7441 | 20.1285 | 20.5355 | 20.953 | 21.3836 | 21.8279 | 22.2652 | 22.6734 | 23.067 | 23.472 | 23.8873 | 24.3116 | 24.7303 | 25.1467 | 25.5649 | 25.9912 | 26.4214 | 26.8741 | 27.3425 | 27.8194 | 28.306 | 28.8054 | 29.2835 | 29.769 | 30.2571 | 30.7533 | 31.2654
INDUSTRIAL: electricity | 29.8128 | 31.5648 | 32.2753 | 33.2201 | 34.0303 | 34.0561 | 34.9618 | 35.0541 | 36.6742 | 37.2181 | 37.8984 | 38.5858 | 39.0508 | 39.5232 | 40.0074 | 40.5475 | 40.9686 | 41.5087 | 42.0129 | 42.5513 | 43.0491 | 43.5407 | 43.9403 | 44.3583 | 44.7069 | 45.1649 | 45.6111 | 46.0546 | 46.4051 | 46.7837 | 47.131 | 47.5807 | 47.9911 | 48.448 | 48.894 | 49.3229 | 49.7833 | 50.1236 | 50.5034 | 50.8195 | 51.1653
TRANSPORTATION: electricity | 1.0317 | 1.1157 | 1.1345 | 1.1712 | 1.195 | 1.226 | 1.3004 | 1.565 | 1.6347 | 1.7239 | 1.8174 | 1.9106 | 2.0121 | 2.1198 | 2.2318 | 2.3561 | 2.4911 | 2.6422 | 2.798 | 2.9675 | 3.1464 | 3.3314 | 3.5253 | 3.7316 | 3.9486 | 4.1799 | 4.4224 | 4.6624 | 4.906 | 5.1617 | 5.4259 | 5.6978 | 5.9835 | 6.2766 | 6.5834 | 6.897 | 7.2023 | 7.505 | 7.807 | 8.1096 | 8.4107
Net electricity generation, world
trillion kilowatthours
Electricity use by sector, world
quadrillion British thermal units
history projections

## Slide 88: —and electricity use in residential buildings is a major contributor to growth
Net electricity generation (to the grid) in countries that are not part of the Organization of Economic Cooperation and Development (OECD) increases an average of 2.3% per year from 2018 to 2050, compared with 1.0% per year in OECD countries.
Electricity use increases the most in the buildings sector, particularly residential, as personal incomes rise and urban migration continues in non-OECD countries. Residential building electricity consumption more than doubles from 2018 to 2050.
The share of electricity used in transportation nearly triples between 2018 and 2050 as more plug-in electric vehicles enter the fleet and electricity use for rail expands. Yet, transportation still accounts for less than 6% of total delivered electricity consumption in 2050.

## Slide 89: In the Reference case, most of the growth in electricity generation is fueled by renewables and natural gas—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Petroleum | 912.3874 | 633.304 | 320.9918 | 189.5673 | 165.2402
Nuclear | 2629.7094 | 2708.5347 | 3035.4463 | 3281.2573 | 3575.6766
Coal | 8076.9116 | 8498.9296 | 8572.9054 | 8601.4451 | 9595.9107
Natural Gas | 4326.4014 | 5911.7692 | 6649.4433 | 8114.5995 | 9254.5427
Renewables | 4186.4387 | 8130.9598 | 12515.4127 | 16920.1308 | 21655.9034
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Petroleum | 912.3874 | 633.304 | 320.9918 | 189.5673 | 165.2402
Nuclear | 2629.7094 | 2708.5347 | 3035.4463 | 3281.2573 | 3575.6766
Coal | 8076.9116 | 8498.9296 | 8572.9054 | 8601.4451 | 9595.9107
Natural Gas | 4326.4014 | 5911.7692 | 6649.4433 | 8114.5995 | 9254.5427
Renewables | 4186.4387 | 8130.9598 | 12515.4127 | 16920.1308 | 21655.9034
Net electricity generation by fuel, world
trillion kilowatthours
Share of net electricity generation, world
percent
history projections

## Slide 90: —and their combined share of total generation rises to 70% in 2050
Renewables (including hydropower) are the fastest-growing source of electricity generation during the 2018 to 2050 period, rising by an average of 3.6% per year. Technological improvements and government incentives in many countries support their increased use.
By 2050, China, India, OECD Europe, and the United States have almost 75% of the world’s renewables generation. Growth in these regions results from both policy and, in the case of India and China, increasing demand for new sources of generation.
Natural gas generation grows by an average of 1.5% per year from 2018 to 2050, and nuclear generation grows by 1.0% per year. The level of coal-fired generation remains relatively stable, but its share of electricity generation declines from 35% in 2018 to 22% by 2050 as total generation increases.
By 2025, in the Reference case, renewables surpass coal as the primary source for electricity generation, and by 2050, renewables account for almost half of total world electricity generation.

## Slide 91: Wind and solar dominate growth in renewables generation—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Hydro | 3402.1538 | 4701.846 | 5406.0007 | 5770.0161 | 5989.3065
Wind | 339.3148 | 1726.1233 | 3170.6318 | 5221.0312 | 6707.873
Solar | 33.3797 | 1298.2591 | 3474.4513 | 5409.1591 | 8331.1039
Geothermal | 64.7182 | 81.4117 | 181.7382 | 219.1008 | 235.5696
Other | 346.8723 | 323.3196 | 282.5906 | 300.8237 | 392.0505
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Hydro | 3402.1538 | 4701.846 | 5406.0007 | 5770.0161 | 5989.3065
Wind | 339.3148 | 1726.1233 | 3170.6318 | 5221.0312 | 6707.873
Solar | 33.3797 | 1298.2591 | 3474.4513 | 5409.1591 | 8331.1039
Geothermal | 64.7182 | 81.4117 | 181.7382 | 219.1008 | 235.5696
Other | 346.8723 | 323.3196 | 282.5906 | 300.8237 | 392.0505
history projections

## Slide 92: —and represent over 70% of related electric generating capacity additions by 2050
With modest growth, hydropower’s share of renewables generation falls from 62% in 2018 to 28% in 2050 because resource availability in OECD countries and environmental concerns in many countries limit the number of new mid- and large-scale projects.
Generation from non-hydropower renewables increases an average of 5.7% per year from 2018 to 2050. By 2050, China, India, OECD Europe, and the United States are responsible for more than 80% of the world’s non-hydropower renewables generation.
Among renewable energy sources, electricity generation from wind and solar resources increase the most between 2018 and 2050, reaching 6.7 trillion and 8.3 trillion kilowatthours (kWh), respectively, as these technologies become more cost competitive and are supported by government policies in many countries.
By 2050, wind and solar account for over 70% of total renewables generation.

## Slide 93: In both OECD and non-OECD countries, increases in electricity demand are primarily met with renewables generation—
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
renewable | 213.4086 | 831.8389 | 1009.8047 | 1155.3905 | 1296.4203 | 1421.6632 | 1542.3642 | 1686.1111 | 1831.9635 | 1978.2223 | 2131.82 | 2277.8183 | 2382.7286 | 2479.5392 | 2581.4372 | 2688.9066 | 2800.4693 | 2923.4998 | 3045.1316 | 3174.4634 | 3302.9559 | 3411.9013 | 3531.2939 | 3635.2842 | 3756.2151 | 3863.6389 | 3970.9441 | 4105.5412 | 4243.8721 | 4364.3525 | 4501.1062 | 4630.2303
non-renewable | -170.1061 | -270.8925 | -343.1713 | -383.7361 | -421.5401 | -445.8631 | -467.1147 | -496.0056 | -527.3662 | -555.5012 | -589.5257 | -625.1332 | -619.1259 | -609.4908 | -601.2677 | -596.6078 | -590.108 | -587.6196 | -581.6331 | -581.8709 | -581.2797 | -563.4098 | -551.1027 | -521.6725 | -507.2864 | -476.3948 | -442.7569 | -426.5142 | -413.7699 | -381.7968 | -366.1651 | -339.8895
total growth | 43.3026 | 560.9464 | 666.6333 | 771.6544 | 874.8803 | 975.8001 | 1075.2497 | 1190.1057 | 1304.5972 | 1422.7212 | 1542.2945 | 1652.6852 | 1763.6027 | 1870.0485 | 1980.1696 | 2092.2989 | 2210.3612 | 2335.8802 | 2463.4986 | 2592.5926 | 2721.6764 | 2848.4914 | 2980.1914 | 3113.6118 | 3248.9289 | 3387.2441 | 3528.1873 | 3679.0272 | 3830.1022 | 3982.5558 | 4134.9412 | 4290.3409
Chart: 
| 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
non-renewable | 132.5178 | 265.0356 | 362.9665 | 460.8974 | 558.8282 | 656.7591 | 754.69 | 892.857 | 1031.0242 | 1169.1914 | 1307.3584 | 1445.5255 | 1598.4422 | 1751.3589 | 1904.2756 | 2057.1922 | 2210.1089 | 2366.464 | 2522.8191 | 2679.1742 | 2835.5293 | 2991.8845 | 3186.6192 | 3381.3541 | 3576.0888 | 3770.8237 | 3965.5586 | 4207.0198 | 4448.4812 | 4689.9424 | 4931.4037 | 5172.8651
renewable | 336.9149 | 673.8299 | 944.1827 | 1214.5355 | 1484.8882 | 1755.2408 | 2025.5937 | 2342.9356 | 2660.2775 | 2977.6195 | 3294.9614 | 3612.3034 | 3936.4787 | 4260.654 | 4584.8294 | 4909.0049 | 5233.1802 | 5563.1318 | 5893.0835 | 6223.0354 | 6552.9871 | 6882.9387 | 7298.3866 | 7713.8347 | 8129.2827 | 8544.7307 | 8960.1787 | 9248.2195 | 9536.2602 | 9824.3009 | 10112.3417 | 10400.3822
total growth | 469.4327 | 938.8654 | 1307.149 | 1675.4326 | 2043.7162 | 2411.9999 | 2780.2835 | 3235.7926 | 3691.3017 | 4146.8107 | 4602.3198 | 5057.8289 | 5534.9209 | 6012.0129 | 6489.1049 | 6966.1969 | 7443.2889 | 7929.5957 | 8415.9026 | 8902.2094 | 9388.5163 | 9874.8231 | 10485.0059 | 11095.1887 | 11705.3715 | 12315.5543 | 12925.7371 | 13455.2392 | 13984.7412 | 14514.2432 | 15043.7452 | 15573.2473
OECD

## Slide 94: —while generation from non-renewables sources in the OECD declines
OECD and non-OECD countries have vastly different electricity demand growth profiles. OECD demand for net electricity generation (to the grid) grows at 1.0% per year between 2018 and 2050, and non-OECD demand grows at 2.3% per year on average.
Although renewables are cost-competitive compared with new fossil-fired electric generating capacity additions, displacing existing non-renewable capacity requires policy incentives.
In OECD countries, where more policy initiatives affect electric generation, demand growth is met primarily with renewables, which also displace some existing generation.
On the other hand, growth in non-OECD electricity demand is met by a mix of renewables and non-renewable generating technologies, generally influenced by regional resource and economic considerations.

## Slide 95: India’s rapidly growing electricity demand is met primarily with renewable generation—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 0.61848 | 1.0873 | 1.4618 | 1.7193 | 2.3578
Gas | 0.10649 | 0.051014 | 0.051954 | 0.094988 | 0.096051
Nuclear | 0.020483 | 0.04348 | 0.069337 | 0.10644 | 0.15085
Hydro | 0.11342 | 0.15561 | 0.24241 | 0.32389 | 0.32389
Wind | 0.01966 | 0.11249 | 0.30068 | 0.97202 | 1.418
Solar | 0.000113 | 0.068201 | 0.30518 | 0.70302 | 1.7768
Other | 0.037602 | 0.030821 | 0.030666 | 0.029433 | 0.043645
Net electricity generation by fuel, India
trillion kilowatthours
Share of net electricity generation, India
percent
history projections
other
solar
wind
hydroelectric
nuclear
natural gas
coal
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 618.4777 | 1087.3478 | 1461.7835 | 1719.2993 | 2357.8319
Gas | 106.4917 | 51.0143 | 51.9541 | 94.9883 | 96.051
Nuclear | 20.483 | 43.4803 | 69.3365 | 106.4397 | 150.8475
Hydro | 113.42 | 155.6105 | 242.4105 | 323.8938 | 323.8938
Wind | 19.66 | 112.4947 | 300.6835 | 972.0226 | 1418.0156
Solar | 0.113 | 68.2012 | 305.1796 | 703.0176 | 1776.8263
Other | 37.6024 | 30.8208 | 30.6663 | 29.4327 | 43.6453

## Slide 96: —leading to a large decrease in the coal’s share of the generation mix
With a 4.6% average annual growth in electricity demand between 2018 and 2050, India’s growth rate surpasses all other regions in the Reference case.
The increase in electricity demand is largely met with generation from wind and solar technologies. Combined, wind and solar generation increase from less than 10% of the generation mix in 2018 to more than 50% in 2050.
Growth in fossil-fired generation supplements the growth in intermittent renewables (solar and wind), and about 70% of the new generation comes from renewables.
Although coal-fired generation more than doubles throughout the projection period, the share of electricity generation from coal falls from 73% in 2018 to 38% in 2050.

## Slide 97: OECD Europe adds renewable generation faster than its electricity demand grows—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 0.84875 | 0.3677 | 0.25791 | 0.23369 | 0.22841
Gas | 0.82701 | 0.76409 | 0.58123 | 0.63382 | 0.64424
Nuclear | 0.87167 | 0.7649 | 0.71065 | 0.67489 | 0.67585
Hydro | 0.55323 | 0.66684 | 0.83071 | 0.86143 | 0.88595
Wind | 0.15038 | 0.50327 | 0.79416 | 1.0009 | 1.2499
Solar | 0.023319 | 0.30445 | 0.71082 | 0.97353 | 1.233
Other | 0.23542 | 0.17171 | 0.091469 | 0.091011 | 0.099492
Net electricity generation by fuel, OECD Europe
trillion kilowatthours
Share of net electricity generation, OECD Europe
percent
history projections
other
solar
wind
hydroelectric
nuclear
natural gas
coal
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 0.84875 | 0.3677 | 0.25791 | 0.23369 | 0.22841
Gas | 0.82701 | 0.76409 | 0.58123 | 0.63382 | 0.64424
Nuclear | 0.87167 | 0.7649 | 0.71065 | 0.67489 | 0.67585
Hydro | 0.55323 | 0.66684 | 0.83071 | 0.86143 | 0.88595
Wind | 0.15038 | 0.50327 | 0.79416 | 1.0009 | 1.2499
Solar | 0.023319 | 0.30445 | 0.71082 | 0.97353 | 1.233
Other | 0.23542 | 0.17171 | 0.091469 | 0.091011 | 0.099492

## Slide 98: —as environmental policies contribute to retiring fossil-fired generators
Similar to many of the OECD regions, OECD Europe electricity demand growth averages about 1% annually throughout the projection period.
Without policy incentives, the low demand growth could limit the potential for additional renewables generation. However, a CO2 cap in OECD Europe reduces generation from carbon-intensive coal and natural gas and facilitates the growth in wind and solar generation from 20% of the generation mix in 2018 to almost 50% of the generation mix in 2050.
During that same period, the fossil-fired generation share is reduced by more than half, from about 38% of the generation mix in 2018 to 18% in 2050.

## Slide 99: In non-OECD Europe and Eurasia, lower demand growth limits the growth of renewables generation—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 0.20949 | 0.16434 | 0.12523 | 0.11907 | 0.12218
Gas | 0.1435 | 0.15576 | 0.18338 | 0.23534 | 0.25483
Nuclear | 0.11117 | 0.11745 | 0.14401 | 0.14975 | 0.15952
Hydro | 0.14145 | 0.14287 | 0.15757 | 0.1676 | 0.18166
Wind | 0.001455 | 0.02075 | 0.02111 | 0.021496 | 0.023045
Solar | 2.75e-05 | 0.011507 | 0.013057 | 0.019066 | 0.042552
Other | 0.015477 | 0.014446 | 0.018301 | 0.021446 | 0.026963
Net electricity generation by fuel, other non-OECD Europe and Eurasia
trillion kilowatthours
Share of net electricity generation, other non-OECD Europe and Eurasia
percent
other
solar
wind
hydroelectric
nuclear
natural gas
coal
history projections
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 209.486 | 164.3444 | 125.2342 | 119.0663 | 122.1838
Gas | 143.5022 | 155.765 | 183.3796 | 235.3352 | 254.8294
Nuclear | 111.173 | 117.4498 | 144.0092 | 149.7469 | 159.516
Hydro | 141.4468 | 142.8744 | 157.5686 | 167.6016 | 181.6608
Wind | 1.455 | 20.7504 | 21.1104 | 21.4959 | 23.0453
Solar | 0.0275 | 11.5065 | 13.0573 | 19.0658 | 42.5521
Other | 15.4771 | 14.4455 | 18.3013 | 21.4456 | 26.9633

## Slide 100: —with fewer policy drivers to change the generation mix
With demand growth less than 1% and no significant policies aimed at reducing CO2 emissions, the mix of generation resources in non-OECD Europe and Eurasia (excluding Russia) changes relatively little.
Hydroelectric remains the main source of renewables generation in the region, and wind and solar account for less than 10% of the generation mix in 2050.
With natural gas resources available in surrounding areas, non-OECD Europe and Eurasia (excluding Russia) displaces some of its coal-fired generation with natural gas-fired generation throughout the projection period. The coal-fired generation share decreases from 31% in 2018 to 15% in 2050, but the natural-fired gas generation share increases from 23% in 2018 to 31% in 2050.

## Slide 101: South Korea increases generation from renewables based on demand growth and related policies—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 0.20612 | 0.10578 | 0.10738 | 0.10151 | 0.090929
Gas | 0.096993 | 0.19162 | 0.16179 | 0.17164 | 0.19495
Nuclear | 0.14189 | 0.19593 | 0.22761 | 0.21612 | 0.21612
Hydro | 0.003632 | 0.003442 | 0.003442 | 0.003442 | 0.003442
Wind | 0.000817 | 0.036643 | 0.077776 | 0.097289 | 0.1168
Solar | 0.000772 | 0.020902 | 0.07816 | 0.14871 | 0.17788
Other | 0.018906 | 0.010803 | 0.0083619 | 0.0082726 | 0.053117
Net electricity generation by fuel, South Korea
trillion kilowatthours
Share of net electricity generation, South Korea
percent
history projections
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 206.1194 | 105.7824 | 107.3827 | 101.5062 | 90.9287
Gas | 96.993 | 191.6164 | 161.7872 | 171.6438 | 194.9502
Nuclear | 141.89 | 195.9267 | 227.6081 | 216.1163 | 216.1163
Hydro | 3.632 | 3.442 | 3.442 | 3.442 | 3.442
Wind | 0.817 | 36.6434 | 77.7759 | 97.2887 | 116.8015
Solar | 0.772 | 20.902 | 78.1603 | 148.7057 | 177.8831
Other | 18.9059 | 10.8033 | 8.3619 | 8.2726 | 53.117
other
solar
wind
hydroelectric
nuclear
natural gas
coal

## Slide 102: ―and non-renewable technologies grow as well
South Korea’s electricity demand is growing faster than most other OECD countries, with an annual average growth rate of 1.4% per year.
Despite high electricity demand growth, a national CO2 cap contributes to a shift from coal to lower emitting nuclear, natural gas, and renewable resources. The share of coal-fired generation decreases from 37% of the electricity generation mix in 2018 to 11% by 2050.
The decrease in coal generation allows gas (82 billion kWh) and renewables (315 billion kWh) generation growth combined to exceed demand growth (307 billion kWh) during the projection period.
Although current policy calls for a gradual phase-out of generation from nuclear plants, they play a continued role in the electric power sector in the region, accounting for 25% of electricity generation in South Korea in 2050.

## Slide 103: Policies lead coal-fired generation to peak in China —
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 3.0453 | 4.3823 | 4.1085 | 3.8392 | 3.7553
Gas | 0.073379 | 0.19219 | 0.45384 | 0.81119 | 0.95573
Nuclear | 0.070962 | 0.33137 | 0.55839 | 0.8391 | 1.1198
Hydro | 0.70427 | 1.3593 | 1.5556 | 1.5556 | 1.5556
Wind | 0.044622 | 0.52236 | 1.1268 | 1.8811 | 2.2692
Solar | 0.0007 | 0.50486 | 1.4991 | 2.1988 | 3.1897
Other | 0.047997 | 0.012777 | 0.0096674 | 0.013887 | 0.05211
Net electricity generation by fuel, China
trillion kilowatthours
Share of net electricity generation, China
percent
other
solar
wind
hydroelectric
nuclear
natural gas
coal
history projections
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Coal | 3045.3218 | 4382.3262 | 4108.54 | 3839.1602 | 3755.3253
Gas | 73.3792 | 192.1891 | 453.8404 | 811.194 | 955.728
Nuclear | 70.962 | 331.3728 | 558.3933 | 839.0987 | 1119.8042
Hydro | 704.269 | 1359.3473 | 1555.5635 | 1555.5635 | 1555.5635
Wind | 44.622 | 522.3583 | 1126.8382 | 1881.0684 | 2269.2216
Solar | 0.7 | 504.8565 | 1499.0597 | 2198.841 | 3189.7111
Other | 47.9966 | 12.7766 | 9.6674 | 13.8873 | 52.1103

## Slide 104: —while demand growth is met predominantly by renewables
Average annual electricity demand in China grows more than 6% from 2010 until 2020, but then it slows to a little more than 2% until 2030 before falling to less than 2% from 2030 to 2050.
The slowing demand growth and the goal of limiting CO2 emissions growth by 2030 also contribute to coal-fired generation peaking in 2025.
As electricity demand continues to grow, albeit at a slower pace than in the early 2000s, renewable sources provide an increasing share of electricity generation and capacity. The electricity generation share of wind and solar grows from 12% in 2018 to 42% in 2050.

## Slide 105: Coal

## Slide 107: In most regions, coal production and consumption are projected to remain near current levels in the Reference case—
World coal production
billion short tons
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Australia and New Zealand | 569.7 | 567.1 | 593.3 | 625.7 | 661.3 | 651.8 | 645.4 | 560.4 | 562.7 | 572 | 580.3 | 584 | 586 | 590.2 | 597 | 602.5 | 603.9 | 606.4 | 609.6 | 615.7 | 620 | 626.1 | 630.6 | 635.8 | 641.7 | 648.3 | 654.4 | 659.8 | 675.5 | 681.9 | 689.6 | 712.7 | 736.8 | 751.8 | 765.6 | 780.1 | 795.2 | 819 | 838.9 | 858.8 | 888.3
OECD Europe | 601.9 | 620.6 | 628.2 | 592 | 574.1 | 551.9 | 527.6 | 490.2 | 441.9 | 385 | 334.7 | 330.6 | 325.4 | 314.3 | 303.9 | 294.5 | 289.1 | 284.1 | 278.4 | 273.8 | 269 | 267.5 | 265.3 | 263.4 | 261.3 | 259.9 | 259.6 | 258.8 | 258.4 | 257.9 | 257.4 | 256.6 | 256.2 | 255.3 | 255 | 254.2 | 254.3 | 254.2 | 254.5 | 255.2 | 255.3
United States | 1084.4 | 1095.6 | 1016.5 | 984.8 | 1000 | 896.9 | 728.4 | 793.5 | 774.6 | 740.6 | 701.3 | 686.4 | 682.2 | 683.2 | 689.6 | 690 | 684.2 | 678.4 | 676 | 681.9 | 682.1 | 672.7 | 656.8 | 656.9 | 650.1 | 648.8 | 648.1 | 644.3 | 643.5 | 642.6 | 642.8 | 639.6 | 638.1 | 636.1 | 638.3 | 638.7 | 637.9 | 633 | 634.1 | 635.1 | 635.5
rest of world | 1033.7 | 1071.3 | 1123 | 1128.3 | 1112 | 1108.1 | 1113.7 | 987.6 | 993.3 | 965.5 | 953.1 | 943.3 | 940.7 | 946.2 | 949.1 | 952.6 | 954.2 | 958 | 959.9 | 964.1 | 968.1 | 980.7 | 993 | 1006.1 | 1019.2 | 1033.2 | 1046.9 | 1060.3 | 1063 | 1076.5 | 1089.2 | 1101.1 | 1113.3 | 1135.7 | 1153.8 | 1169.2 | 1192.5 | 1224 | 1255.6 | 1285.9 | 1310.4
Other non-OECD Asia | 508 | 604.8 | 646.6 | 674 | 650.1 | 651 | 664.8 | 706.4 | 693.3 | 719.9 | 730.6 | 741 | 751.9 | 759 | 766.5 | 774.6 | 793.5 | 812.6 | 833.1 | 854.1 | 874.6 | 881.2 | 887.1 | 894 | 899.9 | 906.3 | 916.7 | 928.5 | 940.4 | 951.7 | 963.3 | 974.1 | 984.6 | 994.4 | 1009.3 | 1032.6 | 1060 | 1077.5 | 1094.3 | 1111.5 | 1128.9
China | 3779.2 | 4149.6 | 4348.8 | 4380.9 | 4270.3 | 4129.9 | 3708.2 | 3900.4 | 3898.1 | 3873.1 | 3870.1 | 3829.3 | 3793.4 | 3761.8 | 3731.5 | 3700.4 | 3643.2 | 3590.8 | 3539 | 3489.2 | 3441.6 | 3407.9 | 3373.6 | 3342.9 | 3311.7 | 3284.7 | 3274.5 | 3265.1 | 3255.7 | 3250.6 | 3242.3 | 3240.8 | 3238.5 | 3240 | 3242.6 | 3245.7 | 3247.1 | 3246 | 3246.6 | 3245.4 | 3243.5
India | 578.2 | 590.8 | 680.6 | 671.4 | 713.5 | 747.1 | 761.7 | 852.3 | 853.6 | 853.6 | 859.8 | 881.4 | 902.9 | 928.2 | 955 | 983.6 | 1023.8 | 1066.9 | 1110.8 | 1155.5 | 1200.1 | 1245.3 | 1290.3 | 1336.1 | 1381.2 | 1426.7 | 1446.1 | 1464.4 | 1484.3 | 1502.9 | 1523.9 | 1563.9 | 1604.8 | 1643.3 | 1681.9 | 1717.5 | 1778.3 | 1836.1 | 1894.4 | 1951.7 | 2006.9
history projections
World coal consumption
billion short tons
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Other OECD | 568.8555 | 569.7139 | 569.8547 | 574.0244 | 563.622 | 572.216 | 565.1024 | 552.0477 | 518.2914 | 482.6808 | 448.1194 | 445.6591 | 443.2177 | 440.8702 | 437.6173 | 434.1346 | 430.3734 | 427.2083 | 424.0862 | 421.2551 | 418.2454 | 418.0472 | 417.5778 | 417.3555 | 416.9448 | 416.7688 | 414.4223 | 411.946 | 409.5225 | 407.2015 | 404.9174 | 407.7726 | 410.6279 | 413.5761 | 416.511 | 419.6188 | 422.8948 | 426.3012 | 429.6851 | 432.8601 | 436.2719
OECD Europe | 837.8759 | 865.3892 | 894.9438 | 851.1486 | 825.3621 | 803.0708 | 765.0086 | 672.4022 | 614.3484 | 552.1094 | 495.7968 | 485.606 | 475.1121 | 464.3837 | 454.4583 | 445.5084 | 439.3975 | 434.0328 | 428.346 | 423.024 | 417.5551 | 415.4974 | 412.6197 | 410.1297 | 407.4479 | 405.475 | 404.5147 | 403.6683 | 402.6951 | 401.6288 | 400.5943 | 399.7573 | 399.2136 | 398.1862 | 397.252 | 396.3972 | 396.3249 | 396.1679 | 396.2483 | 396.3391 | 396.301
United States | 1047.1999 | 1001.4933 | 887.0268 | 921.3645 | 915.1117 | 794.6538 | 727.5871 | 707.2734 | 677.0614 | 646.7175 | 612.6961 | 591.514 | 586.2632 | 586.3712 | 591.6896 | 589.213 | 582.3775 | 576.4362 | 573.6256 | 582.8415 | 584.4539 | 575.8623 | 559.5971 | 559.5823 | 552.8792 | 551.6229 | 551.4031 | 547.6152 | 546.8195 | 545.9518 | 546.1632 | 542.8976 | 541.4884 | 539.4184 | 540.0655 | 542.0051 | 540.9185 | 541.4446 | 542.6045 | 542.829 | 543.3083
Other non-OECD | 792.9874 | 838.2885 | 847.8461 | 804.47 | 779.6726 | 796.5113 | 788.1223 | 691.5046 | 682.892 | 670.5189 | 661.725 | 662.0393 | 661.9483 | 662.6311 | 662.6972 | 662.9278 | 663.7626 | 664.8073 | 665.449 | 667.1084 | 668.711 | 676.9322 | 683.9562 | 691.4883 | 698.956 | 707.3095 | 715.1265 | 722.574 | 729.5499 | 737.0069 | 744.146 | 750.2961 | 756.7262 | 763.1079 | 769.5992 | 776.2634 | 787.8424 | 799.3301 | 810.8633 | 821.8075 | 832.1999
Other non OECD Asia | 305.4142 | 310.0623 | 316.6792 | 323.4082 | 344.7349 | 364.6104 | 387.9815 | 414.0971 | 438.5706 | 458.3821 | 481.0397 | 491.8485 | 501.3366 | 510.3965 | 519.9745 | 530.3494 | 546.7155 | 564.5685 | 582.3765 | 600.6901 | 618.5894 | 622.7684 | 626.3646 | 630.8711 | 634.4333 | 638.5205 | 648.0398 | 657.5348 | 667.284 | 676.7962 | 686.6742 | 698.9535 | 710.9832 | 722.5524 | 734.4617 | 746.0204 | 765.7073 | 785.7179 | 804.5326 | 823.677 | 843.8205
China | 3847.1529 | 4287.5573 | 4538.5069 | 4678.4896 | 4537.2567 | 4376.3262 | 4170.6388 | 4184.8171 | 4194.4121 | 4191.4239 | 4200.4822 | 4153.5461 | 4113.5954 | 4080.5129 | 4049.9024 | 4018.7867 | 3960.1222 | 3906.0016 | 3852.5233 | 3801.5015 | 3752.291 | 3716.8653 | 3681.0439 | 3648.7338 | 3616.1745 | 3587.5676 | 3576.6092 | 3566.4272 | 3556.2697 | 3550.3404 | 3541.3483 | 3540.861 | 3539.4548 | 3541.8024 | 3544.7261 | 3548.9516 | 3550.1708 | 3549.6807 | 3550.6106 | 3548.5704 | 3547.5633
India | 684.5657 | 724.6154 | 856.4022 | 879.8647 | 962.6125 | 980.9413 | 966.2887 | 1068.7158 | 1091.9214 | 1107.9728 | 1130.1292 | 1165.8117 | 1201.0865 | 1237.6888 | 1276.3122 | 1317.221 | 1369.0447 | 1424.1739 | 1480.4527 | 1537.8907 | 1595.7347 | 1655.5161 | 1715.6021 | 1777.0669 | 1838.2852 | 1900.6613 | 1936.2711 | 1971.3952 | 2008.5695 | 2045.0888 | 2084.6842 | 2148.2778 | 2213.7184 | 2278.0481 | 2343.8623 | 2408.902 | 2501.3619 | 2591.2306 | 2683.9633 | 2777.4165 | 2869.3448

## Slide 108: —with long-term growth expected in India and non-OECD Asia
Worldwide coal production holds steady at about 8 billion short tons, or 160 quadrillion British thermal units (Btu), per year through 2040. Increased coal use in India and other Asian countries that are not part of the Organization of Economic Cooperation and Development (OECD) helps drive consumption to more than 9 billion short tons (175 quadrillion Btu) by 2050.
In the Reference case, India increases its annual coal production by 2.7% per year from 850 million short tons in 2018 to 2 billion short tons by 2050 to help meet growing domestic demand. India’s coal consumption grows by an average of 3.1% per year, from 1.1 billion short tons (17 quadrillion Btu) in 2018 to 2.9 billion short tons (46 quadrillion Btu) in 2050.
China remains the largest producer and the largest user of coal, consuming about 3.5 billion short tons (74 quadrillion Btu) in 2050 after peaking at 4.7 billion short tons (nearly 95 quadrillion Btu) in 2013.
In OECD countries, coal consumption decreases by 2.5% per year from 2018 to 2025, before remaining relatively constant throughout the remainder of the projection period.

## Slide 109: India is the world’s largest importer of coal in 2050 in the Reference case—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
OECD Europe | 166 | 168.6 | 155.9 | 150.5 | 150.5
Japan | 207.7 | 201.6 | 183.3 | 170.9 | 169.5
South Korea | 131.7 | 105.9 | 112.8 | 120.5 | 136.7
China | 179.6 | 278.9 | 261.5 | 250.4 | 244.5
Other non-OECD Asia | 173.7 | 253.6 | 307.6 | 357.3 | 458.8
India | 122.2 | 270.3 | 395.6 | 560.8 | 862.4
Rest of World | 94.1 | 128.6 | 142.9 | 157.8 | 174.5
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Australia | 331.7 | 396 | 458.4 | 540.4 | 715.3
United States | 81.7 | 96.1 | 101.6 | 101.4 | 94.3
Africa | 74.2 | 86.8 | 106.3 | 120.4 | 175.9
Other non-OECD America | 80.5 | 91.8 | 99.2 | 115.2 | 140.2
Eurasia | 81.3 | 185.2 | 181.2 | 206.7 | 270.5
Other non-OECD Asia | 361.2 | 503.1 | 563.6 | 633.9 | 743.9
Rest of world | 85.3 | 50.2 | 50.9 | 51.8 | 58.4
Coal imports
billion short tons
Coal exports
billion short tons

## Slide 110: —and Australia and Indonesia remain the largest exporters
World coal trade is projected to grow from 2018 to 2050 at an average rate of 1.4% per year, totaling 2.2 billion short tons by 2050.
Increasing coal demand in the Asian economies is driving growth in coal trade. India coal imports grow by 4.1% per year, China coal imports remain relatively constant, and the remaining countries in non-OECD Asia increase imports by 1.8% per year.
Metallurgical coal trade increases gradually as industrial consumption shifts to India and other countries that have limited or no metallurgical coal production.
In contrast to Asia, coal imports to the Americas—largely the United States and the other non-OECD America region – grow slowly through 2050..
The Australia and New Zealand region continues to be the world’s top coal exporter, followed by other non-OECD Asia, which is predominantly accounted for as Indonesia. By 2050, Australia accounts for 33% of global coal exports, and other non-OECD Asia accounts for nearly 35% of global coal exports.

## Slide 111: In the Reference Case, China decreases its coal use in the first half of the projection period—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
industrial | 39.8948 | 37.6057 | 32.9039 | 31.5907 | 32.7566
electric power | 34.264 | 46.2664 | 42.1027 | 39.3547 | 38.5341
buildings | 3.6564 | 3.3908 | 2.9455 | 2.6244 | 2.4082
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
series0 | 3.7792 | 3.8701 | 3.4416 | 3.2423 | 3.2435
series1 | 0.1796 | 0.2789 | 0.2615 | 0.2504 | 0.2445
Coal consumption in China
quadrillion British thermal units
Coal supply in China
billion short tons
history projections

## Slide 112: —but continues to consume coal despite policies encouraging nuclear and renewable energy use
Coal’s share of China’s electricity generation decreases from 64% in 2018 to 30% in 2050. In 2050, electricity generation is projected to account for 39 quadrillion Btu of coal, while renewables, nuclear, and natural gas account for 73, 12, and 7 quadrillion Btu, respectively.
Projected coal consumption in China for uses other than electricity generation falls from 43 quadrillion Btu in 2018 to 35 quadrillion Btu in 2050 as a result of the decreasing use of both steam and metallurgical coal in industrial boilers and steel manufacturing.
In 2050, China remains the largest consumer and producer of coal in the world, with coal consumption of 74 quadrillion Btu and coal production of 3.1 Billion short tons (69.2 quadrillion Btu). Production of coal decreases as consumption decreases.
China continues to produce 93% of coal needs and import about 7% of its coal demand through 2050.

## Slide 113: India’s use of coal in the Reference case increases throughout the projection period—
Coal consumption by sector, India
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
buildings | 0.23677 | 0.30836 | 0.3846 | 0.46741 | 0.5532
industrial | 4.4794 | 6.4491 | 9.7166 | 14.8302 | 21.5429
electric power | 6.3612 | 11.3371 | 15.4482 | 18.0803 | 23.845
Chart: 
| 2010 | 2020 | 2025 | 2040 | 2050
Petroleum | 0.080906 | 0.043792 | 0.043758 | 0.044439 | 0.043805
Nuclear | 0.25066 | 0.46365 | 0.55391 | 1.135 | 1.6086
Gas | 1.051 | 0.33563 | 0.45965 | 0.64201 | 0.63951
Coal | 6.3612 | 11.3371 | 12.9851 | 18.0803 | 23.845
Renewables | 1.4426 | 3.723 | 5.6404 | 20.7321 | 36.4402
Power sector energy consumption by fuel, India
quadrillion British thermal units
renewables
coal
natural gas
nuclear
liquids
history projections

## Slide 114: —but its share of the country’s power sector consumption declines
In 2018, India was the world’s second-largest coal consumer after China, consuming more than 17 quadrillion Btu. Sustained industrial growth and significant efforts to further electrify the country’s rural areas are expected to continue to drive India’s coal consumption growth.
In the power sector, coal consumption increases by 2.5% per year between 2018 and 2050 but it is outpaced by renewables consumption, which grows by 8.1% per year during the same period. By 2050, power sector coal consumption is 24 quadrillion Btu, and renewables consumption reaches 36 quadrillion Btu.
Strong growth in industrial applications leads projected industrial consumption to increase from 6 quadrillion Btu in 2018 to 22 quadrillion Btu in 2050.

## Slide 115: Petroleum and other liquids

## Slide 117: World petroleum and other liquid fuels consumption increases more than 20% in the Reference case—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Commercial | 3.7769 | 3.7035 | 3.598 | 3.6885 | 3.5238 | 3.8887 | 3.8668 | 3.9743 | 3.9369 | 3.9504 | 3.9249 | 3.8688 | 3.8483 | 3.8452 | 3.8515 | 3.8461 | 3.8588 | 3.8645 | 3.8863 | 3.9007 | 3.9303 | 3.9504 | 3.9675 | 3.9775 | 4.0003 | 4.0197 | 4.0398 | 4.057 | 4.0683 | 4.0979 | 4.1174 | 4.1416 | 4.1547 | 4.1872 | 4.2016 | 4.2268 | 4.2367 | 4.2672 | 4.2931 | 4.3118 | 4.336
Residential | 8.9839 | 8.6268 | 8.615 | 8.8185 | 8.7863 | 8.9399 | 8.7698 | 9.0494 | 8.8831 | 8.7678 | 8.651 | 8.5203 | 8.4534 | 8.4107 | 8.3842 | 8.3267 | 8.3208 | 8.3059 | 8.3051 | 8.2986 | 8.3058 | 8.3034 | 8.2911 | 8.279 | 8.2796 | 8.2762 | 8.272 | 8.2661 | 8.2497 | 8.2623 | 8.2563 | 8.257 | 8.2396 | 8.2452 | 8.2309 | 8.2274 | 8.2052 | 8.2128 | 8.21 | 8.2024 | 8.1974
Industrial | 58.4134 | 58.0442 | 59.208 | 58.8252 | 60.0855 | 61.1289 | 62.1488 | 61.7001 | 62.4094 | 62.635 | 63.1505 | 63.7584 | 64.0159 | 64.224 | 64.5173 | 65.1501 | 65.3077 | 65.9477 | 66.5104 | 67.1766 | 67.8527 | 68.595 | 69.1768 | 69.8122 | 70.3942 | 71.1488 | 71.7751 | 72.4995 | 73.2921 | 73.8128 | 74.4788 | 75.3088 | 76.0868 | 76.6902 | 77.4471 | 78.1609 | 78.9985 | 79.6959 | 80.5417 | 81.1075 | 81.9011
Transportation | 97.5161 | 99.1317 | 100.4013 | 102.3902 | 105.0579 | 108.0782 | 111.5867 | 112.6778 | 113.8648 | 114.9678 | 115.7829 | 116.5015 | 117.2766 | 117.8168 | 118.3346 | 118.7705 | 119.1608 | 119.4139 | 119.7096 | 119.918 | 120.1318 | 120.3411 | 120.6145 | 120.8469 | 121.2584 | 121.7737 | 122.4461 | 123.1245 | 123.8791 | 124.7092 | 125.5454 | 126.4871 | 127.4362 | 128.5821 | 129.6104 | 130.7059 | 131.7354 | 132.9321 | 134.1201 | 135.269 | 136.486
Petroleum and other liquids consumption
quadrillion British thermal units
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
OECD | 90.7423 | 89.6607 | 88.9316 | 88.4212 | 87.577 | 88.8403 | 89.851 | 91.1402 | 91.1997 | 91.4122 | 90.8334 | 90.3681 | 89.8349 | 89.1673 | 88.4659 | 87.8281 | 87.1393 | 86.6172 | 86.1513 | 85.6944 | 85.2623 | 84.8966 | 84.5083 | 84.1187 | 83.8229 | 83.6248 | 83.4981 | 83.4613 | 83.4792 | 83.4849 | 83.5833 | 83.7862 | 83.9694 | 84.1969 | 84.452 | 84.736 | 85.0712 | 85.4527 | 85.9104 | 86.18 | 86.5471
Non-OECD | 86.3711 | 88.4544 | 91.9734 | 94.1094 | 97.593 | 100.3957 | 102.4535 | 105.2371 | 107.707 | 109.9986 | 112.5104 | 113.8798 | 115.1609 | 116.33 | 117.6318 | 119.0981 | 120.2537 | 121.5857 | 122.8501 | 124.1116 | 125.3913 | 126.7163 | 127.9471 | 129.1847 | 130.485 | 131.9661 | 133.4254 | 134.9023 | 136.4572 | 137.8626 | 139.2987 | 140.9853 | 142.6163 | 144.2613 | 145.8849 | 147.5268 | 149.1649 | 150.8381 | 152.569 | 154.1421 | 155.9313
history projections

## Slide 118: —driven by non-OECD demand in the transportation and industrial sectors
Global liquid fuels demand increases more than 20% between 2018 and 2050, with total consumption reaching more than 240 quadrillion British thermal units (Btu) in 2050. Demand in countries in the Organization of Economic Cooperation and Development (OECD) remains relatively stable during the projection period, and non-OECD demand increases by about 45%.
Finished petroleum products such as motor gasoline, diesel, and jet fuel are increasingly consumed in the transportation sector. Other liquids are also consumed in large quantities, including natural gas plant liquids (NGPL) as an industrial feedstock.

## Slide 119: World petroleum and other liquid fuels consumption nearly doubles in non-OECD regions in the Reference case—
Non-OECD liquid fuels consumption
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Americas | 12.7834 | 13.495 | 13.9855 | 14.7291 | 15.7996
Europe and Eurasia | 9.846 | 11.7568 | 11.5499 | 11.489 | 11.7174
Africa | 7.1972 | 9.7245 | 11.5297 | 14.0917 | 17.8055
Middle East | 15.0415 | 18.532 | 20.0285 | 21.1512 | 22.951
Other Asia | 15.2148 | 18.6919 | 21.053 | 25.1672 | 30.9338
India | 6.5991 | 10.3625 | 14.1592 | 18.8749 | 22.903
China | 19.6891 | 29.9478 | 33.0855 | 33.7956 | 33.8209
China
India
other Asia
Middle East
Africa
Europe
and Eurasia
Americas
OECD liquid fuels consumption
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Americas | 46.121 | 47.506 | 44.6509 | 44.5385 | 46.9366
Europe | 29.3455 | 28.3985 | 26.0652 | 24.3401 | 24.0937
Asia | 15.2757 | 14.9289 | 14.5463 | 14.7047 | 15.5169
Asia
Europe
Americas
history projections

## Slide 120: —with most of the growth occurring in non-OECD Asia
Non-OECD countries account for nearly all growth in liquid fuels consumption between 2018 and 2050, as growing populations and expanding economies increasingly consume energy. Non-OECD liquid fuels consumption increases 45% during the projection period, growing from 108 quadrillion Btu in 2018 to 156 quadrillion Btu by 2050.
Non-OECD Asia accounts for about three-quarters of the global increase in liquid fuels consumption. India, in particular, experiences rapid industrial growth and increased demand for motorized transportation.
OECD liquid fuels demand declines slowly during the projection period; growth in demand is less than the reductions produced by efficiency improvements. Although liquid fuels demand in OECD Americas and OECD Asia is relatively unchanged between 2018 and 2050, liquid fuels consumption in OECD Europe falls by 4 quadrillion Btu, or 15% to 24 quadrillion Btu in 2050.

## Slide 121: Transportation remains the largest consumer of liquid fuels in the Reference case—
Refined petroleum and other liquids consumption by sector
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
ELECTRIC_POWER: liquids | 5.7041 | 3.7444 | 1.9409 | 1.1591 | 1.0771
Buildings | 6.0314 | 6.8107 | 6.8303 | 7.0472 | 7.2399
INDUSTRIAL.liquids | 32.6027 | 37.7197 | 41.4854 | 46.8002 | 52.707
TRANSPORTATION.liquids | 41.8125 | 57.8649 | 67.6797 | 75.6534 | 84.9003
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
ELECTRIC_POWER: liquids | 1.7105 | 1.1841 | 0.61057 | 0.4458 | 0.38155
Buildings | 6.7293 | 5.7652 | 5.4058 | 5.3265 | 5.2935
INDUSTRIAL.liquids | 25.8106 | 25.4307 | 26.3673 | 27.6786 | 29.1941
TRANSPORTATION.liquids | 55.7037 | 57.918 | 52.4521 | 49.892 | 51.5856
history projections

## Slide 122: —with significant growth in non-OECD countries
The transportation sector is responsible for more than half of liquid fuels demand in OECD and non-OECD countries in the Reference case. Growth in transportation liquid fuel consumption is concentrated in non-OECD countries, where consumption increases about 50% from 2018 to 2050, from 56 quadrillion Btu in 2018 to 85 quadrillion Btu in 2050.
The industrial sector consumes a considerable share of liquid fuels in OECD and non-OECD countries, accounting for about one-third of liquid fuels consumption by 2050. In this sector, liquid fuels serve as chemical feedstocks, provide process heat, and power equipment.
The buildings sector accounts for a similar share of liquid fuel consumption in OECD and non-OECD countries, accounting for about 5% of liquid fuels consumption by 2050. In this sector, liquid fuels are often used to provide space heat in areas where natural gas infrastructure is limited.
The electric power sector consumes a relatively small and declining share of liquid fuels, accounting for less than 1% of world consumption by 2050.

## Slide 123: World crude oil production rises nearly 30% in the Reference case, led by production increases in OPEC countries—
World petroleum and other liquid fuels production
million barrels per day
Chart: 
| 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
ngpl | 16.8942 | 17.2046 | 17.4084 | 17.7076 | 17.9117 | 17.9972 | 18.1067 | 18.1678 | 18.261 | 18.3514 | 18.4717 | 18.5714 | 18.6417 | 18.7471 | 18.8163 | 18.9144 | 18.949 | 18.9994 | 19.099 | 19.1473 | 19.2383 | 19.325 | 19.3829 | 19.476 | 19.5658 | 19.6265 | 19.7374 | 19.8117 | 19.9317 | 19.9918 | 20.108 | 20.2126 | 20.3142
non-OPEC | 47.9982 | 49.6555 | 51.1897 | 50.845 | 52.1759 | 53.5933 | 52.1077 | 53.0009 | 52.8118 | 52.3884 | 52.0001 | 51.616 | 51.9036 | 52.4658 | 52.6844 | 52.8462 | 53.4703 | 54.0463 | 54.0159 | 54.5036 | 55.0178 | 55.8237 | 56.0131 | 56.8508 | 57.022 | 57.3462 | 57.0242 | 57.0767 | 58.3113 | 58.0039 | 57.7194 | 58.5551 | 59.0839
OPEC | 34.8553 | 33.5717 | 33.0953 | 32.0194 | 32.945 | 33.6387 | 35.3754 | 36.3418 | 37.3689 | 38.5317 | 39.9772 | 40.7853 | 41.1457 | 41.5043 | 41.5598 | 41.4601 | 41.7974 | 41.9014 | 42.0184 | 42.2893 | 42.8517 | 42.5929 | 42.4376 | 42.5541 | 43.2031 | 44.0308 | 44.7973 | 45.7584 | 45.0317 | 46.3295 | 47.0155 | 47.6104 | 47.7016

## Slide 124: —but most production remains in non-OPEC countries
Members of the Organization of the Petroleum Exporting Countries (OPEC) and countries that are not members of OPEC produce increasing amounts of crude oil, lease condensate, natural gas plant liquids (NGPLs) and other liquid fuels from 2018 to 2050, reaching 127 million barrels per day (b/d) in 2050, or about 30% more than 2018 levels. During the projection period, crude and lease condensate production grows by 13 million b/d among OPEC members and 11 million b/d among non-OPEC producers, corresponding to increases of about 40% and 25%, respectively.
Non-OPEC countries produce slightly more than half of crude oil output through the projection period, accounting for 55% of global production in 2050.

## Slide 125: Crude oil production in OPEC countries increases 37% between 2018 and 2050 in the Reference case—
OPEC crude and lease condensate production by select regions
million barrels per day
Chart: 
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 26.776 | 25.8063 | 32.72 | 35.276 | 38.6463
Chart: North Africa
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 2.3005 | 2.398 | 2.3726 | 2.8007 | 3.0513
Chart: Central and West Africa
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 3.9528 | 4.1969 | 4.0131 | 1.791 | 0.47399
Chart: South America
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 1.8259 | 0.6941 | 2.0399 | 2.5698 | 5.53

## Slide 126: —with most of the production and growth occurring in the Middle East
OPEC crude oil and lease condensate production grows 37% between 2018 and 2050, from 35 million b/d in 2018 to 48 million b/d in 2050. OPEC continues to supply a large portion of the world market, accounting for over 40% of global oil supplies through the projection period.
OPEC crude oil and lease condensate production is largely concentrated in the Middle East, which increases from 27 million b/d in 2018 to 39 million b/d in 2050, a 44% increase. Production from large, low-cost oil resources in the Middle East remains a critical part of global crude oil supply during the projection period.
OPEC countries in North Africa and South America increase crude oil and lease condensate production but represent a smaller share of total OPEC growth. A net decrease in crude oil and lease condensate production occurs in Central and West Africa because of increasingly less cost-competitive onshore and offshore resources.

## Slide 127: Crude oil and lease condensate production in non-OPEC countries is highest in Russia and the United States in the Reference case—
Non-OPEC crude and lease condensate production by select regions
million barrels per day
Chart: Russia
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 10.7587 | 11.0076 | 11.0366 | 12.4173 | 13.0861
Chart: United States
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 10.9616 | 13.0967 | 13.7506 | 13.9455 | 12.1842
Chart: Canada
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 4.263 | 4.3706 | 4.6405 | 6.0565 | 9.6311
Chart: Brazil
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 2.5932 | 3.1417 | 3.6969 | 3.8232 | 4.1294

## Slide 128: —with considerable growth in Canada in the 2040s and 2050s.
Non-OPEC crude oil and lease condensate production grows 23% between 2018 and 2050, reaching 59 million b/d in 2050. These increases are driven by growth in Russia (22%), the United States (11%), Canada (126%), and Brazil (59%).
United States crude oil and lease condensate production increases from 11 million b/d in 2018 to approximately 14 million b/d from 2025 to 2040, driven by hydraulic fracturing of tight resources in the U.S. Southwest. Subsequent production falls to 12.2 million b/d by 2050, as development moves into less productive areas and well productivity declines. Nevertheless, 2050 production increases 11% from 2018 levels.
Russia’s 2.3 million b/d increase in production by 2050 comes mainly from non-tight resources, but the country also sees accelerated growth in tight oil production after 2030.
Canada’s 5.4 million b/d increase in production by 2050 is a result of oil sands development, particularly toward the end of the projection period, as easily accessible global resources are increasingly depleted and global oil prices gradually increase.
Brazil’s 1.5 million b/d increase in production by 2050 results from continued development of offshore pre-salt oil resources.

## Slide 129: Asian refineries process increasing volumes of crude oil in the Reference case—
Refinery throughput
million barrels per day
Chart: Americas
| 2018 | 2020 | 2025 | 2030 | 2040 | 2045 | 2050
Middle East | 26.9445 | 27.8371 | 27.3801 | 26.6323 | 27.2336 | 27.9429 | 29.0933
Chart: Europe, Middle East, Africa
| 2018 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Middle East | 32.0798 | 29.7846 | 28.3888 | 26.8698 | 27.1726 | 27.0216 | 29.129 | 30.2857
Chart: Asia
| 2018 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Middle East | 31.5798 | 34.3035 | 37.8848 | 41.4951 | 43.3978 | 46.274 | 48.3076 | 50.5711

## Slide 130: —to meet increasing Asian demand for petroleum products
Global refinery throughput grows throughout the projection period. The largest increases occur in Asia, where demand for finished petroleum products is greatest.
Refinery throughput in Asia increases by 60% between 2018 and 2050, from 32 million b/d in 2018 to 51 million b/d in 2050. Refinery runs increase to keep pace with regional demand, as developing economies industrialize and a growing middle class demands a larger amount of consumer goods.
In the Americas, refinery runs remain largely unchanged through the projection period, even as crude oil production increases.
Refinery throughput in Europe, the Middle East, and Africa decreases slightly through much of the projection period before an uptick in refinery buildout occurs between 2040 and 2050, which is driven by countries in Africa that demand increasing amounts of petroleum products.

## Slide 131: Natural gas

## Slide 133: World natural gas consumption increases more than 40% from 2018 to 2050 in the Reference case—
Chart: 
World natural gas consumption
quadrillion British thermal units
history projections

## Slide 134: —with growth in non-OECD countries outpacing OECD growth
Global natural gas consumption increases more than 40% between 2018 and 2050, and total consumption reaches nearly 200 quadrillion British thermal units (Btu) by 2050. Natural gas use accelerates the most in countries outside of the Organization of Economic Cooperation and Development (OECD) to meet demand from increased industrial activity, natural gas-fired electricity generation, and transportation fueled by liquefied natural gas (LNG).
Natural gas consumption in non-OECD countries grows from about 70 quadrillion Btu in 2018 to 120 quadrillion Btu in 2050, a 70% increase. During this time, the non-OECD share of global natural gas consumption increases from about 51% to 61%. In OECD countries, natural gas consumption increases 17% between 2018 and 2050, reaching 78 quadrillion Btu.

## Slide 135: Natural gas consumption increases across all sectors in the Reference case—
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Buildings | 18.9293 | 18.9153 | 18.9872 | 19.3905 | 19.9563
Transportation | 1.0082 | 1.497 | 2.769 | 3.575 | 4.6011
Power Generation | 18.382 | 23.788 | 22.384 | 23.7923 | 24.951
Industrial | 20.4126 | 24.2994 | 25.8805 | 27.1884 | 28.7801
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Buildings | 9.8822 | 11.8466 | 13.8019 | 15.8581 | 17.9001
Transportation | 2.8881 | 4.6548 | 8.9017 | 12.6339 | 17.701
Power Generation | 21.4099 | 23.5979 | 26.1964 | 33.3601 | 39.5884
Industrial | 26.8686 | 31.6439 | 35.3091 | 40.1976 | 46.3397
Natural gas consumption by sector
quadrillion British thermal units

## Slide 136: —and most of the growth occurs in the non-OECD industrial sector
In non-OECD countries, industrial sector natural gas consumption increases nearly 50%, from 32 quadrillion Btu in 2018 to 46 quadrillion Btu in 2050. Chemical and primary metals manufacturing, as well as oil and natural gas extraction, account for most of the growing demand.
Natural gas consumption for electricity generation in non-OECD countries increases more than 60%, at 1.5% per year, accounting for part of the 2.2% per year growth in electricity demand in those countries. In OECD countries, natural gas demand in the power sector grows at 0.3% per year, and electricity demand grows at 0.9% per year.
Consumption of natural gas in the transportation sector remains the smallest of the end-use sectors throughout the projection period, and yet this sector shows relatively strong growth in non-OECD countries. Increases in demand are driven mostly by LNG use to move freight (truck and rail).

## Slide 137: Natural gas consumption grows most in non-OECD Asian countries—
Non-OECD natural gas consumption
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Americas | 4.9568 | 4.8674 | 5.6935 | 6.6307 | 8.1467
Europe and Eurasia | 23.7619 | 21.9973 | 22.4868 | 24.1348 | 25.4495
Africa | 3.7491 | 5.3663 | 6.4678 | 8.2548 | 10.6283
Middle East | 13.8948 | 18.6714 | 21.5207 | 25.0394 | 29.4458
Other Asia | 8.0134 | 9.8249 | 11.6712 | 14.1099 | 16.7812
India | 2.4278 | 2.1596 | 3.2006 | 5.0729 | 7.4272
China | 3.938 | 8.5185 | 12.7129 | 18.1431 | 22.7143
China
India
other Asia
Middle East
Africa
Europe
and Eurasia
Americas
OECD natural gas consumption
quadrillion British thermal units
Chart: 
| 2010 | 2020 | 2030 | 2040 | 2050
Americas | 30.7226 | 38.8779 | 40.8055 | 43.323 | 46.028
Europe | 20.7736 | 20.2286 | 20.0778 | 21.1445 | 22.1134
Asia | 7.2358 | 9.3933 | 9.1374 | 9.4786 | 10.1472
Asia
Europe
Americas
history projections

## Slide 138: —driven by economic growth, and expanded use in the electric power generation and industrial sectors
Non-OECD Asia accounts for most of the growth in natural gas consumption from 2018 to 2050, growing to more than 45 quadrillion Btu and representing about 40% of all non-OECD consumption. The increase in natural gas consumption is driven by an expanding industrial sector (which uses natural gas as feedstock and as a source to produce process heat) and a growing use of natural gas for power generation.
Led by OECD Americas, OECD natural gas demand increases across all regions, reaching 78 quadrillion Btu in 2050, or nearly 20% higher than 2018 levels. The power sector accounts for most of the increase as relatively inexpensive natural gas displaces coal-fired electricity generation.

## Slide 139: The Middle East, United States, Russia, and non-OECD Asia lead natural gas production—
Natural gas production by select regions
trillion cubic feet
Chart: United States
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 29.4667 | 33.5519 | 38.4939 | 40.7163 | 43.4074
Chart: Russia
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 23.6918 | 25.713 | 28.4793 | 31.2605 | 33.5406
Chart: Non-OECD Asia
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 17.755 | 16.9096 | 17.5159 | 22.8473 | 26.8912
Chart: Canada
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 5.7305 | 5.7205 | 6.0218 | 7.1336 | 6.805
Chart: 
| 2018 | 2020 | 2030 | 2040 | 2050
Middle East | 21.8834 | 21.2996 | 24.1503 | 29.9213 | 36.8484

## Slide 140: shifting historical trade patterns toward satisfying increased Asian demand
The United States remains the world’s largest natural gas producer throughout the projection period, reaching 43 trillion cubic feet (Tcf) in 2050, a nearly 50% increase. U.S. shale resources production continues to expand in the Appalachian region and in tight oil formations in and around Texas.
Middle East natural gas production increases 15 Tcf from 2018 to 2050, reaching 37 Tcf in 2050, about a 70% increase. After 2030, countries in the Middle East increase production of low-cost, abundant hydrocarbon resources to meet growing demand worldwide.
Natural gas production in Russia increases about 40% during the projection period, reaching 34.0 Tcf in 2050, and most of the increase is exported to Asia and Europe.
Canada continues to produce relatively large amounts of natural gas, reaching 6.8 Tcf in 2050, a nearly 20% increase.

## Slide 141: Non-OECD Asia surpasses OECD Europe as the largest natural gas net importer by 2050 in the Reference case—
Net imports of natural gas
trillion cubic feet
Chart: 
| Americas | Europe | Australia and New Zealand | Japan and South Korea | Middle East | Europe and Eurasia | Africa | Asia
2020 | -2.4209 | 13.3984 | -3.366 | 6.1581 | -3.5681 | -9.341 | -3.5307 | 3.2498
2030 | -5.4157 | 14.7309 | -3.2917 | 6.1788 | -3.7017 | -12.5505 | -5.0435 | 9.2356
2040 | -6.4281 | 16.2794 | -3.7502 | 6.4379 | -6.1461 | -15.5107 | -4.8134 | 13.2337
2050 | -6.815 | 17.5124 | -4.1625 | 6.8216 | -8.8696 | -17.4773 | -6.0777 | 18.3726
OECD
non-OECD
2020 2030 2040 2050

## Slide 142: —which is mostly imported from the United States, the Middle East, and Russia
Despite strong growth in LNG trade, pipeline flows continue to account for most of the interregional natural gas trade during the projection period as pipeline infrastructure is further developed.
Non-OECD Europe and Eurasia (primarily Russia) remains the largest net exporter of natural gas in 2050, followed by the Middle East. During this time, OECD Europe increases its dependence on Russian pipeline natural gas, and non-OECD Asia imports a growing amount of LNG.
The Americas grow as a net exporter of natural gas, driven mostly by LNG shipments from the United States, to countries outside the region.

## Slide 143: Asian natural gas consumption grows faster than its production—
Chart: 
Natural gas consumption and production, Asia
trillion cubic feet

## Slide 144: —leading to increasing net natural gas imports during the projection period
Asia experiences the greatest growth in global natural gas consumption because the economies of countries such as China and India are rapidly expanding. Non-OECD natural gas demand in Asia increasingly outpaces regional supply, despite relatively large increases in natural gas production in China. As a result, net imports of natural gas to Asia (all countries) more than triple from 2018 to 2050.
China’s use of natural gas is expected to increase nearly 190% from 2018 to 2050, reaching 21.7 Tcf, while India increases natural gas consumption by more than 250%, reaching 7.0 Tcf. During the projection period, both countries expand industrial sectors as a growing middle class, growing GDPs, increasing natural gas generation, and growing populations all cause increasing demand for consumer goods.

## Slide 145: Natural gas fuels the oil and natural gas extraction industries—
Natural gas consumption for oil and gas extraction industries
quadrillion British thermal units
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Rest of World | 3.3239 | 3.2838 | 3.5129 | 3.6318 | 3.5537 | 3.5883 | 3.752 | 3.6684 | 3.7074 | 3.7522 | 3.8301 | 4.0631 | 4.042 | 4.0424 | 4.0288 | 3.9937 | 4.1723 | 4.0806 | 4.1167 | 4.0722 | 3.9892 | 4.0089 | 4.0994 | 4.2233 | 4.3854 | 4.552 | 4.5864 | 4.5964 | 4.4893 | 4.5844 | 4.7319 | 4.7177 | 4.8293 | 4.8737 | 4.9229 | 4.9226 | 4.9061 | 4.898 | 4.95 | 4.8738 | 5.0708
United States | 1.3183 | 1.3534 | 1.4307 | 1.5231 | 1.9842 | 1.9983 | 2.0238 | 2.0707 | 2.3172 | 2.5615 | 2.7363 | 2.8104 | 2.8525 | 2.9236 | 3.0004 | 3.0799 | 3.1708 | 3.2109 | 3.248 | 3.2666 | 3.2772 | 3.2943 | 3.3099 | 3.3142 | 3.3293 | 3.3394 | 3.3611 | 3.3722 | 3.3938 | 3.4086 | 3.4321 | 3.4277 | 3.4301 | 3.4215 | 3.4242 | 3.4177 | 3.4149 | 3.4063 | 3.4089 | 3.3977 | 3.3992
Canada | 0.9551 | 0.9476 | 1.0487 | 1.1435 | 1.1986 | 1.1801 | 1.2086 | 1.2716 | 1.3336 | 1.2895 | 1.3154 | 1.3053 | 1.2907 | 1.2943 | 1.3066 | 1.3248 | 1.3137 | 1.3221 | 1.3147 | 1.3328 | 1.2998 | 1.2937 | 1.2969 | 1.3127 | 1.3337 | 1.3597 | 1.3816 | 1.3821 | 1.4013 | 1.536 | 1.6772 | 1.6667 | 1.7173 | 1.7443 | 1.6824 | 1.7505 | 1.8843 | 1.9752 | 2.0777 | 2.2485 | 2.2593
Middle East | 0.658 | 0.6916 | 0.7401 | 0.7758 | 0.7854 | 0.859 | 0.939 | 0.94162 | 0.94676 | 1.2149 | 1.1798 | 1.3229 | 1.3307 | 1.3358 | 1.3556 | 1.4296 | 1.58 | 1.6434 | 1.7515 | 1.763 | 1.7623 | 1.7789 | 1.8296 | 1.8889 | 1.9361 | 1.896 | 1.899 | 1.9175 | 1.9301 | 1.9277 | 1.946 | 1.965 | 2.0394 | 2.1221 | 2.2034 | 2.2655 | 2.2828 | 2.3307 | 2.3559 | 2.3931 | 2.415
Eurasia | 0.7739 | 0.8066 | 0.7747 | 0.8285 | 0.851 | 0.9431 | 0.8941 | 0.90661 | 0.92665 | 0.94957 | 0.94106 | 0.93569 | 0.92984 | 0.93695 | 0.93149 | 0.9381 | 0.94798 | 0.96241 | 0.96823 | 1.0009 | 1.12 | 1.1481 | 1.0712 | 1.0629 | 1.0465 | 1.0471 | 1.0634 | 1.0772 | 1.1612 | 1.137 | 1.0884 | 1.1564 | 1.1144 | 1.1229 | 1.1294 | 1.1546 | 1.1633 | 1.1634 | 1.1864 | 1.204 | 1.2192
history projections

## Slide 146: —leading to regional consumption patterns that follow oil and natural gas production
Lease and plant fuel consumption of natural gas increases nearly 60% from 2018 to 2050, from 9 quadrillion Btu in 2018 to more than 14 quadrillion Btu in 2050. Energy requirements to power drilling operations, natural gas processing, and LNG liquefaction and regasification cause higher natural gas demand.
From 2018 to 2050, the United States, Canada, and the Middle East represent about half of the natural gas consumption associated with oil and natural gas extraction activities.
Liquefaction facilities consume an increasing share of lease and plant fuel demand as LNG terminal build out occurs in the United States, the Middle East, Russia, and other exporting regions.
In addition to lease and plant fuel, considerable quantities of natural gas are required to fuel the movement of natural gas through pipelines at compressor stations, amounting to 3.0 quadrillion British thermal units (quads) in 2018 and 3.6 quads in 2050.

## Slide 147: CO2

## Slide 149: Although population and incomes continue to rise in both OECD and non-OECD countries—
Chart: 
Chart: 
Chart: 
Chart: 
Population
billion people
Per capita gross domestic product
thousand dollars per person
Carbon intensity
metric tons CO2 per billion British thermal units
Energy intensity
thousand British thermal units per dollar

## Slide 150: —energy and carbon intensity are projected to continue to fall in the Reference case
Worldwide, the amount of energy used per unit of economic production (energy intensity) has declined steadily for many years. The amount of carbon dioxide (CO2) emissions per unit of energy consumption (carbon intensity) declined in OECD countries since 2008 and in non-OECD countries since 2014.
Energy intensity continues to decline in both OECD and non-OECD countries because of efficiency gains and gross domestic product (GDP) increases generated from low-energy-intensive services.
Carbon intensity continues to decline largely as a result of China and other countries’ move away from coal; worldwide growth in the use of non-CO2-emitting sources of energy, such as wind and solar; and improvements in process efficiencies.

## Slide 151: Reference case energy-related carbon dioxide emissions grow—
Energy-related carbon dioxide emissions
billion metric tons
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Total OECD | 13131.107 | 13015.1276 | 12837.9228 | 12951.6985 | 12816.4929 | 12716 | 12659.1222 | 12518.3395 | 12463.633 | 12275.6578 | 12033.3036 | 11941.039 | 11886.9813 | 11823.841 | 11762.425 | 11704.6056 | 11638.361 | 11579.3421 | 11532.9228 | 11497.3783 | 11445.3846 | 11414.0467 | 11373.5211 | 11353.8744 | 11336.8473 | 11332.3547 | 11334.7356 | 11331.6051 | 11330.48 | 11345.7249 | 11378.0002 | 11402.4744 | 11440.8323 | 11474.8025 | 11512.2178 | 11563.6849 | 11605.9199 | 11657.169 | 11709.1121 | 11753.671 | 11812.2024
Total Non-OECD | 19311.7472 | 20708.6234 | 21705.5011 | 22286.313 | 22541.1805 | 22545.1937 | 22371.0503 | 22584.0367 | 22856.278 | 23055.9282 | 23306.4542 | 23440.6512 | 23553.7214 | 23682.2734 | 23829.9601 | 23999.9209 | 24176.0154 | 24367.4646 | 24558.1305 | 24757.2188 | 24960.0455 | 25189.5572 | 25400.7533 | 25633.4576 | 25863.8981 | 26124.7737 | 26371.5376 | 26636.4944 | 26911.2556 | 27172.8755 | 27437.1892 | 27790.8295 | 28135.0355 | 28493.4955 | 28857.2243 | 29218.2617 | 29629.9735 | 30031.0698 | 30458.251 | 30854.885 | 31272.749
history projections

## Slide 152: —accelerating in later projection years in non-OECD countries
World energy-related CO2 emissions grow at an average rate of 0.6% per year between 2018 and 2050, compared with the average growth rate of 1.8% per year from 1990 to 2018.
In the near term, energy-related CO2 emission growth is slowed by increases in energy efficiency and a gradual shift from coal toward natural gas and renewable energy sources. In the longer term, broad population and economic growth leads to increased emissions.
In OECD countries, projected energy-related CO2 emissions decline slightly (-0.2% annually) through 2050 and are 14% lower than their 2005 levels in 2050 even as their economies gradually expand.
Energy-related CO2 emissions from non-OECD countries grow at a rate of about 1% per year from 2018 to 2050, slower than the related growth in energy consumption (1.6% per year).

## Slide 153: Energy-related carbon dioxide emissions grow from all three fossil fuel sources in the Reference case—
Energy-related carbon dioxide emissions
billion metric tons
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
Liquids CO2 | 11363.3801 | 11537.0157 | 11631.7971 | 11954.5003 | 12116.3589 | 12331.3927 | 12545.4942 | 12784.7044 | 12980.3132 | 13134.6315 | 13221.6368 | 13256.9586 | 13298.9437 | 13324.0565 | 13356.3149 | 13401.9883 | 13431.7659 | 13475.7082 | 13521.95 | 13564.8736 | 13611.1977 | 13665.4718 | 13714.6197 | 13762.1239 | 13823.6825 | 13897.0456 | 13980.5869 | 14069.8886 | 14163.777 | 14252.4361 | 14349.963 | 14469.2242 | 14583.576 | 14708.6177 | 14827.2065 | 14950.4794 | 15075.7554 | 15208.0761 | 15347.3328 | 15467.9287 | 15606.4107
Natural Gas CO2 | 6323.9237 | 6512.9897 | 6662.056 | 6760.0958 | 6785.6371 | 6887.3676 | 7032.4749 | 7153.8224 | 7298.1851 | 7333.9451 | 7387.3433 | 7463.8781 | 7513.1854 | 7559.3915 | 7601.8526 | 7665.8093 | 7770.8422 | 7863.3545 | 7957.6765 | 8041.3634 | 8120.3512 | 8232.5579 | 8341.9874 | 8452.6377 | 8565.4531 | 8685.7174 | 8788.3588 | 8904.7994 | 9020.0322 | 9136.1555 | 9261.9354 | 9388.2362 | 9518.979 | 9645.9909 | 9778.8148 | 9914.5213 | 10031.2323 | 10143.1031 | 10268.2489 | 10381.2928 | 10510.3041
Coal CO2 | 14755.5504 | 15673.7456 | 16249.5708 | 16523.4154 | 16455.6774 | 16042.4334 | 15452.2034 | 15163.8494 | 15041.4127 | 14863.0093 | 14730.7776 | 14660.8535 | 14628.5735 | 14622.6663 | 14634.2176 | 14636.7289 | 14611.7684 | 14607.744 | 14611.4267 | 14648.36 | 14673.8813 | 14705.5741 | 14717.6673 | 14772.5704 | 14811.6098 | 14874.3655 | 14937.3275 | 14993.4115 | 15057.9264 | 15130.0088 | 15203.291 | 15335.8436 | 15473.3128 | 15613.6893 | 15763.4208 | 15916.9459 | 16128.9056 | 16337.0596 | 16551.7813 | 16759.3344 | 16968.2367
history projections

## Slide 154: —and liquid fuels and coal emissions approach similar levels
Coal-related CO2 emissions are projected to increase at an average rate of 0.4% per year between 2018 and 2050, as coal use generally declines in OECD regions and China, but it accelerates after 2040 in India and other parts of non-OECD Asia.
Liquids-related CO2 emissions grow an average 0.6% per year from 2018 to 2050. Despite large increases in transportation demand, particularly in China and India, this change in emissions is lower than the 1.3% per year increase in liquids-related CO2 emissions that occurred from 1990 to 2018.
Natural gas CO2 emissions increase an average of 1.1% per year between 2018 and 2050. Even though the use of natural gas in electricity generation rises, the related emission growth rates are lower than the 2.2% per year increases seen from 1990 to 2018.

## Slide 155: Liquids-related carbon dioxide emissions remain flat or decline in OECD countries—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
United States | 2301.908 | 2254.639 | 2201.9901 | 2233.1283 | 2254.714 | 2299.3201 | 2327.2206 | 2343.4045 | 2392.9109 | 2401.8664 | 2330.3016 | 2293.6915 | 2277.0282 | 2247.7112 | 2215.9895 | 2187.1985 | 2164.4289 | 2143.1829 | 2128.2665 | 2108.3161 | 2088.6726 | 2076.0076 | 2063.0229 | 2050.0049 | 2042.5535 | 2030.0664 | 2024.0739 | 2026.0191 | 2026.1188 | 2026.5372 | 2029.0451 | 2032.7769 | 2035.8273 | 2044.3086 | 2051.3474 | 2059.5564 | 2070.833 | 2083.3951 | 2094.9726 | 2101.2704 | 2111.038
OECD Europe | 1996.5 | 1971.7 | 1907.1 | 1881.1826 | 1865.8212 | 1906.6248 | 1936.6932 | 1914.015 | 1910.6222 | 1917.3788 | 1924.1602 | 1913.6414 | 1898.2577 | 1880.3139 | 1863.3238 | 1848.2088 | 1831.4736 | 1815.3685 | 1798.8655 | 1782.557 | 1767.4106 | 1750.2956 | 1733.7336 | 1715.192 | 1699.8272 | 1687.2383 | 1675.5427 | 1663.986 | 1654.6891 | 1646.3068 | 1641.2826 | 1638.288 | 1635.2746 | 1632.9496 | 1629.2166 | 1627.0216 | 1624.3311 | 1623.8421 | 1626.3437 | 1624.9596 | 1624.5687
OECD Asia | 898 | 942 | 981 | 976.4442 | 950.0623 | 948.5287 | 949.304 | 935.8067 | 915.1009 | 900.1887 | 885.565 | 882.0529 | 878.1674 | 874.9516 | 871.3497 | 867.3086 | 862.6567 | 859.2302 | 856.9786 | 855.8241 | 855.7097 | 855.5939 | 854.9809 | 854.6044 | 855.0255 | 856.3003 | 858.3207 | 859.8818 | 860.84 | 862.7739 | 865.9648 | 870.7132 | 874.9888 | 880.4122 | 885.4135 | 890.7761 | 895.9597 | 901.7773 | 907.712 | 912.3359 | 917.8789
Non-OECD Europe and Eurasia | 649.5 | 693.6 | 718 | 722.6336 | 758.4264 | 745.18 | 756.6194 | 746.3194 | 761.3061 | 774.338 | 789.223 | 788.8965 | 787.9737 | 787.0911 | 786.7767 | 788.4907 | 787.0153 | 786.1387 | 783.9658 | 781.9461 | 779.4971 | 778.3739 | 776.5319 | 774.7075 | 773.7486 | 774.1785 | 774.9239 | 775.4287 | 776.0314 | 776.3204 | 776.6533 | 779.0973 | 781.0234 | 782.644 | 784.2276 | 786.9087 | 788.5105 | 789.8255 | 791.2519 | 792.6778 | 793.8983
China | 1160 | 1257 | 1306 | 1437.7102 | 1492.2939 | 1585.0404 | 1641.6 | 1729.3516 | 1798.3475 | 1853.6982 | 1909.5817 | 1940.55 | 1968.5315 | 1992.4595 | 2016.6339 | 2037.9091 | 2052.3831 | 2066.8651 | 2080.2898 | 2091.0679 | 2102.1133 | 2110.4802 | 2116.0718 | 2119.4778 | 2122.6048 | 2126.3282 | 2129.3907 | 2131.0394 | 2133.1784 | 2133.2401 | 2130.0127 | 2131.1861 | 2130.8839 | 2130.4423 | 2128.6913 | 2126.6095 | 2123.4525 | 2121.6461 | 2120.8308 | 2116.4407 | 2115.0897
India | 428 | 414 | 435 | 470.7943 | 481.0133 | 519.707 | 548.0955 | 594.7038 | 626.0036 | 655.0085 | 682.9683 | 704.3498 | 725.7757 | 748.3366 | 772.2639 | 798.0125 | 823.5855 | 851.515 | 879.9445 | 908.4558 | 938.7533 | 969.1111 | 999.7341 | 1030.5063 | 1061.6951 | 1093.9497 | 1126.3024 | 1157.762 | 1188.4126 | 1217.9916 | 1247.6742 | 1278.3022 | 1307.4781 | 1336.5738 | 1365.1571 | 1392.2237 | 1416.9828 | 1439.6585 | 1462.8089 | 1484.3055 | 1502.4601
Liquids-related carbon dioxide emissions for selected countries/regions
billion metric tons

## Slide 156: —but grow rapidly in India
CO2 emissions from liquid fuels, about half of which is used in transportation, decline in OECD countries as increases in energy efficiency offset increases in passenger and freight services.
China’s liquids-related CO2 emissions grow at a decreasing rate as growth in the country’s population slows. From 2030 to 2050, China and U.S. liquids-related CO2 emissions levels are similar.
India experiences continuous growth in liquids-related CO2 emissions as its economy expands, although it starts from a lower level. By 2030, India’s emissions exceed those in OECD Asia and non-OECD Europe and Eurasia; by 2050, they approach those of OECD Europe.

## Slide 157: Natural gas has the greatest carbon dioxide emissions growth in the Reference case—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
United States | 1291.5453 | 1311.4229 | 1371.56 | 1409.3552 | 1439.5257 | 1482.9838 | 1496.3668 | 1473.596 | 1587.278 | 1600.1191 | 1635.5963 | 1646.2027 | 1661.8867 | 1668.8367 | 1670.2186 | 1685.9287 | 1703.0394 | 1711.7532 | 1724.0568 | 1718.9339 | 1718.3067 | 1728.6731 | 1748.6615 | 1750.961 | 1757.4185 | 1764.5131 | 1770.834 | 1777.2342 | 1784.9494 | 1789.5265 | 1801.2605 | 1807.9774 | 1819.4903 | 1825.3412 | 1836.1092 | 1850.1954 | 1855.5007 | 1860.5614 | 1872.7557 | 1879.2935 | 1889.0315
OECD Europe | 1102.1799 | 1016.0881 | 980.9453 | 979.0219 | 897.2234 | 928.2791 | 985.1241 | 1059.4167 | 1063.5934 | 1067.4539 | 1071.422 | 1074.4651 | 1075.6009 | 1078.3366 | 1082.5871 | 1088.1848 | 1083.9034 | 1080.6029 | 1074.6019 | 1070.1157 | 1063.4339 | 1068.9479 | 1072.2322 | 1078.8558 | 1086.8064 | 1096.3681 | 1101.8915 | 1105.7998 | 1106.4431 | 1113.525 | 1119.9358 | 1124.9616 | 1131.4454 | 1135.1485 | 1138.773 | 1143.26 | 1149.6118 | 1154.6355 | 1159.3016 | 1163.8767 | 1171.2502
OECD Asia | 383.9087 | 426.1768 | 446.963 | 452.0279 | 445.0282 | 425.854 | 447.4419 | 466.8459 | 478.7587 | 491.2063 | 497.8738 | 503.3661 | 502.8903 | 501.5092 | 497.9031 | 489.7152 | 484.9591 | 483.2141 | 482.3267 | 484.4846 | 484.2941 | 483.6795 | 482.5205 | 485.422 | 488.1745 | 488.7425 | 493.1975 | 494.6638 | 492.8398 | 497.2296 | 502.3677 | 505.1929 | 510.4928 | 514.6584 | 520.644 | 524.708 | 525.779 | 532.2745 | 527.6147 | 528.5498 | 537.7548
Non-OECD Europe and Eurasia | 1260.7296 | 1332.1414 | 1306.2495 | 1271.1372 | 1256.5799 | 1213.2462 | 1197.54 | 1191.5167 | 1188.7811 | 1178.2365 | 1165.5919 | 1162.7138 | 1153.5195 | 1148.5272 | 1141.2218 | 1138.6244 | 1156.0621 | 1164.7022 | 1170.8618 | 1182.4349 | 1191.4363 | 1206.4941 | 1210.0857 | 1221.9975 | 1229.5731 | 1248.0858 | 1246.8745 | 1260.4762 | 1271.0625 | 1277.9389 | 1278.7085 | 1296.1668 | 1302.625 | 1311.4597 | 1322.3351 | 1333.717 | 1335.7511 | 1329.009 | 1343.3455 | 1340.7889 | 1348.3124
China | 208.9395 | 256.3489 | 281.3194 | 319.3655 | 354.6901 | 373.5916 | 405.4807 | 403.3199 | 420.8404 | 435.909 | 452.368 | 470.4106 | 483.9286 | 498.3562 | 514.76 | 528.6712 | 558.4256 | 585.6425 | 616.2356 | 644.0138 | 675.1064 | 704.7711 | 735.5643 | 763.9477 | 796.2072 | 825.9256 | 857.6438 | 879.9593 | 910.797 | 933.7637 | 963.4697 | 985.5403 | 1009.4993 | 1038.6145 | 1064.3856 | 1086.2451 | 1111.1589 | 1137.1476 | 1160.6986 | 1183.8078 | 1206.2193
India | 128.8098 | 127.851 | 119.0826 | 104.8614 | 102.5485 | 99.1549 | 108.0291 | 108.8442 | 110.9223 | 111.713 | 114.7094 | 120.5932 | 126.2769 | 131.9916 | 137.9661 | 144.3044 | 148.7633 | 153.8128 | 159.027 | 164.419 | 170.0037 | 178.1121 | 186.5532 | 195.5052 | 204.57 | 214.1308 | 224.4982 | 235.0595 | 246.32 | 257.6329 | 269.4513 | 280.3085 | 291.8955 | 303.8123 | 315.9454 | 328.1276 | 340.9649 | 353.5629 | 366.6334 | 379.6897 | 394.497
Natural gas-related carbon dioxide emissions for selected countries/regions
billion metric tons
history projections

## Slide 158: —with the greatest increases in China, the United States, and India
CO2 emissions from natural gas, a relatively lower-emitting fossil fuel used in many applications, grow across all regions as natural gas consumption increases throughout the projection period.
China has the largest increase in absolute natural gas-related CO2 emission levels because natural gas is increasingly used for power generation and in transportation.
On a percentage basis, the largest growth in natural gas-related CO2 emissions from 2018 to 2050 is in India, although it starts from a low level. As India’s economy grows, natural gas use increases along with other fuels, and maintains its share at 6% of total energy consumed.
In OECD Europe, natural gas-related CO2 emissions begin moderately increasing after 2030 as natural gas-fired capacity begins to replace retiring nuclear generation, putting upward pressure on overall emission levels and increasing the carbon intensity of their fuel mixes.

## Slide 159: World coal-related carbon dioxide emissions continue to grow through 2050 in the Reference case—
Chart: 
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049 | 2050
United States | 1986.1601 | 1875.78 | 1657.2677 | 1717.829 | 1713.5423 | 1480.3231 | 1354.1609 | 1318.3062 | 1257.8482 | 1202.8838 | 1138.1357 | 1098.6154 | 1087.3527 | 1086.6026 | 1096.2845 | 1091.7159 | 1079.2421 | 1068.2135 | 1062.9803 | 1080.4622 | 1083.8193 | 1067.9224 | 1037.7627 | 1037.7442 | 1025.3742 | 1023.0267 | 1022.6916 | 1015.6162 | 1014.0103 | 1012.3588 | 1012.77 | 1006.8385 | 1004.2178 | 1000.3157 | 1001.3785 | 1004.7867 | 1002.4739 | 1003.2451 | 1005.1475 | 1005.5417 | 1006.4355
OECD Europe | 1166.5037 | 1201.8525 | 1252.8098 | 1198.0587 | 1159.1312 | 1139.7181 | 1060.1904 | 912.116 | 833.3658 | 748.9384 | 672.5502 | 658.7263 | 644.4913 | 629.9382 | 616.4744 | 604.3338 | 596.0443 | 588.7671 | 581.0529 | 573.8336 | 566.415 | 563.6238 | 559.7202 | 556.3425 | 552.7046 | 550.0283 | 548.7257 | 547.5775 | 546.2574 | 544.811 | 543.4077 | 542.2722 | 541.5347 | 540.1411 | 538.8738 | 537.7143 | 537.6162 | 537.4032 | 537.5123 | 537.6354 | 537.5838
Non-OECD Europe and Eurasia | 924.3994 | 991.078 | 1004.2384 | 933.5363 | 880.9474 | 904.9151 | 890.195 | 750.7379 | 735.5374 | 715.8945 | 699.0443 | 694.1779 | 688.4001 | 684.1474 | 678.8264 | 674.239 | 672.4203 | 670.1719 | 666.92 | 665.3522 | 663.9019 | 665.1424 | 664.1751 | 663.7931 | 663.4214 | 663.9855 | 663.8817 | 663.0715 | 661.499 | 660.7832 | 659.3284 | 658.3972 | 657.9349 | 657.8499 | 658.0547 | 658.345 | 658.9222 | 659.2076 | 659.0935 | 659.4707 | 657.7949
China | 7409.4404 | 8258.9482 | 8749.7246 | 9008.4473 | 8846.8057 | 8591.7393 | 8211.624 | 8139.2379 | 8157.8995 | 8152.0876 | 8169.7056 | 8078.4175 | 8000.7155 | 7936.372 | 7876.8363 | 7816.3179 | 7702.2186 | 7596.9571 | 7492.9447 | 7393.7102 | 7297.9984 | 7229.0974 | 7159.4268 | 7096.5855 | 7033.2594 | 6977.6206 | 6956.3072 | 6936.5036 | 6916.7478 | 6905.2156 | 6887.7266 | 6886.7788 | 6884.0439 | 6888.6099 | 6894.2962 | 6902.5146 | 6904.8858 | 6903.9326 | 6905.7412 | 6901.7732 | 6899.8144
India | 1071.6492 | 1136.3032 | 1344.818 | 1381.1757 | 1511.0194 | 1531.9761 | 1502.5046 | 1698.4033 | 1735.2818 | 1760.7906 | 1796.0016 | 1852.7082 | 1908.767 | 1966.9354 | 2028.3157 | 2093.3279 | 2175.6862 | 2263.2975 | 2352.7357 | 2444.0163 | 2535.942 | 2630.9466 | 2726.4353 | 2824.1151 | 2921.4033 | 3020.5314 | 3077.1225 | 3132.9418 | 3192.0191 | 3250.0557 | 3312.9807 | 3414.0436 | 3518.0418 | 3620.2746 | 3724.8665 | 3828.2276 | 3975.165 | 4117.9843 | 4265.3552 | 4413.871 | 4559.9634
Coal-related carbon dioxide emissions for selected countries/regions
billion metric tons
history projections

## Slide 160: —and increases from India more than offset decreases from most other regions
World coal-related CO2 emissions grow 0.4% per year annually from 2018 to 2050, compared with their historical growth rate of 2.1% per year from 1990 to 2018.
China shifts from coal to natural gas, nuclear power, and renewable energy during the projection period. This shift is a departure from historical trends and has a major effect on global energy-related CO2 emissions because of the size of China’s economy.
The decline in China’s coal-related CO2 emissions is more than offset by growth in India’s coal-related emissions. India has significant coal resources, which it uses to meet its rapidly expanding electricity and industrial demand. Coal-related emissions in India remain much lower than in China through 2050.

## Slide 161: References

## Slide 163: Acronyms and abbreviations used in this report
AEO = Annual Energy Outlook
b/d = barrels per day
BkW = billion kilowatts
Btu = British thermal unit(s)
CHP = combined heat and power
CO2 = carbon dioxide
EIA = U.S. Energy Information Administration
GDP = gross domestic product
GTL = gas-to-liquids
GW = gigawatts
IEO = International Energy Outlook
LNG = liquefied natural gas
LPG = liquefied petroleum gas
MARPOL = “marine pollution,” the International Convention for the Prevention of Pollution from Ships

## Slide 164: Acronyms and abbreviations used in this report
OECD = Organization for Economic Cooperation and Development
OPEC = Organization of the Petroleum Exporting Countries = Algeria, Angola, Ecuador, Equatorial Guinea, Gabon, Iran, Iraq, Kuwait, Libya, Nigeria, Qatar, Saudi Arabia, United Arab Emirates, and Venezuela. Qatar exited OPEC in December 2018, but is included in this analysis. Congo joined OPEC in June 2018, but is excluded in this analysis.
Petroleum and other liquids = crude oil and lease condensate (including tight oil, shale oil, extra-heavy oil, field condensate, and bitumen) and other liquid fuels (natural gas plant liquids; liquids from renewable sources—biofuels, including ethanol, biodiesel, and biomass-to-liquids [BTL]; liquids from natural gas—gas-to-liquids [GTL], liquids from coal—coal to liquids [CTL]; and liquids from kerogen—oil shale).
Tcf = trillion cubic feet
WEPS+ = World Energy Projection System Plus

## Slide 165: IEO regional definitions – OECD Regions
OECD Americas = United States, Canada, Chile, and Mexico.
OECD Europe = Austria, Belgium, Czech Republic, Denmark, Estonia, Finland, France, Germany, Greece, Hungary, Iceland, Ireland, Italy, Latvia, Luxembourg, Netherlands, Norway, Poland, Portugal, Slovakia, Slovenia, Spain, Sweden, Switzerland, Turkey, and United Kingdom. Note: Israel is included in OECD Europe for statistical reporting purposes.
OECD Asia = Australia, Japan, New Zealand, and South Korea.

## Slide 166: IEO regional definitions – non-OECD Regions
Non-OECD Europe and Eurasia = Albania, Armenia, Azerbaijan, Belarus, Bosnia and Herzegovina, Bulgaria, Croatia, Cyprus, Faroe Islands, Georgia, Gibraltar, Kazakhstan, Kosovo, Macedonia, Malta, Moldova, Montenegro, Romania, Russia, Serbia, Tajikistan, Turkmenistan, Ukraine, and Uzbekistan. Lithuania is included in this grouping, although it joined the OECD in 2018.
Non-OECD Asia = Afghanistan, American Samoa, Bangladesh, Bhutan, Brunei, Burma (Myanmar), Cambodia (Kampuchea), China, Cook Islands, Fiji, French Polynesia, Guam, Hawaiian Trade Zone, Hong Kong, India, Indonesia, Kiribati, Laos, Macau, Malaysia, Maldives, Mongolia, Nauru, Nepal, New Caledonia, Niue, North Korea, Pakistan, Papua New Guinea, Philippines, Samoa, Singapore, Solomon Islands, Sri Lanka, Taiwan, Thailand, Timor-Leste (East Timor), Tonga, U.S. Pacific Islands, Vanuatu, Vietnam, and Wake Islands.
Middle East = Bahrain, Iran, Iraq, Jordan, Kuwait, Lebanon, Oman, Palestinian Territories, Qatar, Saudi Arabia, Syria, United Arab Emirates, and Yemen.

## Slide 167: IEO regional definitions – non-OECD Regions
Africa = Algeria, Angola, Benin, Botswana, Burkina Faso, Burundi, Cameroon, Cape Verde, Central African Republic, Chad, Comoros, Congo (Brazzaville), Congo (Kinshasa), Côte d’Ivoire, Djibouti, Egypt, Equatorial Guinea, Eritrea, Ethiopia, Gabon, The Gambia, Ghana, Guinea, Guinea-Bissau, Kenya, Lesotho, Liberia, Libya, Madagascar, Malawi, Mali, Mauritania, Mauritius, Morocco, Mozambique, Namibia, Niger, Nigeria, Reunion, Rwanda, Sao Tome and Principe, Senegal, Seychelles, Sierra Leone, Somalia, South Africa, South Sudan, St. Helena, Sudan, Swaziland, Tanzania, Togo, Tunisia, Uganda, Western Sahara, Zambia, and Zimbabwe
Non-OECD Americas = Antarctica, Antigua and Barbuda, Argentina, Aruba, The Bahamas, Barbados, Belize, Bermuda, Bolivia, Brazil, British Virgin Islands, Cayman Islands, Colombia, Costa Rica, Cuba, Dominica, Dominican Republic, Ecuador, El Salvador, Falkland Islands, French Guiana, Greenland, Grenada, Guadeloupe, Guatemala, Guyana, Haiti, Honduras, Jamaica, Martinique, Montserrat, Netherlands Antilles, Nicaragua, Panama, Paraguay, Peru, Puerto Rico, St. Kitts and Nevis, St. Lucia, St. Pierre and Miquelon, St. Vincent/Grenadines, Suriname, Trinidad and Tobago, Turks and Caicos Islands, Uruguay, U.S. Virgin Islands, and Venezuela.

## Slide 168: Map of IEO regions

## Slide 169: Contacts
Refer questions about the IEO2019 to the following analysts:
Topic | Subject matter expert contact information |  | 
General questions |  | InternationalEnergyOutlook@eia.gov | 
Economic activity | Elizabeth Sendich | elizabeth.sendich@eia.gov | 202-586-7145
Petroleum and other liquid fuels | Troy Cook | troy.cook@eia.gov | 202-586-4493
Natural gas | David Manowitz | david.manowitz@eia.gov | 202-586-2815
Coal | Bonnie West | bonnie.west@eia.gov | 202-586-2415
Electricity | Kenneth Dubin | kenneth.dubin@eia.gov | 202-586-0477
Renewable energy | Michelle Bowman | michelle.bowman@eia.gov | 202-586-0526
Nuclear power | Slade Johnson | slade.johnson@eia.gov | 202-586-3945
Buildings sector | Behjat Hojjati | behjat.hojjati@eia.gov | 202-586-1068
District heat | Meera Fickling | meera.fickling@eia.gov | 
Industrial sector | Peter Gross | peter.gross@eia.gov | 202-586-8822
Transportation sector | John Maples | john.maples@eia.gov | 202-586-1757
Energy-related CO2 emissions | Perry Lindstrom | perry.lindstrom@eia.gov | 202-586-0934

## Slide 170: For more information
U.S. Energy Information Administration home page | www.eia.gov
Short-Term Energy Outlook | www.eia.gov/steo
Annual Energy Outlook | www.eia.gov/aeo
International Energy Outlook | www.eia.gov/ieo
Monthly Energy Review | www.eia.gov/mer
Today in Energy | www.eia.gov/todayinenergy
September 24, 2019
www.eia.gov/outlooks/ieo
#IEO2019